## Slide 1: Frequency of Association Request in KDDI data
Date: 2013-07-17
Authors:

## Slide 2: Abstract
The presentation analysis data captured by KDDI in Tokyo railway station and investigates frequency of Association Request observed in the sniffer trace

## Slide 3: Histogram indicating the rate of Association Request
Consider the time difference between consecutive Association Request
  Say it is called delta_T_AscReq
Most of the Association Request are within 5 secs of each other (i.e. delta_T_AscReq < 5 secs)
There are 79 Association Request and hence 78 time intervals

## Slide 4: Histogram indicating the rate of Association Request
The following histogram considers only data with delta_T_AscReq < 1 sec
This may be considered as a zoomed in part of the previous histogram
As seen that there are only 7 Association Request within 100 millisec

## Slide 5: Overall Statistics
Statistics:
  Mean: 3.9021 sec
  Median: 1.6644 sec
  Min: 0.0012 sec
  Max: 43.6548 sec
Total number of Association Request considered: 79
  There are 79 Association Request and hence 78 time intervals
Time interval of the sniffer trace 303.809803 sec on a single

## Slide 6: Conclusion
Assuming the standard Beacon interval of 100msec.
From the 79 observed Association Request only 7 Association Requests coming within a Beacon Interval
This is very easily handled by existing CSMA and no peak of Association Request was observed