## Slide 1: Stacking Tags In LLC Media
Date: 2013-11-14
Authors:

## Slide 2: Abstract
Work now in progress on P802.1Qbz and P802.11ak has shown that the method currently defined in IEEE 802.1Q for adding and removing tags (e.g., the VLAN tag) to frames on LLC media (e.g., 802.11) is untenable. A new scheme is proposed in P802.1Qbz Draft 1.3 for use by P802.11ak. In the worst case, this change could invalidate a currently-compliant implementation of 802.11. This presentation solicits comments from any organization or individual that might be affected by this change.

## Slide 3: Current tagging situation

## Slide 4: Back to basics: The 802.11 Data Frame
IEEE Std 802.11-2012
802.1AC mac_service_data_unit (MSDU)

## Slide 5: Back to basics: The 802.3 Data Frame
IEEE Std 802.3-2008
PREAMBLE
SFD
DA
LENGTH
/ TYPE
FCS
EXTENSION
SA
MAC CLIENT DATA
Octets
7 1 6 6 2 46-1982 4 var.
802.1AC mac_service_data_unit (MSDU)

## Slide 6: Back to basics: 802.3 Length/Type MSDU
EtherType data (e.g. IP packet):
LLC data (e.g. Bridge Protocol Data Unit [BPDU]):
SNAP:
LENGTH / TYPE
MAC CLIENT DATA
. 2 3 M
M+3
42-42-03
BPDU
LENGTH < 05-DD
LLC, LL ≠ AA-AA
data
LENGTH / TYPE
MAC CLIENT DATA
. 2 3 3 2 M
M+8
AA-AA-03
00-00-00
LENGTH < 05-DD
LLC, LL = AA-AA
OUI or 0
08-00
EtherType or subtype
IP header
data
IP data
TYPE > 05-FF
MAC CLIENT DATA
08-00
IP header
IP data
LENGTH / TYPE
MAC CLIENT DATA
. 2 M

## Slide 7: Back to basics: 802.2/802.11 LLC MSDU
LLC data (e.g. Bridge Protocol Data Unit [BPDU]):
SNAP:
MSDU
3 M
42-42-03
BPDU
LLC, LL ≠ AA-AA
data
MSDU
3 3 2 M
AA-AA-03
00-00-00
LLC, LL = AA-AA
OUI or 0
08-00
EtherType or subtype
data
IP header
IP data

## Slide 8: Old tagging process: IEEE Std 802.1Q-2011 and IEEE Std 802.11-2012 Annex P
Length/Type no tag:
Length/Type tagged:
LLC no tag:
LLC tagged:
MAC CLIENT DATA
MSDU
. 2 M
LENGTH / TYPE
MSDU
3 M
LLC
data
EtherType
MAC CLIENT DATA
81-00
MSDU
. 2 L 2 M
LENGTH / TYPE
Tag value
02-44
MSDU
. 6 2 L 3 M
LLC
data
EtherType
81-00
Tag value
02-44
SNAP
AA-AA-03-00-00-00
Simply add or remove tag; MSDU is unchanged.
Simply add or remove tag; MSDU is unchanged.

## Slide 9: Old tagging process: IEEE Std 802.1Q-2011 and IEEE Std 802.11-2012 Annex P
On LLC media, the first 3 bytes following every tag are LLC.
On Length/Type media, the first 2 bytes following every tag are a Length/Type.
You know how to decode the whole frame, because you know whether the medium is LLC or Length/Type.
You cannot tell from the data, itself, whether the bytes following a tag are LLC or Length/Type, because there are many two-bytes values that are valid in both formats. Knowledge of the media type is essential.

## Slide 10: Why that is a problem

## Slide 11: The end-to-end tag stacking problem today All tags must be translated at once by B3
802.1Q decoder ring: BA = Backbone Addresses, I = I-tag, CA = Customer Addresses, S = Service VLAN tags, Q = Customer VLAN tags.
B4
B3
B1
E1
data
Q
CA
data
Q
S
CA
B2
data
Q
S
CA
BA
I
data
Q
S
CA
BA
I
data
Q
S
CA
data
CA
LLC encoding on LLC media
Length/Type encoding on L/T media
L/T
L/T
LLC
LLC
LLC
L/T
L/T
L/T
L/T
L/T
data
CA
LLC
B5
B6
E2
LLC
LLC
LLC
LLC
LLC
L/T
LLC
Q
L/T

## Slide 12: The end-to-end tag solution today
Tagging near the edges of the network must be in the format expected by the medium in that area.
  Otherwise, they cannot decode the tag stack.
  We cannot, ex post facto, require every bridge and tag-aware end station to start translating between encapsulations.
  Heuristics to do the translation are possible, but not reliable.
We could ask the bridge (B3) that connects to two media types to convert all tags and the original MSDU.
  That is difficult to do in high speed in ASICs.
  It makes it impossible to deploy new tags at the edge, because the core devices will not know how long those tags are.
  That’s how you know it is a violation of the principles of layering.

## Slide 13: proposal for tagging in P802.1Qbz D1.3

## Slide 14: Tagging process in P802.1Qbz Draft 1.3
Length/Type no tag:
Length/Type tagged:
LLC no tag:
LLC tagged:
MAC CLIENT DATA
MSDU
. 2 M
LENGTH / TYPE
MSDU
3 M
LLC
data
EtherType
MAC CLIENT DATA
81-00
MSDU
. 2 L 2 M
LENGTH / TYPE
Tag value
02-44
MSDU
. 6 2 L 2 M
EtherType
81-00
Tag value
02-44
SNAP
AA-AA-03-00-00-00
Simply add or remove tag; MSDU is unchanged.
Change MSDU when adding or removing a tag.
MAC CLIENT DATA
LENGTH / TYPE

## Slide 15: LLC tagging process P802.1Qbz Draft 1.3 We want this in 802.11ak, also
Add/remove tag on SNAP frame
Add: Convert old outer item LLC  L/T, add LLC tag.
Remove: Delete LLC tag, convert new outer item L/TLLC.
OR: Add/remove tag between LLC-SNAP and MSDU.
Untagged MSDU
3 3 2 M
AA-AA-03
00-00-00
LLC, LL = AA-AA
0
08-00
EtherType
IP header
data
IP data
Untagged MSDU
3 3 2 L 2 M
AA-AA-03
00-00-00
LLC, LL = AA-AA
0
08-00
EtherType
IP header
data
IP data
EtherType
81-00
Tag value
02-44
TAG
Tagged MSDU

## Slide 16: LLC tagging process P802.1Qbz Draft 1.3 We want this in 802.11ak, also
Add/remove tag on LLC frame
Add or remove both the LLC tag and the Length field.
3 3 2 2 2 3 M
AA-AA-03
00-00-00
LLC, LL = AA-AA
0
EtherType
88-A8
Tag value
02-44
TAG
Tagged MSGU
Untagged MSDU
3 M
42-42-03
BPDU
LLC, LL ≠ AA-AA
data
Untagged MSDU
42-42-03
BPDU
LLC, LL ≠ AA-AA
data
Length
M+3

## Slide 17: The new end-to-end tag stacking solution One translation per tag or media change
B4
B3
B1
E1
data
Q
CA
data
Q
S
CA
B2
data
Q
S
CA
BA
I
data
Q
S
CA
BA
I
data
Q
S
CA
LLC encoding on LLC media
Length/Type encoding on L/T media
L/T
L/T
L/T
L/T
L/T
L/T
L/T
LLC
L/T
LLC
LLC
L/T
L/T
L/T
L/T
L/T
802.1Q decoder ring: BA = Backbone Addresses, I = I-tag, CA = Customer Addresses, S = Service VLAN tags, Q = Customer VLAN tags.
data
CA
LLC
B5
B6
E2
data
CA
L/T
Q
L/T

## Slide 18: The end result desired
Multiple tags on Length/Type (802.3) frame:
Multiple tags on LLC (802.11) frame:
Only the first item is LLC-encoded on an LLC medium; all other items are Length/Type-encoded.
(An untagged MSDU is LLC or Length/Type, by medium.)
Length/Type MSDU
Length/Type Tag 3
Length/Type Tag 2
Length/Type Tag 1
Length/Type MSDU
Length/Type Tag 3
Length/Type Tag 2
LLC SNAP Tag 1

## Slide 19: The new end-to-end tag solution
We keep the whole stack, except for the outermost item, in Length/Type format.
Every device knows how to encode/decode frames.
Only one item is converted per tag added or removed, or when changing between 802.3 and 802.11.
New end-to-end tags can be invented without altering B3.
The outermost item still follows the rules for the medium in question.
We could equally well have used the LLC format in all except the outermost item, except that 802.3 devices already use multiple tags and (as far as this author knows) 802.11 devices do not yet use tags.
(There is also a new EtherType defined in P802.1Qbz D1.2 to encode an LLC MSDU longer than 1500 bytes.)

## Slide 20: A plea
This example is from 802.11-2012 Table P-3. If you use this format, please tell 802.1 Interworking and/or 802.11 TGak, because we propose to remove this format from the standards; it stacks SNAP encodings:
(This frame would be encoded, in the new scheme as:)
If there is such a use, then we will have to re-examine our options.
Slide 20
Norman Finn, Cisco Systems
. 6 2 L 6 2 M
EtherType
81-00
Tag value
87-65
SNAP
AA-AA-03-00-00-00
08-06
EtherType
IP ARP packet
data
SNAP
AA-AA-03-00-00-00
. 6 2 L 2 M
EtherType
81-00
Tag value
87-65
SNAP
AA-AA-03-00-00-00
08-06
EtherType
IP ARP packet
data