## Slide 1: Legacy Support on HEW frame structure
Date: 2013-09-16
Authors:

## Slide 2: Introduction
This contribution provides requirement for legacy support on HEW frame structure

## Slide 3: History of legacy support
In 11n [1],
  “Some of the modes of operation defined in the proposal shall be backwards compatible with 802.11a/g.”
  “11n AP can be configured to reject or accept associations from legacy STA because they are legacy STA.”
In 11ac [2],
  “The TGac amendment shall be backwards compatible with 802.11a/n which operates at 5GHz.”
  “The TGac amendment shall provide mechanisms that ensure coexistence between TGac and legacy IEEE802.11a/n devices.”

## Slide 4: Clarification on legacy support
Backward compatibility can be interpreted as follows:
  New devices shall be able to operate with legacy devices (‘2’ in the below figure)
Coexistence can be interpreted as follows:
  Legacy AP/STA shall be able to transmit and receive the frames as the same behavior/procedure regardless of the existence of new AP/STA (‘3’ in the figure)

## Slide 5: Legacy support in 11n and 11ac (example)
Backward compatibility
  New devices shall be able to operate with legacy devices.
    E.g., .11n device can transmit and receive .11a frames
    E.g., .11ac device can transmit and receive .11a/n frames
    Coexistence
  Legacy AP/STA shall be able to transmit and receive the frames as the same behavior/procedure regardless of the existence of new AP/STA
    This is for CCA behavior
    .11n GF format: Energy detection only
    .11n MF format, .11ac format: Energy detection and Preamble detection
 Legacy device can decode new device’s L-STF/L-LTF/L-SIG since it is identical

## Slide 6: Legacy support on HEW frame structure
Strictly required to maintain L-Part
For example, increasing CP length (by increasing FFT size) only in New-Part, does not impact on legacy support.[1],[2]

## Slide 7: Conclusion
In this contribution, we provided considerations on legacy support in view of frame structure
If we keep the L-Part (i.e. L-STF, L-LTF, and L-SIG) in HEW frame, we can design New-Part freely such as increasing CP length with no harm of legacy support.

## Slide 8: Reference
[1] IEEE 802.11-02/813r11, “802.11 TGn Functional Requirements”
[2] IEEE 802.11-09/00451r16, “TGac Functional Requirements and Evaluation Methodology”
[3] IEEE 802.11-13-0843, “Further evaluation on outdoor Wi-Fi”
[4] IEEE 802.11-13-0536, “HEW SG PHY Considerations For Outdoor Environment”