## Slide 1: Summary On HEW Channel Models
Date: 2013-09-12
Authors:

## Slide 2: Introduction to Channel Model Documents
HEW usage models include both indoor and outdoor usage models [1]
  High density of STAs – Indoor
  High density of APs (low/medium density of STAs per AP) – Indoor
  High density of APs and high density of STAs per AP – Outdoor
Both indoor and outdoor channel model need to be considered
  Indoor channel models
    TGn (IEEE 802.11-03/940r4) and TGac (IEEE 802.11-09/0308r12) channel model documents provided SISO, MIMO and MU-MIMO channels models.
    Principle: take advantage of well-established TGn and TGac channel models
  Outdoor channel model
    Three outdoor channel model proposals have been proposed in HEW (summary in following slides)
    Current principle: adopt outdoor channel model from other organizations instead of developing outdoor channel model based on measurements from IEEE 802.11 working group.

## Slide 3: Proposed outdoor channel models
Continue..
Document | Channel Model | Rational | Discussions
802.11-13/0756 Ron Porat, etc. [4] | The ITU Urban Micro (UMi) [2] shall be used to test outdoor Microcell /Picocell deployments. For deployments that co-locate WLAN in Macro cellular cells the Urban Macro (UMa) channel may be considered. | ITU models are applicable for up to 100MHz signal BW, 2-6GHz center frequency and outdoor and indoor environments. All models are defined for NLOS and LOS channels with a distance dependent LOS probability | 160MHz bandwidth can be directly derived from ITU models.
802.11-13/0536 Wookbong Lee, etc. [5] | Proposed to adopt ITU Urban Macro (UMa) channel | Same rational as document #0756 | UMa models have large delay spread, which is more than the CP length of current 11n/ac. Channel variations need to be handled.
802.11-13/0858 Shahrnaz Azizi, etc. [6] | WINNER II channel models described in [3] | Applicable for 2 – 6 GHz frequency range with up to 100 MHz RF bandwidth. Covered multiple propagation scenarios, such as indoor-to-outdoor, urban micro-cell, outdoor-to-indoor, etc. Supports multi-antenna technologies, polarization, multi-user, multi-cell, and multi-hop networks | WINNER II channel models are pre-cursor of ITU channel models; WINNER II channel models reflects more scenarios.

## Slide 4: Comparison of Outdoor Channel Models
In [7], Kaushik (Samsung) provided a detailed comparison between ITU channel models and WINNER II channel models
  The modeling methodology and channel construction between WINNER II and ITU are the same
    ITU channel models are a sub-set of WINNER II channel models
  The values for the parameters are slightly different
    Path loss models for both IITU and WINNER II are similar
    Quantitative difference (outage capacity) for Urban NLOS case is small
    Two models are different only in urban LOS case
  Conclusion: Not much difference between ITU UMi channel models and WINNER II channel models.
Given the fact that ITU channel models are developed based on WINNER II, let us choose ITU channel models as HEW outdoor channel models.

## Slide 5: UMi or UMa (Environments)
Definitions of UMi environment and UMa environment
  Urban Micro cell environment:
    In urban micro-cell scenario the height of both the antenna at the BS and that at the UT is assumed to be well below the tops of surrounding buildings. The channel model for urban micro-cell scenario is called urban micro (UMi).
  Urban Macro cell environment:
    In typical urban macro-cell scenario, the mobile station is located outdoors at street level and the fixed base station clearly above the surrounding building heights. The channel model for urban macro-cell scenario is called urban macro (UMa).
Difference:
  The main difference is the height of the BS antenna. Higher elevation antennas increases the channel delay spread - about 2x factor between UMi and UMa.

## Slide 6: UMi and UMa (Deployments)
Wi-Fi is increasingly being added to small cell (Pico and Femto) deployments of cellular carriers, cable providers and in certain hotspots e.g. stadiums.
Wi-Fi may also be added to carriers’ Macro cells in some cases:
  In lieu of Pico cells (where Pico locations are not available or costly to acquire)
  Providing broadband wireless access in emerging markets
  Simple add-on to existing cellular infrastructure.
Note however that even when co-located in a Macro cell, the Wi-Fi coverage is quite smaller than cellular, typically due to regulatory limits (sometimes as low as 20dBm). Hence the intent here is not ubiquitous coverage as achieved by cellular but rather a hotspot coverage leveraging existing Macro cells.

## Slide 7: Proposal on outdoor channel model and requirements
Selection Rationale
  It will be unfortunate if future outdoor deployments of HEW devices are strictly limited to certain antenna heights – in practice no one will check that aspect accurately.
  On the other hand side, re-designing Wi-Fi to optimally support Macro deployments may be a stretch considering the majority of deployment scenarios described in [1]
    We have already designed 11ah to support Macro deployments by smart grid companies (albeit for very low traffic requirements).
Basic Design Criteria
  HEW design shall ensure that Wi-Fi works well under UMi
  HEW design should ensure that Wi-Fi still works under UMa (connection is supported but reduced performance is possible)

## Slide 8: Straw Poll 1
Do you agree to adopt ITU channel models as the base line of HEW outdoor channel models?

## Slide 9: Straw Poll 2
Do you agree the basic design criteria for different outdoor channel models shown in slide 7?

## Slide 10: References
“Usage models for IEEE 802.11 High Efficiency WLAN study group (HEW SG) – Liaison with WFA”, IEEE 802.11-13/0657r6, Orange, Laurent Cariou .
Report ITU-R M.2135-1, (12/2009), Guidelines for evaluation of radio interface technologies for IMT-Advanced
IST-4-027756 WINNER II, D1.1.2 V1.1, WINNER II Channel Models
“HEW Channel Model “, IEEE 802.11-13/0756r, Broadcom, Ron Porat, etc.
“HEW SG PHY Considerations For Outdoor Environment”, IEEE 802.11-13/0536, LGE, Wookbong Lee, etc.
“Enhanced Channel Model for HEW”, IEEE 802.11-13/0858, Intel, Shahrnaz Azizi, etc.
“Outdoor Channel Model Candidates for HEW”, IEEE 802. 11-13/0996r1, Samsung, Kaushik Josiam, etc.