## Slide 1: Discussion of the comments related to FILS Request Parameter
Date: 2013-09-16
Authors:

## Slide 2: Abstract
The presentation contains a set of clarification questions for FILS Request Parameters. FILS Request Parameters is transmitted in Probe Request frame and it sets criteria to Probe Response transmission.
The discussion is related to definitions and the formats of the fields.

## Slide 3: 8.4.2.177 FILS Request Parameters element
  CIDs 2763, 3129, 3130, 3312, 3313, 3350, 3351, 3372 and 3373.
Define (transmission) resource requirement instead of PHY layer type.
Discussion:
  The HT and VHT capabilities are simple criteria for responder. Tesource requirement is hard to estimate.
 | B0 | B1 – B3 | B4 | B5 | B6 – B7
 | Reduced Neighbor Report Request | BSS Delay Criteria | HT Support Criteria | VHT Support Criteria | Reserved
Bits: | 1 | 3 | 1 | 1 | 2
Figure 8-401cu—Parameter Control Bitmap field

## Slide 4: HT and VHT support FILS Criteria
  If a STA wants to receive a Probe Response frame from only a HT capable STA, the STA can transmit a Probe Request frame in HT PPDU format. Similarly VHT PPDU may be used for VHT AP responses
Discussion:
  If the HT or VHT PPDU is transmitted, the transmission time of Probe Request will be longer:
    PLCP header of the HT PPDU adds at minimum 8 microseconds
    PLCP header of the VHT frame adds at minimum 12 microseconds

## Slide 5: Strawpoll
Are you in favour of having of option 1 or option2?
Option 1: use 2 bits to specify that the responder shall be HT or VHT capable as in 802.11ai draft 1.0.
Option 2: use HT PPDU or VHT PPDU to identify the capabilities of the responding AP as proposed by comments.
Results:
Option 1: 6
Option 2: 1

## Slide 6: Reduced Neighbor Report Request
Reduced Neighbor Report Request: CIDs 3349, 3371
  Request element (sub-clause 8.4.2.10) can be placed in a Probe Request frame to request that the responding STA include the requested information in the Probe Response frame. What is the difference with the Request element?
Discussion:
  The proposed mode is default operation to request all other elements
 | B0 | B1 – B3 | B4 | B5 | B6 – B7
 | Reduced Neighbor Report Request | BSS Delay Criteria | HT Support Criteria | VHT Support Criteria | Reserved
Bits: | 1 | 3 | 1 | 1 | 2

## Slide 7: Delay Criteria
CIDs 3293
The maximum value (of access delay) is therefore 200us x 255 = 51ms. Is this a concern?
Discussion:
The delay increases exponentially as a function of traffic load and congestion. In small delays the preciseness of the delay value is more important than in large delays.
Recovering from the delay requires transmission resources and time to transmit the buffered frames.
The APs with large delay values are not good candidates.

## Slide 8: Example resolutions:
What the group feels on the correct granularity of the access delay criteria?
Keep the value as it is: 200us x 255 = 51ms
Increase the value to 400us: 400us x 255 = 102ms
Use value 200us to 0-127 values and 400 us to 128-255, 200us x 127 + 400us x 128 = 77ms
Some other value / formula?

## Slide 9: Minimum Data Rate
CIDs 3352, 3374
Comment: "The Minimum Data Rate field is 3 octets long and contains an unsigned integer in units of kilobits per second that specifies the lowest total data rate specified at the MAC_SAP for transport of MSDUs or AMSDUs that the STA is going to transmit. The minimum MAC_SAP data rate does not include the MAC and PHY overheads incurred in transferring the MSDUs or A-MSDUs."
What is the definition of the lowest total data rate? Is it a long-term throughput? Is it a singly linked throughput?
Discussion:
- The lowest total data rate is an estimation of the data amount that will be transmitted in future. Is it better to say that it is average or peak value of throughput in future?

## Slide 10: Strawpoll
Is the current definition as specified below acceptable for you?
"The Minimum Data Rate field is 3 octets long and contains an unsigned integer in units of kilobits per second that specifies the lowest total data rate specified at the MAC_SAP for transport of MSDUs or AMSDUs that the STA is going to transmit. The minimum MAC_SAP data rate does not include the MAC and PHY overheads incurred in transferring the MSDUs or A-MSDUs."
Yes: 3
No: 2
Don’t care: 5