## Slide 1: 45 GHz Spectrum Allocation in China
Authors/contributors:
Date: 2013-11-14
Presenter: Haiming WANG
Name | Company | Address | Phone | Email
Haiming WANG | SEU/CWPAN | 2 Sipailou, Nanjing 210096, China | +86-25-5209 1653-301(ext.) | hmwang@seu.edu.cn
Wei HONG |  |  | +86-25-5209 1650 | weihong@seu.edu.cn
Jixin CHEN |  |  | +86-25-5209 1653-403(ext.) | jxchen@seu.edu.cn
Bo SUN | ZTE/CWPAN |  |  | sun.bo1@zte.com.cn
Pei LIU | Hisilicon/CWPAN |  |  | 
Lan ZHUO | CESI/CWPAN |  |  | 

## Slide 2: Abstract
This presentation gives the information of 45 GHz frequency spectrum allocation in China.

## Slide 3: Background
In 2010, SG5 whose main objective is to research the possibilities of 45 GHz band for WLAN application was setup in CWPAN.
In 2011, a serial of application documents of the 45 GHz frequency band were submitted to the Radio Management Bureau of the Ministry of Industry and Information Technology (MIIT) of the People’s Republic of China for the usage of the 45 GHz frequency band.
In September 2013, after multiple rounds of modification, the document “The usage of 40-50 GHz frequency band for mobile services in broadband wireless access systems” was published in the MIIT website, which was intended to ask for suggestions and comments.

## Slide 4: Main parameters in 45GHz frequency band
Frequency band: 42.3~47.0 GHz, 47.2~48.4 GHz
Bandwidth: 1080 MHz, 540 MHz
Frequency tolerance: 100×10-6
Maximum transmit power at antenna port: 20dBm
Maximum EIRP: 36dBm
CH 1
CH 1
B0 = 1080 MHz
42.795GHz
43.065 GHz
B0 = 540 MHz
CH 2
CH 3
CH 4
CH 5
CH 6
CH 7
CH 8
CH 9
CH 10
46.575 GHz
47.53GHz
48.07 GHz
42.3 GHz
47.0 GHz
47.2 GHz
48.4 GHz
CH 2
CH 3
CH 4
CH 5
46.305 GHz
47.8 GHz

## Slide 5: Reference
[1] MIIT, The usage of 40-50 GHz frequency band for mobile services in broadband wireless access systems, n15635784, http://www.miit.gov.cn/ n11293472/n11293832/n12845605/n13916913/15636214.html
Notes: 《40—50吉赫兹频段移动业务中宽带无线接入系统频率使用相关事宜》