## Slide 1: Simultaneous Transmission Technologies for HEW
Date: 2013-11-12

## Slide 2: Background
HEW SG is aiming to start up a new Task Group to improve the area throughput / per-user-throughput in high density APs/STAs scenarios.
There are three ways to improve the performance by PHY related technologies.
  Simultaneous transmission: More WLANs, Higher density
  Wider bandwidth: More Spectrum
  Higher spatial streams/MCS: higher spectrum efficiency in each link
Most PHY technologies presented in HEW SG improves the area throughput by simultaneous transmission technologies in the high density APs/STAs scenarios.
This contribution focuses on the technologies for simultaneous transmission for HEW.

## Slide 3: Evolution history of IEEE 802.11 PHY techniques
11n supports space division multiplexing to enhance P2P link throughput.
11ac supports DL MU-MIMO to enhance P2MP system throughput.
HEW shall extend the enhancement to the area throughput.
To achieve the goal, straightforward extensions of transmission topology (extended P2MP/MP2P/MP2MP) will be beneficial.
Year
1G
10G
100M
10M
1M
Aggregate throughput
[bit/s]
2005
2010
2015
2000
1995
.11b
802.11
.11a
.11g
.11n
.11ac
HEW SG
DL MU-MIMO
OFDM
P2MP
P2P
P2P
AP
AP
AP
SU-MIMO
(P2P link extension)
DL MU-MIMO
(P2MP transmission)
SU-MIMO
Simultaneous Transmission
P2MP/MP2P/MP2MP
AP
AP
100G

## Slide 4: Expected effect of simultaneous transmission in HEW
Current 802.11 standard shares wireless medium in the time domain by CSMA/CA protocol.
Spatial and frequency domain technologies may enhance the CSMA/CA enabling simultaneous transmission by managing interference and selecting appropriate MCS.
Simultaneous transmission is the reasonable way to improve the area throughput in the high density scenarios.

## Slide 5: Simultaneous transmission in the frequency domain
Various frequency domain technologies have been presented such as DL OFDMA[1][2] and UL OFDMA[3].
Multi-channel / OFDMA has the capability of utilizing the frequency resource that cannot be used by legacy devices, 11a/g/n/ac, in both uplink and downlink.
It also improves the MAC efficiency for short data packets.
The frequency resource usage becomes flexible with simultaneous transmission with DL/UL OFDMA.
AP coordination obtains further spectrum efficiency improvement.

## Slide 6: Simultaneous transmission in the spatial domain
DL MU-MIMO is specified in 11ac and improves the spectrum efficiency in P2MP scenarios.
UL MU-MIMO improves the spectrum efficiency in MP2P scenarios [4].
Interference management mechanism in the spatial domain / spatial reuse mechanism and appropriate setting for transmission power, CCA level, and MCS have the capability of improving the area throughput in MP2MP scenarios [5]-[8].
Enhancing the spatial domain approach to P2MP and MP2MP scenario is the reasonable way to improve the area throughput in the high density scenario.
UL MU-MIMO
Interference management
Dynamic Sensitivity
Control
P2MP
DL MU-MIMO
MP2P
MP2MP

## Slide 7: Example of the effect of the simultaneous transmission for MP2MP
The performance is improved by solving the exposed terminal problem due to CSMA/CA.
Dynamic sensitivity control (DSC) or transmitting power control (TPC) has been investigated for this purpose [7].
Measured results indicate that the STA with DSC obtains higher throughput than the STA without DSC.
Tx1
Rx1
Tx2
Rx2
1m
1m
Desired
Undesired
Config.1: DSC Enabled
Config.2: DSC Disabled (Conventional CSMA/CA)
Tx2 transmits frames consecutively (WLAN frames are transmitted at SIFS Intervals)

## Slide 8: Summary
Straightforward extensions of transmission topology (extended P2MP/MP2P/MP2MP) are beneficial for HEW.
Simultaneous transmission technologies in the frequency and the spatial domain are the reasonable way to improve the area throughput in the high density scenario.

## Slide 9: Straw Poll
Do you agree that simultaneous transmission in frequency and/or spatial domain are the reasonable approach to improve the area throughput in HEW?
Result:
  Yes: 61
  No: 0
  Abstain: 27

## Slide 10: References
[1] B. Hart (Cisco Systems), “DL-OFDMA for mixed clients,” doc.:IEEE802.11-10/0317r1.
[2] Y. Inoue (NTT), “Improved spectrum efficiency for the next generation WLANs,” doc.:IEEE802.11-12/0820r0.
[3] R. Stacey (Intel), “Technology and use cases for TGac,” doc.:IEEE802.11-09/0789r2.
[4] R. V. Nee (Qualcomm), “UL MU-MIMO for 11ac,” doc.:IEEE802.11-09/0852r0.
[5] Y. Asai (NTT), “Update of interference management using beamforming technique in OBSS environment,” Doc. :IEEE802.11-10/08455r0.
[6] J. Wang (MediaTek), “HEW beamforming enhancements,” doc.:IEEE802.11-13/0877r0.
[7] G. Smith (DSP Group), “Dynamic sensitivity control for HEW,” doc.:IEEE802.11-13/1290r0.
[8] H. Zhang (Marvell), “Beamforming under OBSS interference,” doc.:IEEE802.11-13/1126r0.