## Slide 1: Date: 2013-11-13
Proposal for UNII-4 band coexistence

## Slide 2: Abstract
This proposal aims
  to promote a discussion of a potential compromise sharing solution between the automotive use and Wi-Fi use of the 5850-5925 MHz band (U-NII-4)
  to propose a technical solution that enables sharing in UNII-4 band among different IEEE amendments.
This document is an updated version of 1276r1.

## Slide 3: Summary of the Previous Proposal
Upper 30 MHz (5895-5925MHz) use 10MHz 11p waveforms
  Dedicated to the DSRC applications
Lower 45MHz (5850-5895) use 20MHz 11p(a) waveforms
  Implement a sharing mechanism based on 20MHz preamble detection
  Both unlicensed devices and DSRC devices access this spectrum
Unlicensed devices that use the lower UNII-4 spectrum are required to meet a tighter spectral mask
Refer to 1276/r1 for details

## Slide 4: Modifications
UNII devices can use the upper 30MHz with the following stricter DFS-like requirements
  Detect DSRC signals at [TBD] (e.g. -90dBm)
  Once DSRC signal is detected, vacate the channel for [TBD] seconds, e.g. (10s)
Lower 45MHz of the spectrum can be used by UNII devices given that
  they satisfy the spectral leakage requirements (Spectral mask requirement does not apply to the DSRC devices)
  they implement “listen before talk” rules based on 802.11 20 MHz detection levels and TBD changes to CCA and EDCA parameters

## Slide 5
U-NII 3
Available for WLAN
Spectrum Allocation and OOBE Requirement
161
DSRC Band
U-NII 4
U-NII Worldwide
5725
Frequency [MHz]
24 – 10log10(B) dBm/MHz
30 – 10log10(B) dBm/MHz
5825
5835
5470
-27 - G dBm/MHz
5850
5875
5925
5895
165
169
173
177
184
180
182
-27-GdBm/MHz
-5-GdBm/MHz
-17-GdBm/MHz

## Slide 6: Strawpoll
Do you support the proposal outlined in Slides 3, 4 and 5 of this document as part of the possible solutions that IEEE 802, after discussing it in the DSRC coexistence tiger team, might communicate to FCC for addressing the sharing problem in the UNII-4 band?
  Y 42
  N 1
  A 5

## Slide 7: APPENDIX

## Slide 8: Current Proposed Spectrum Allocation and OOBE Requirements in NPRM
Available for WLAN
161
DSRC Band
U-NII 4
U-NII Worldwide
U-NII 3
5725
Frequency [MHz]
24 – 10log10(B) dBm/MHz
30 – 10log10(B) dBm/MHz
5825
5835
5470
-27 - G dBm/MHz
5850
5875
5925
5895
165
169
173
177
181
-17 - G dBm/MHz

## Slide 9: Proposed Scheme 2: Spectrum Allocation and OOBE Requirement
U-NII 3
Available for WLAN
Keep Ch180, 182 and 184 for DSRC dedicated use
Relax the OOBE requirement for UNII devices in DSRC band
161
DSRC Band
U-NII 4
U-NII Worldwide
5725
Frequency [MHz]
24 – 10log10(B) dBm/MHz
30 – 10log10(B) dBm/MHz
5825
5835
5470
-27 - G dBm/MHz
5850
5875
5925
5895
165
169
173
177
184
180
182
-27-GdBm/MHz
-5-GdBm/MHz
-17-GdBm/MHz
Notes: Questions:
What is the basis of picking OOBE rule? (Mike)
What is band next to DSRC band? (Mike)
What is the current OOBE rule for DSRC channels? (Check with Amir, Roger, John or Sue)

## Slide 10: Technical Issues and Mitigation
Cross-channel interference: does the proposed compromise make the cross channel interference worse?
  Not really. The two 10MHz channels in dedicated DSRC spectrum will see less cross-channel interference as compared to the NRPM proposal or current DSRC channelization
  Cross-channel interference has always been a problem between existing service channel and safety channel; the compromise does not make things worse
High power public safety channel (aka Ch184) and potentially other channels requested by other ITS players:
  Ch184 has not been the focus of existing model deployment
  A good time to revisit the need or spectrum allocation for such channel
    May be combined with the V2x safety channel
    May be assigned to the shared spectrum rather than using the dedicated spectrum
20MHz channelization and performance degradation in shared spectrum: 20MHz channelization does not necessarily lead to performance degradation with the latest receiver technology

## Slide 11: Cross-Channel Interference Comparison (I)
Previous DSRC channel plan
  Ch172 is 5MHz away from the ISM band
  ISM band has OOBE rule of only -20dBr from the PSD limit (33dBm/MHz with 30dBm peak power)
  Ch172 can potentially see maximum 13dBm/MHz interference leakage from ISM band
Available for WLAN
DSRC Band
Frequency [GHz]
5.85
5.725
0 dBr
-20 dBr
FCC 15.247(d)
Total Power ≤ 30 dBm
FCC 15.247(b)(3)
5.875
172

## Slide 12: Cross-Channel Interference Comparison (II)
NPRM channel allocation
  Ch172 overlaps Ch173 (20MHz) and corresponding 40MHz, 80MHz and 160MHz channels
    Remaining interference may exist from spectrum sharing techniques
  Ch172 is right next to Ch169 (20MHz) and 10MHz away from Ch177
    Interference from adjacent channels with potentially no protection
Available for WLAN
161
DSRC Band
U-NII 4
U-NII Worldwide
U-NII 3
5725
Frequency [MHz]
24 – 10log10(B) dBm/MHz
30 – 10log10(B) dBm/MHz
5825
5835
5470
5850
5875
5925
5895
165
169
173
177
181
-17 - G dBm/MHz
172

## Slide 13: Cross-Channel Interference Comparison (III)
Proposed compromise scheme
  10MHz away from closet Wi-Fi channel (Ch177)
  Maximum interference limited by -17dBm/MHz (-7dBm over 10MHz channel)
  Practical interference from measurement: Ch182 sees -17dBm/MHz+pathloss (35dB attenuation at 10MHz edge); Ch184 sees -27dBm/MHz+pathloss (45dB attenuation at 20MHz edge)
    Can further be improved by limiting the maximum transmit power allowed on Ch177
    48dB free space pathloss for co-located 5.9GHz transmitter/receiver at 1m apart
U-NII 3
Available for WLAN
161
DSRC Band
U-NII 4
U-NII Worldwide
5725
Frequency [MHz]
24 – 10log10(B) dBm/MHz
30 – 10log10(B) dBm/MHz
5825
5835
5470
-27 - G dBm/MHz
5850
5875
5925
5895
165
169
173
177
182
-17-GdBm/MHz
5905
184

## Slide 14: Cross-Channel Interference between DSRC Channels
In current DSRC channelization, service channel and safety channels are next to each other with no guard band
  When transmitting at service channel, the leakage will contaminate the reception capability on the safety channel
  May be controlled by lowering the maximum allowed power on service channel
May require improved receiver to further mitigate the problem
Proposed compromise does not change or worsen the nature of the problem