## Slide 1: Dense Apartment Complex Capacity Improvements with Channel selection and Dynamic Sensitivity Control
Date: 2013-11
Authors:

## Slide 2: Background
13/1012r4 Described Dynamic Sensitivity Control DSC and provided a throughput calculation for a hypothetical Cell Structure network.
  3005Mbps vs. 397Mbps
This presentation looks at the Apartment Complex Use Case and provides an estimate of the improvement in Capacity/Throughput when using Channel Selection and DSC

## Slide 3: Dynamic Sensitivity Control - DSC
STA measures the RSSI of the AP Beacon (R dBm)
Then sets its RX Sensitivity Threshold at (R – M) dBm, where M is the “Margin”
Hence, for example:
  STA receives Beacon at -50dBm, with Margin = 20dB STA sets RX Sensitivity Threshold to -70dBm.
Also set an Upper Limit, L, to Beacon RSSI at, say, -30 or -40dBm to cater for case when STA is very close to AP.
  Need to ensure that all the STAs in the wanted area do see each other. Hence if one STA very close to AP, then it could set RX Sensitivity too high and we get hidden STAs.

## Slide 4: Single Apartment complex

## Slide 5: Double Apartment Complex

## Slide 6: Channels
Ref:Wikipedia

## Slide 7: AP Channel Selection Analysis Program
Set-Up
Set up an Apartment block
  Number of Apartments per floor
  Number of floors
Select number of Channels (24 max)
Select percentage of Apartments to be assigned (0 – 100%)
Select number of times to run through the program
  So as to obtain a reasonable variation (e.g. run 10 times)
Program outline
Randomly select an Apartment
Scan the surrounding apartments in range
  Select channel(s) with least other APs
Output
Number of Apartments with no overlapping networks
Number of Apartments with 1 overlapping networks
Number of Apartments with 2 overlapping networks
Number of Apartments with 2+ overlapping networks

## Slide 8: Random Channel Selection
10 CH only 7% of apartments
have no overlap
25% have 3 or more overlapping
10 CH only 25 out of 100 apartments
have no overlap
26 out of 100 have 3 or more overlapping
For both double and single apartment complexes
10 CH 89% apartments have no overlap

## Slide 9: Intelligent Channel Selection – Big Improvement
Compare
Compare
Compare
Random
Channel Selection

## Slide 10
3a Dense apartment building – private access and cellular offload
Pre-Conditions
Each apartment has Wi-Fi network deployed to access internet and cloud services. In each apartment up to 3 users stream concurrently video content from the network and up to 50% of the networks are active.
At the same time each of the active Wi-Fi networks is used by 2 users for web browsing
Environment
Building with 100 apartments. One AP in each apartment of 10mx10m randomly positioned. 5 STA per AP randomly positioned in the apartment.
Applications
Cloud based applications supporting video streaming with 8k resolution.
Video throughput assumptions are: ~112Mbps per STA, delay is < 200ms, 1.0E-3 PER.
Online game
Cloud-based application as big storage
Web browsing assumptions for Social Networking are: ~20Mbps, PER 1e-3, delay<50ms
150 active video users and 100 active web browsing users in the building.
Traffic Conditions
Strong interference from unmanaged overlapping networks (neighboring apartments, and outdoor Wi-Fi network).
Multiple video display are operational simultaneously.
Interference with Zigbee, Bluetooth.
Use Case
Users watch the high quality video contents coming from the Internet or video contents stored in their PVR with VHD Display. There may be another video streams to be recorded in the Blu-ray deck.
People enjoy playing online games or local game machine with two or more people.
Other users are just accessing the Internet for email access, web browsing, etc.
Laurent Cariou (Orange)

## Slide 11: Capacity/Throughput Requirement
From Use Case
5 STAs per Apartment
Video 112Mbps
Web Browsing 20Mbps
What is peak requirement?
1- 2 STAs Video 112 -224Mbps
3 Browsing 60Mbps
Total per Apartment 172 - 284Mbps
Is this what was meant in the Use Case?

## Slide 12: Single Apartment Complex – 11n

## Slide 13: Double Apartment Complex – 11n

## Slide 14: Single Apartment Complex 11ac

## Slide 15: Single Apartment Complex Total Capacity
2.96 x Improvement

## Slide 16: Double Apartment Complex Total Capacity
4.12 x Improvement

## Slide 17: Dense Apartment Complex
2SS 65k A-MPDU
Random Channel Selection
  Single Complex Capacity average 163Mbps per apartment
    Note: 9% are at 119Mbps, 1% at 500Mbps
  Double Apartment Capacity is average 117Mbps per apartment
    Note: 11% are at 85Mbps, 8% at 265Mbps
Channel Selection
  Single Complex Capacity is average 163Mbps per apartment
  Double Apartment Capacity is average 133Mbps per apartment
DSC plus Channel Selection
  Single and Double Complex Capacity is average 481Mbps per apartment
    Note: 92% are at 500Mbps, 8% at 265Mbps (Meets 224Mbps requirement)
296% improvement for Single Apartment Complex
412% improvement for Double Apartment Complex

## Slide 18: Discussion
The techniques shown here can be applied for most Use Cases:
  Available Channels
  Overlap calculation
  Channel Selection
  Effective Throughputs (EDCA Overhead)
We could (should) establish the ‘present situation’ for each major Use Case, and results compared to the ‘required capacities’. This gives PAR number.
Then apply ‘new ideas’ to establish the possible gains
DSC could provide good improvements in (Most/Some) Use Cases