## Slide 1: CC11 Comments Analysis
Date: 2014-01-07
Authors:

## Slide 2: Abstract
This submission provides an analysis of comments received on the draft PAR (11-13/1410r1). Subsections analyzed are:
  5.2b and 5.5 (scope and need)
  8.1 (explanatory notes)

## Slide 3: Changes in 11-13/1410r2
IEEE 802.11 scope  5.2a (r2)
5.2.a (r1)  5.2b (r2)
5.2b (r1)  deleted
IEEE 802.11 purpose  5.4 (r2)
5.4 (r1)  5.5 (r2)
5.5 (r1)  deleted

## Slide 4: Section 5.2b -Current Scope
This amendment defines standardized modifications to both the 802.11 physical layers (PHY) and the 802.11 Medium Access Control Layer (MAC) that enable modes of operation capable of supporting TBD times improvements in the average throughput per station in indoor, outdoor, and dense deployment scenarios.
The new standard operates below 6 GHz carrier frequency while ensuring backward compatibility and coexistence with legacy IEEE802.11 devices in the 2.4 GHz and 5 GHz unlicensed bands.

## Slide 5: Section 5.5 - Purpose
WLAN devices are currently been deployed in diverse scenarios. Previous amendments have focused on increasing peak rates and have shown modes of operation capable of supporting several Gbps rates. This project will focus on the need for efficiency improvements in high density deployments. In addition, improvements will be made to support environments such as wireless corporate office, outdoor hotspot, dense residential apartments, or stadiums. Improvements will target increasing the area throughput and/or average throughput per station. Quality of experience for the user will be addressed by improving the minimum average data rate, or maximum connection setup delay, or maximum packet transmission delay.

## Slide 6: Power Efficiency
Issue | CID | Options
Include power efficiency in the scope | 6,12,62,11,29,256,182 | Add some text related to power consumption in scope in explanatory notes do nothing

## Slide 7: Target Frequency Bands
Issue | CID | Options
Be specific about the bands where HEW is expected to operate | 16, 99, 199, 209, 286, 227 | -explicit mention of 2.4 and 5 GHz Add 60 GHz band

## Slide 8: Backward Compatibility and Coexistence with Legacy 802.11 Devices
Issue | CID | Options
What does legacy mean? | 100, 200, 201, 247, 250, 259, 299 | Limit backward compatibility to 11n and 11ac devices only backward compatible to OFDM devices - Backward compatibility to all devices

## Slide 9: Metrics
Issue | CID | Options
Include more than one metric in the scope (add area throughput or be less specific) | 3, 4, 33, 35, 36, 37, 40, 44, 45, 51, 61, 63, 68, 70, 71, 82, 84, 95, 97, 101, 103, 104, 113, 114, 116, 117, 120, 131, 177, 179, 184, 188, 189, 198, 202, 203, 224, 235, 238, 242, 243, 246, 248, 258, 260, 283, 288, 295, 296, 304, 305 | Do nothing add area throughput in the scope be less specific by adding ..”metrics such as …” add more metrics in explanatory notes.
QoE definition and how it relates to metrics |  | - QoE is subjective. Remove references to QoE and substitute with other term
Add 5th percentile (CDF) metric to ensure adequate distribution of throughput among STAs |  | Add 5th percentile in scope in explanatory notes
Reference scenario(s) for improved performance |  | - Reference doc 11-13/1001r5
Consistency of performance metrics. |  | Delete references to delay, jitter and setup delay.

## Slide 10: Miscellaneous
Issue | CID | Options
Outdoor should be limited to pedestrian speeds | 15, 98 | - Limit outdoor to pedestrian speeds
Support of 802.11ac in 2.4 GHz band (256 QAM, MU-MIMO, VHT preamble, etc.) | 30 | Do nothing. The subject is already covered by HEW scope draft a separate PAR for VHT on 2.4 GHz
Relationship to cellular and 5G | 1, 46 | Add text to emphasize relationship to cellular do nothing

## Slide 11: Miscellaneous
Issue | CID | Options
Security and privacy | 181 | - Do nothing. HEW will use any security enhancements defined elsewhere in the WG
Improved coexistence with BT and 802.15.4 operating in the same band | 179 | do nothing. Coexistence assurance document is required.
TBD | 47, 180, 213, 226, 263 | Replace with 2 (or 200%) replace with a different value one value or many values – one for each metric

## Slide 12
Issue | CID | Options
Section 5.5 – need to focus on the need for the project not repeat what the project will do |  | - rewrite

## Slide 13: Proposed “Scope” (5.2b)
This amendment defines standardized modifications to both the 802.11 physical layers (PHY) and the 802.11 Medium Access Control Layer (MAC) that enable modes of operation capable of supporting at least two (2) times improvements in the average throughput per station (measured at the MAC data service access point) in dense indoor, and pedestrian-speed outdoor, and dense deployment scenarios.
The new standard operates in the 2.4 GHz and 5 GHz frequency bands. below 6 GHz carrier frequency while ensuring The new amendment shall include a mode of operation ensuring backward compatibility and coexistence with legacy IEEE802.11 devices in the 2.4 GHz and 5 GHz unlicensed bands operating in the same bands.

## Slide 14: Proposed “Need for the Project” (5.5)
WLAN devices are currently being been deployed in diverse environments scenarios. These environments are characterized by the existence of many access points and many stations in a geographically limited areas. Increased interference from neighbouring devices gives rise to performance degradation. Additionally WLAN devices are increasingly required to support a variety of applications such as video, cloud access, and offloading. With the real-time performance requirements of some of these application, WLAN users demand improved reliability in delivering their applications. Unlike previous amendments where the focus was on improving aggregate throughput, this amendment will focus on improving metrics that are affecting user experience, such as average per station throughput, the 5th percentile of per station throughput, and area throughput. Previous amendments have focused on increasing peak rates and have shown modes of operation capable of supporting several Gbps rates. This project will focus on the need for efficiency improvements in high density deployments. In addition, Improvements will be made to support environments such as wireless corporate office, outdoor hotspot, dense residential apartments, or stadiums. Improvements will target increasing the area throughput and/or average throughput per station. Quality of experience for the user will be addressed by improving the minimum average data rate, or maximum connection setup delay, or maximum packet transmission delay.

## Slide 15: Proposed “Explanatory Notes” (8.1)
Unlike previously developed IEEE 802.11 amendments, this amendment will focus on system-level metrics representative of the performance obtained by stations in typical deployment environments. Previous amendments focused on peak theoretical throughput achieved in ideal conditions.
5.2.b
Average throughput per station is related to both aggregate throughput and area throughput. To ensure even distribution of throughput among a number of stations in an area, the 5th percentile measure of the per station throughput will be used.
Since the values of these metrics of interest will depend on the scenario, the focus will be on the relative improvement of these metrics compared to previous 802.11 amendments (802.11n in 2.4GHz and 802.11ac in 5GHz).
The amendment will be evaluated with a set of typical deployment scenarios representative of the main expected usage models that are expected to suffer bottlenecks in the coming years: residential, enterprise, indoor and outdoor hotspots. HEW SG has initiated the creation of a high-level simulation scenario working document (ref: 11-13/0657r61001r5) to model these scenarios.

## Slide 16: Proposed Explanatory Notes (8.1)- cntd
These scenarios highlight three categories of objectives to improve WLAN efficiency in WLANs:
  Significantly increase airtime usage efficiency Efficient use of spectrum resources in scenarios with a high density of STAs per BSS.
  Significantly Increase spectral reuse and manage interference between neighboring OBSS in scenarios with a high density of both STAs and BSSs, in cases where they may or may not share the same management entity
  Increased robustness to outdoor propagation characteristics and increase uplink transmission reliability
The metrics will directly correspond to the user experience in the identified scenarios, including overall throughputs, distribution of throughputs (e.g. 5th percentile of user throughput CDF), and satisfaction of packet delay and latency/jitter/packet loss constraints requirements of applications.
This amendment may include the capability to handle multiple simultaneous communications in both the spatial and frequency domains, in both the UL and DL.
This amendment may include modes of operation that improve the power consumption of battery- operated devices.

## Slide 17: References