## Slide 1: Thoughts on HEW PAR
Date: 2014-01-20
Authors:

## Slide 2
Authors:

## Slide 3: Introduction
WLAN has been incredibly successful over the last decade, thanks to its ease of deployment and low cost
The HEW SG has been created to focus on improving efficiency, especially in high density networks, for the next generation WLAN
We believe that enhancements to both Quality of Experience (QoE) and power efficiency would be needed to make the next generation WLAN more attractive and competitive

## Slide 4: Enhanced QoE
QoE would benefit from achieving lower latency, lower jitter, and higher average minimum throughput per STA to support delay sensitive applications
Such requirements have been largely incorporated in the draft PAR [3]
  5.5 Need for the Project
    Additionally WLAN devices are increasingly required to support a variety of applications such as video, cloud access, and offloading. With the real-time performance requirements of some of these application, WLAN users demand improved reliability in delivering their applications. Unlike previous amendments where the focus was on improving aggregate throughput, this amendment will focus on improving metrics that are affecting user experience, such as average per station throughput, the 5th percentile of per station throughput, and area throughput.
  8.1 Explanatory Notes
    The metrics will directly correspond to the user experience in the identified scenarios, including overall throughputs, distribution of throughputs (e.g. 5th percentile of user throughput CDF), and satisfaction of packet delay and packet loss requirements of applications.

## Slide 5: Power Efficiency
Power efficiency is critical to battery powered devices to enable future pervasive WLAN use cases
New challenges to the next generation WLAN:
  Dense deployments may lead to congested wireless medium, thereby diminishing the benefits of existing 802.11 power saving schemes
  Better QoE support, especially better support of low-latency applications, may force devices to power ON radios more frequently
  With the increase in peer-to-peer communication and Internet of Things, a mobile device may operate as a “master” from time to time. The traditional AP/STA power saving modes may not be useful or applicable

## Slide 6: Proposed PAR text changes (1)
5.2.b Scope of the project:
This amendment defines standardized modifications to both the 802.11 physical layers (PHY) and the 802.11 Medium Access Control Layer (MAC) that enable modes of operation capable of supporting at least two (2) times improvements in the average throughput per station (measured at the MAC data service access point) in dense indoor and pedestrian-speed outdoor deployment scenarios., while also improving average power efficiency per station.

## Slide 7: Proposed PAR text changes (2)
5.5 Need for the Project:
WLAN devices are currently being deployed in diverse environments. These environments are characterized by the existence of many access points and many stations in a geographically limited areas. Increased interference from neighbouring devices gives rise to performance degradation. Additionally WLAN devices are increasingly required to support a variety of applications such as video, cloud access, and offloading. With the real-time performance requirements of some of these application, WLAN users demand improved reliability and lower latency in delivering their applications. Further, users of battery powered WLAN devices also desire good battery life while consuming these applications in such dense environments. Unlike previous amendments where the focus was on improving aggregate throughput, this amendment will focus on improving metrics that are affecting user experience, such as average per station throughput, the 5th percentile of per station throughput, and area throughput., and average power efficiency per station. Improvements will be made to support environments such as wireless corporate offices, outdoor hotspots, dense residential apartments, or stadiums.

## Slide 8: References
[1] 11-13-1333-00-0hew-power-efficiency-par-requirements
[2] 11-13-1410-01-0hew-802-11-hew-draft-par-and-5c
[3] 11-14-0013-00-0hew-cc11-comments-analysis