## Slide 1: E-Education Analysis HEW SG
Date: 2014-01
Authors:

## Slide 2: Background
This presentation looks at the E-Education HEW Use Case.
See also:
Use Case Dense Apartments 13/1487r2
Airport Capacity 13/1489r4
DSC is explained in 13/1012

## Slide 3: Objective
To look at the prime HEW Use Cases and see what is theoretically possible using known techniques.
Then to determine if there is a “gap” that can lead to a requirement for HEW.

## Slide 4
1e e-Education
Scenario Characteristics:
  Dense STAs (40~60 STAs) in one classroom with one AP
  20~30 classrooms in one typical school building (3~6 floors)
  Thus, nearby 1,000 STAs with 20~30 APs within a building space.
Typical education applications:
  Video streaming among teacher and students;
  Teachers/Students demonstrate theirs desktop to others;
  File transfer and sharing;
  4+ subgroup in one classroom with multicasting traffic for screen sharing or video;
  Throughput assumption: longtime/stable throughput in one classroom >= 20 Mbps
Challenges and Issues:
  Fast Connection: Very long STAs registering time (1~5 minutes) delay the start of a class;
  Interference Control and Delay Optimization:
    Annoying lag in screen sharing, video streaming and command response (sometimes it is longer than 20 seconds)
    Very low bandwidth for e-homework submission in the same period.
Laurent Cariou (Orange)

## Slide 5: 1e e-Education
Pre-Conditions
WLAN is deployed in a each classroom of a campus in order to provide communication tools for e-Education.
Environment
Dense STAs (40~60 STAs) in one classroom with one AP. 20~30 classrooms in one typical school building (3~6 floors).
Nearby 1,000 STAs with 20~30 APs within a building space.
Applications
Video streaming among teacher and students;
Teachers/Students demonstrate theirs desktop to others;
File transfer and sharing;
4+ subgroup in one classroom with multicasting traffic for screen sharing or video;
Throughput assumption: longtime/stable throughput in one classroom >= 20 Mbps
Traffic Conditions
Interference between APs in different classrooms belonging to the same managed ESS due to high density deployment.
interference with peer-to-peer networks within each classroom.
Use Case
e-Education starts in multiple classrooms simultaneously.
Teacher/students demonstrated their desktop to others, video or screens are shared.
Laurent Cariou (Orange)

## Slide 6: Classroom
Say 30 x 30ft
40 desks

## Slide 7: Channels
Ref:Wikipedia

## Slide 8: Building Complex example – one side
Assumed 3dB wall loss
10dB Floor loss
Use of directivity on antennas could assist

## Slide 9: Building Complex Example – Other side
Note: Without DSC blocked rooms doubles.

## Slide 10: Channel Selection
As situation is controlled, AP channels can be preset
Example is extreme for 36 classrooms, worse case layout

## Slide 11: 11ac Rates
Assuming 2SS for the STA, and using SU MIMO
With DSC 10 Channels (40MHz)
Without DSC 20 Channels (20MHz)
Signal strength within each class is >-45dBm hence can use 256 QAM 5/6
  11ac PHY Rate for 40MHz, 2SS is 400Mbps (10 Channels)
    Max Throughput 344Mbps (131k agg)
    Say 240Mbps throughput*
  11ac PHY Rate for 20MHz, 2SS is 173Mbps (3/4 rate, 5/6 is excluded)
    Max Throughput 150Mbps (65k agg – 131k exceeds length)
    Say 105Mbps throughput*
Downlink could use MU-MIMO?
*Assuming EDCA Overhead.

## Slide 12: What is Use Case Requirement?
Unclear what the Use Case requirement is.
  20 Mbps?
Downlink would be multicast?
With DSC ~240Mbps per class (6Mbps per pupil)
Without DSC ~ 105Mbps per class (2.6Mbps per pupil)
Not sure what the ‘gap’ is, but hopefully this quick analysis will help determine it.

## Slide 13: Discussion
Isolation between classrooms could be improved by antenna directivity
With 11ac SU-MIMO, DSC provides 240Mbps per classroom throughput
Without DSC SU-MIMO provides ~105Mbps per classroom throughput
“Fast” connection – is this satisfied with 11ai?
Interference/OBSS greatly improved by DSC and also by antenna positing.

## Slide 14: Conclusions
My personal opinion is that 11ac provides sufficient data throughput and efficiency and not easy to see any need for improvement.
The basic need is for higher channel re-use so that the higher BWs can be used.
Channel re-use can be improved with DSC but also by not using omni-directional antennas.
  Corner antennas, such as used in cellular for example.
  Easy to do if a ‘managed’ network.