IEEE P802.11
Wireless LANs

| 802.11 CID2128 Re-write of Probe Response text |
| --- |
| Date: 2014-02-26 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Adrian Stephens | Intel Corporation |  |  | Adrian.p.stephens@intel.com |
| Mark Rison | Samsung |  |  |  |
| Jarkko Kneckt | Nokia |  |  |  |
| Marc Emmelmann |  |  |  |  |

# Status (R4)

R3 was reviewed and kicked around by the co-authors.  Mark Rison restructured the conditions into a much more pleasing and consistent form. Marc Emmelmann restructured the outcome in preparation for TGai.  A bunch of inconsistencies and terminology difficulties were then addressed.

# Status (R3)

R2 was reviewed by TGmc.

Carlos Cordeiro agreed to research the logic behind the following text commented below:  “A Multi-band capable non-AP STA for which the last received probe request included a Multi-band element”

Marc Emmelmann and Jarkko Kneckt agreed to verify logic and indicated the subclause should be split into two parts.  One part to define filtering conditions.  The other to describe construction of the probe response.

The author expects that a consensus position can be brought to TGmc prior to or during the March 2014 session.

# Comment and proposed change

| 2129 | 1365.52 | 10.1.4.3.3 |  | "Only the following STAs respond to probe requests"Either this statement has no effect, or it creates an exception to the normative statement "STAs ... shall respond" at 1365.27. | Merge this list with the lettered list, or find a way to call out the exceptions from the "shall respond" statement. |
| --- | --- | --- | --- | --- | --- |

Discussion:

At 1365.27, we have:  “STAs, subject to the criteria below, receiving Probe Request frames shall respond”.

At 1365.41, we have: “Additionally, STAs … shall … response”

At 1365.52, we have: “only the following STAs respond…”

At 1366.14, we have “STAs … shall respond”

At 1366.29, we have “mesh STA ... shall not respond”

It is not immediately clear that all of these shalls and shall nots are distinct.  Certainly a “shall” and a matching “shall not” creates a conflict.

In doing this work, I found plenty of conflicts.   For example the “only … STAs shall respond” does not include a non-AP STA in an infrastructure BSS.   But 1365.27 says it does.

At 1366.14, a STA shall respond if there is a match on SSID,  without calling out any other fields,  such as Address 1 or Address 3.

The more I look at this,  the more tempted I am to say “let sleeping worms lie”.

The original text is:

STAs, subject to the criteria below, receiving Probe Request frames shall respond with a probe response only if the Address 1 field in the probe request is the broadcast address or the specific MAC address of the STA, and either of the following applies:(#1475) The STA is a mesh STA and the Mesh ID in the probe request is the wildcard Mesh ID or the specific Mesh ID of the STA. The STA is not a mesh STA and The SSID in the probe request is the wildcard SSID, the SSID in the probe request is the specific SSID of the STA, or the specific SSID of the STA is included in the SSID List element, and The Address 3 field in the probe request is the wildcard BSSID or the BSSID of the STA. Additionally, STAs with dot11InterworkingServiceActivated equal to true, receiving Probe Request frames containing an Interworking field in the Extended Capabilities element set to 1 shall examine the Interworking element in the received Probe Request frame and respond with a probe response only if The HESSID field, if present in the Interworking element, is the wildcard HESSID or the HESSID of the STA, and The Access Network Type field in the Interworking element is the wildcard Access Network Type or the Access Network Type of the STA. Only the following STAs respond to probe requests:(Ed) DMG STAs that are not members of a PBSS that are performing active scan as defined in Fehler! Verweisquelle konnte nicht gefunden werden.(M34) Multi-band capable non-AP STAs for which the last received probe request included a Multi-band element(11ad) APs PCPs(11ad) STAs in an IBSS STAs in an MBSS A result of the procedures defined in this subclause is that in each non-DMG(11ad)(Ed) infrastructure BSS, and in each IBSS there is at least one STA that is awake at any given time to receive and respond to probe requests. In an MBSS, STAs might not be awake at any given time to respond to probe requests. In an infrastructure BSS or in an IBSS, a STA that sent a Beacon frame shall remain in the Awake state and shall respond to probe requests, subject to criteria in the next paragraph, until a Beacon frame with the current BSSID is received. If the STA is contained within an AP, it shall remain in the Awake state and always respond to probe requests, subject to criteria in the next paragraph. There may be more than one STA in an IBSS that responds to any given probe request, particularly in cases where more than one STA transmitted a Beacon or DMG Beacon(11ad)(Ed) frame following the most recent TBTT, either due to not receiving successfully a previous Beacon or DMG Beacon(11ad)(Ed) frame or due to collisions between beacon transmissions. In an infrastructure BSS or in an IBSS, STAs receiving Probe Request frames shall respond with a probe response when the SSID in the probe request is the wildcard SSID or matches the specific SSID of the STA or when the specific SSID of the STA is included in the SSID List element. Furthermore, a STA with dot11RadioMeasurementActivated true receiving a probe request with a DSSS Parameter Set element containing a Current Channel field value that is not the same as the value of dot11CurrentChannel shall not respond with a probe response. A DMG STA that is not member of a PBSS but that is performing active scan as defined in Fehler! Verweisquelle konnte nicht gefunden werden., an(11ad) AP, and a PCP(11ad) shall respond to all probe requests meeting the above criteria if the transmit antenna of the DMG STA is trained to transmit to the STA from which a probe request was received.(Ed)(M34) In an IBSS a STA that transmitted a Beacon or DMG Beacon(11ad) frame since the last TBTT shall respond to group addressed Probe Request frames. A STA in an IBSS shall respond to Probe Request frames sent to the individual address of the STA. An (#1151)mesh STA that receives a Probe Request frame shall not respond with a Probe Response frame when dot11RadioMeasurementActivated is true and the Probe Request frame contains a DSSS Parameter Set element with its Current Channel field value different from the value of dot11CurrentChannelNumber. Probe Response frames shall be sent as directed frames to the address of the STA that generated the probe request.(#1511) Requested Element IDs in the Request element shall be included in the Probe Response if the responding STA supports it. In an improperly formed Request element, a STA may ignore the first element requested that is not ordered properly and all subsequent elements requested. In the Probe (#99)Response frame, the STA shall return the requested elements in the same order as requested in the Request element. If dot11RadioMeasurementActivated is true and if the Request element of the Probe Request includes the RCPI element ID, the STA shall include in the Probe Response an RCPI element containing the measured RCPI value of the received Probe Request frame. If no measurement result is available, the RCPI value shall be set to indicate that a measurement is not available.

I propose to replace this text with the following:

10.1.4.3.3 Criteria for sending a probe response A STA that receives a Probe Request frame shall not respond if any of the following apply: The STA does not match any of the following criteria: The STA is an AP The STA is an IBSS STA The STA is a mesh STA The STA is a DMG STA that is not a member of a PBSS and that is performing active scan as defined in 10.1.4.3.2 The STA is a PCP The STA is a multi-band capable non-AP STA for which the last received probe request included a Multi-band element The Address 1 field of the Probe Request frame contains an individual address that is not the MAC address of the STA. The STA is a non-AP STA in an infrastructure BSS and the Address 1 field of the Probe Request frame contains the broadcast address. The STA is a non-PCP STA in a PBSS and the Address 1 field of the Probe Request frame contains the broadcast address. The STA is in an IBSS and did not transmit a Beacon or DMG Beacon frame since the last TBTT, and the Address 1 field of the Probe Request frame contains the broadcast address. The STA is a mesh STA and either of the following criteria are met: The Probe Request frame does not contain a Mesh ID element, or The Mesh ID element in the Probe Request frame is present but does not contain the wildcard Mesh ID and does not match the Mesh ID of the MBSS with which the STA is peered. The STA is not a mesh STA and none of the following criteria are met: The SSID in the Probe Request frame is the wildcard SSID, or The SSID in the Probe Request frame matches the SSID of the STA’s, or The SSID List element is present in the Probe Request frame and includes the SSID of the STA’s BSS. The STA is not a mesh STA and the Address 3 field of the Probe Request frame does not contain a wildcard BSSID and does not match the BSSID of the STA’s BSS. The STA has dot11InterworkingServiceActivated equal to true and the Probe Request frame contains an Interworking element and an Extended Capabilities element whose Interworking field contains the value 1, and at least one of the following criteria is not met: The HESSID field of the Interworking element is absent, or is present and contains the wildcard HESSID or matches the HESSID field of the InterworkingInfo parameter of the last MLME-START.request or MLME-JOIN.request primitive, or The Access Network Type field of the Interworking element contains the wildcard Access Network Type or matches the Access Network Type of the STA. The STA has dot11RadioMeasurementActivated equal to true and the Probe Request frame contains a DSSS Parameter Set element in which the Current Channel field contains a value that is not the same as dot11CurrentChannel. The STA is a DMG STA and the transmit antenna of the DMG STA is not trained to transmit to the STA from which the Probe Request frame was received. An AP shall remain in the Awake state, and shall respond to probe requests, subject to the criteria above. An IBSS STA that sent a Beacon or DMG Beacon frame shall remain in the Awake state, and shall respond to probe requests, subject to the criteria above, until a Beacon or DMG Beacon frame with the BSSID of the STA’s IBSS is received. A mesh STA or PCP that is awake shall respond to probe requests, subject to the criteria above. NOTE--A result of the procedures defined in this subclause is that: In a infrastructure BSS, the AP is is awake at any given time to respond to probe requests. In an IBSS there is at least one STA that is awake at any given time to respond to probe requests. More than one STA might respond to any given probe request, particularly in cases where more than one STA transmitted a Beacon or DMG Beacon(11ad)(Ed) frame following the most recent TBTT, either due to not receiving successfully a previous Beacon or DMG Beacon(11ad)(Ed) frame or due to collisions between beacon transmissions. In an MBSS or PBSS, no STA might be awake at any given time to respond to probe requests. 10.1.4.3.3a Contents of a probe response A STA that responds to a probe request according to 10.1.4.3.3 shall transmit a Probe Response frame as follows: The Probe Response frame is individually addressed to the STA that generated the Probe Request frame. Each element requested in a Request element shall be included in the Probe Response frame if the responding STA supports that element. In the Probe (#99)Response frame, the STA shall return the requested elements in the same order as requested in the Request element. If dot11RadioMeasurementActivated is true and if the Request element of the Probe Request includes the RCPI element ID, the STA shall include in the Probe Response an RCPI element containing the measured RCPI value of the received Probe Request frame. If no measurement result is available, the RCPI value shall be set to indicate that a measurement is not available.

State of play after commenting on R3:

10.x.x.x Probe response criteria A STA that receives a Probe Request frame shall not respond if any of the following apply: The STA does not match any of the following criteria: The STA is a DMG STA that is not a member of a PBSS and that is performing active scan as defined in Fehler! Verweisquelle konnte nicht gefunden werden. The STA is a multi-band capable non-AP STA for which the last received probe request included a Multi-band element The STA is an AP The STA is a PCP The STA is in an IBSS The STA is in an MBSS The Address 1 field of the Probe Request frame contains an individual address that is not the MAC address of the STA. The STA is a non-AP STA in an infrastructure BSS and the Address 1 field of the Probe Request frame contains the broadcast address. The STA is in an IBSS and did not transmit a Beacon or DMG Beacon frame since the last TBTT, and the Address 1 field of the Probe Request frame contains the broadcast address. The STA is a mesh STA and the Mesh ID in the Probe Request frame is not the wildcard Mesh ID and does not match the specific Mesh ID of the STA. The STA is not a mesh STA and none of the following criteria are met: The SSID in the Probe Request frame is the wildcard SSID, or The SSID in the Probe Request frame matches the SSID of the STA, or The SSID List element is present and includes the SSID of the STA. The STA is not a mesh STA and the Address 3 field of the Probe Request frame does not contain a wildcard BSSID and does not match the BSSID of the STA. The STA has dot11InterworkingServiceActivated equal to true and the Probe Request frame contains an Interworking element and an Extended Capabilities element whose Interworking field contains the value 1, and at least one of the following criteria is not met: The HESSID field of the Interworking element is absent, or is present and contains the wildcard HESSID or matches the HESSID of the STA, or The Access Network Type field of the Interworking element contains the wildcard Access Network Type or matches the Access Network Type of the STA. The STA has dot11RadioMeasurementActivated equal to true and the Probe Request frame contains a DSSS Parameter Set element in which the Current Channel field contains a value that is not the same as dot11CurrentChannel. The STA is a DMG STA and the transmit antenna of the DMG STA is not trained to transmit to the STA from which the probe request was received. A result of the procedures defined in this subclause is that: In each non-DMG(11ad)(Ed) infrastructure BSS, and in each IBSS there is at least one STA that is awake at any given time to receive and respond to probe requests. In an MBSS, STAs might not be awake at any given time to respond to probe requests. In an infrastructure BSS or in an IBSS, a STA that sent a Beacon frame shall remain in the Awake state, and shall respond to probe requests, subject to the criteria above, until a Beacon frame with the current BSSID is received. If the STA is contained within an AP, it shall remain in the Awake state, and shall respond to probe requests, subject to the criteria above. There may be more than one STA in an IBSS that responds to any given probe request, particularly in cases where more than one STA transmitted a Beacon or DMG Beacon(11ad)(Ed) frame following the most recent TBTT, either due to not receiving successfully a previous Beacon or DMG Beacon(11ad)(Ed) frame or due to collisions between beacon transmissions. 10.x.x.x Sending a response to probe request If a STA shall respond to a probe request according to REF-TO-NEW-CLAUSE-ABOVE, the STA shall transmit a Probe Response frame as follows: Otherwise, the STA shall transmit a Probe Response frame as follows: The Probe Response frame is individually addressed to the STA that generated the Probe Request frame. Requested Element IDs in the Request element shall be included in the Probe Response if the responding STA supports it. In an improperly formed Request element, a STA may ignore the first element requested that is not ordered properly and all subsequent elements requested. In the Probe (#99)Response frame, the STA shall return the requested elements in the same order as requested in the Request element. If dot11RadioMeasurementActivated is true and if the Request element of the Probe Request includes the RCPI element ID, the STA shall include in the Probe Response an RCPI element containing the measured RCPI value of the received Probe Request frame. If no measurement result is available, the RCPI value shall be set to indicate that a measurement is not available.

Status: for additional review

# Analysis

I will try and demonstrate that each normative statement in the original has a matching rules in the final.

| Original Rule | Rule | Met by |
| --- | --- | --- |
| OR1 | STAs, subject to the criteria below, receiving Probe Request frames shall respond with a probe response only if the Address 1 field in the probe request is the broadcast address or the specific MAC address of the STA, except if OR2 or OR3 applies | 1.If the Address 1 field of the Probe Request frame contains an individual address that is not the MAC address of the STA, the procedure terminates without sending a response. The STA transmits a Probe Response frame as follows |
| OR2 | The STA is a mesh STA and the Mesh ID in the probe request is the wildcard Mesh ID or the specific Mesh ID of the STA. | If the STA is a mesh STA and the Mesh ID in the Probe Request frame is not the wildcard Mesh ID and does not match specific Mesh ID of the STA, the procedures terminates without sending a response |
| OR3 | The STA is not a mesh STA and The SSID in the probe request is the wildcard SSID, the SSID in the probe request is the specific SSID of the STA, or the specific SSID of the STA is included in the SSID List element, and The Address 3 field in the probe request is the wildcard BSSID or the BSSID of the STA | If the STA is not a mesh STA: a. If none of the following apply the procedures terminates without sending a response, The SSID in the Probe Request frame is the wildcard SSID, The SSID in the Probe Request frame matches the SSID of the STA, The SSID List element is present and includes the SSID of the STA. |
| OR4 | Additionally, STAs with dot11InterworkingServiceActivated equal to true, receiving Probe Request frames containing an Interworking field in the Extended Capabilities element set to 1 shall examine the Interworking element in the received Probe Request frame and respond with a probe response only if The HESSID field, if present in the Interworking element, is the wildcard HESSID or the HESSID of the STA, and The Access Network Type field in the Interworking element is the wildcard Access Network Type or the Access Network Type of the STA. | A STA that has dot11InterworkingServiceActivated equal to true and receives a Probe Request frame containing the Interworking field in the Extended Capabilities element equal to 1 and an Interworking element terminates the procedure without sending a response unless both the following criteria are met: The HESSID field of the Interworking element is absent or is present and contains the wildcard HESSID or matches the HESSID of the STA, and The Access Network Type field of the Interworking element contains the wildcard Access Network Type or matches the Access Network Type of the STA. |
| OR5 | Only the following STAs respond to probe requests:(Ed) DMG STAs that are not members of a PBSS that are performing active scan as defined in Fehler! Verweisquelle konnte nicht gefunden werden.(M34) Multi-band capable non-AP STAs for which the last received probe request included a Multi-band element(11ad) APs PCPs(11ad) STAs in an IBSS STAs in an MBSS | If the STA does not match any of the following criteria, and the procedure terminates without sending a response. A DMG STA that is not a member of a PBSS and that is performing active scan as defined in Fehler! Verweisquelle konnte nicht gefunden werden. A Multi-band capable non-AP STA for which the last received probe request included a Multi-band element The STA is an AP The STA is a PCP The STA is in an IBSS The STA is in an MBSS |
| OR6 | In an infrastructure BSS or in an IBSS, STAs receiving Probe Request frames shall respond with a probe response when the SSID in the probe request is the wildcard SSID or matches the specific SSID of the STA or when the specific SSID of the STA is included in the SSID List element. | If the STA is not a mesh STA: a. If none of the following apply the procedures terminates without sending a response, The SSID in the Probe Request frame is the wildcard SSID, The SSID in the Probe Request frame matches the SSID of the STA, The SSID List element is present and includes the SSID of the STA. The STA transmits a Probe Response frame |
| OR7 | Furthermore, a STA with dot11RadioMeasurementActivated true receiving a probe request with a DSSS Parameter Set element containing a Current Channel field value that is not the same as the value of dot11CurrentChannel shall not respond with a probe response. | A STA that has dot11RadioMeasurementActivated equal to true and receives a Probe Request frame containing a DSSS Parameter Set element in which the Current Channel field contains a value that is not the same as dot11CurrentChannel terminates without sending a response. |
| OR8 | A DMG STA that is not member of a PBSS but that is performing active scan as defined in Fehler! Verweisquelle konnte nicht gefunden werden., an(11ad) AP, and a PCP(11ad) shall respond to all probe requests meeting the above criteria if the transmit antenna of the DMG STA is trained to transmit to the STA from which a probe request was received. | If the STA does not match any of the following criteria, and the procedure terminates without sending a response. A DMG STA that is not a member of a PBSS and that is performing active scan as defined in Fehler! Verweisquelle konnte nicht gefunden werden. The STA is an AP The STA is a PCP A DMG STA terminates the procedure without sending a response if the transmit antenna of the DMG STA is not trained to transmit to the STA from which a probe request was received. |
| OR9 | In an IBSS a STA that transmitted a Beacon or DMG Beacon(11ad) frame since the last TBTT shall respond to group addressed Probe Request frames. A STA in an IBSS shall respond to Probe Request frames sent to the individual address of the STA. | If the STA does not match any of the following criteria, and the procedure terminates without sending a response. The STA is in an IBSS If the STA is in an IBSS, the STA did not transmit a Beacon or DMG Beacon frame since the last TBTT, and the Address 1 field of the Probe Request frame contains the broadcast address, the procedure terminates without sending a response … The STA transmits a Probe Response frame |
| OR10 | An (#1151)mesh STA that receives a Probe Request frame shall not respond with a Probe Response frame when dot11RadioMeasurementActivated is true and the Probe Request frame contains a DSSS Parameter Set element with its Current Channel field value different from the value of dot11CurrentChannelNumber. | STA that has dot11RadioMeasurementActivated equal to true and receives a Probe Request frame containing a DSSS Parameter Set element in which the Current Channel field contains a value that is not the same as dot11CurrentChannel terminates without sending a response. |
| OR11 | Probe Response frames shall be sent as directed frames to the address of the STA that generated the probe request.(#1511) | The Probe Response frame is individually addressed to the STA that generated the Probe Request frame |
| OR12 | Requested Element IDs in the Request element shall be included in the Probe Response if the responding STA supports it. In an improperly formed Request element, a STA may ignore the first element requested that is not ordered properly and all subsequent elements requested. In the Probe (#99)Response frame, the STA shall return the requested elements in the same order as requested in the Request element. | Requested Element IDs in the Request element shall be included in the Probe Response if the responding STA supports it. In an improperly formed Request element, a STA may ignore the first element requested that is not ordered properly and all subsequent elements requested. In the Probe (#99)Response frame, the STA shall return the requested elements in the same order as requested in the Request element. |
| OR13 | If dot11RadioMeasurementActivated is true and if the Request element of the Probe Request includes the RCPI element ID, the STA shall include in the Probe Response an RCPI element containing the measured RCPI value of the received Probe Request frame. If no measurement result is available, the RCPI value shall be set to indicate that a measurement is not available. | If dot11RadioMeasurementActivated is true and if the Request element of the Probe Request includes the RCPI element ID, the STA shall include in the Probe Response an RCPI element containing the measured RCPI value of the received Probe Request frame. If no measurement result is available, the RCPI value shall be set to indicate that a measurement is not available. |
| OR14 | A result of the procedures defined in this subclause is that in each non-DMG(11ad)(Ed) infrastructure BSS, and in each IBSS there is at least one STA that is awake at any given time to receive and respond to probe requests. In an MBSS, STAs might not be awake at any given time to respond to probe requests. In an infrastructure BSS or in an IBSS, a STA that sent a Beacon frame shall remain in the Awake state and shall respond to probe requests, subject to criteria in the next paragraph, until a Beacon frame with the current BSSID is received. If the STA is contained within an AP, it shall remain in the Awake state and always respond to probe requests, subject to criteria in the next paragraph. There may be more than one STA in an IBSS that responds to any given probe request, particularly in cases where more than one STA transmitted a Beacon or DMG Beacon(11ad)(Ed) frame following the most recent TBTT, either due to not receiving successfully a previous Beacon or DMG Beacon(11ad)(Ed) frame or due to collisions between beacon transmissions. | A result of the procedures defined in this subclause is that in each non-DMG(11ad)(Ed) infrastructure BSS, and in each IBSS there is at least one STA that is awake at any given time to receive and respond to probe requests. In an MBSS, STAs might not be awake at any given time to respond to probe requests. In an infrastructure BSS or in an IBSS, a STA that sent a Beacon frame shall remain in the Awake state and shall respond to probe requests, subject to criteria in the next paragraph, until a Beacon frame with the current BSSID is received. If the STA is contained within an AP, it shall remain in the Awake state and always respond to probe requests, subject to criteria in the next paragraph. There may be more than one STA in an IBSS that responds to any given probe request, particularly in cases where more than one STA transmitted a Beacon or DMG Beacon(11ad)(Ed) frame following the most recent TBTT, either due to not receiving successfully a previous Beacon or DMG Beacon(11ad)(Ed) frame or due to collisions between beacon transmissions. |

# Comments

Could merge as a. The STA is an AP, an IBSS STA, a mesh STA or a PCP

I agree,  we could.  Not sure it adds to clarity.

Wouldn’t “that supports” be better or do we really want to say that the STA is right now running an active scan.  As Mark said, “performing” seems not to be the right word here.

If we said “that supports”, the reference to 1..1.4.3.2 would be right again as we would said “support .. active scan .. according to the algorithms defined in xxx”

So a scanning DMG STA which is not in a BSS, or is the STA of a PCP, is required to respond (subject to Address and SSID etc. matches) while it is scanning?  That doesn’t seem right

Clause 10.1.4.3.2 provides the algorithm for scanning STA. There is no rules how to send the probe response.

Also it is not clear when the STA is preforming active scanning. The start and times or criteria should be clearly defined.

This is superfluous since APs match anyway

The words last received may not be needed here. The received probe request is already defined.

Is this the one just received?  Or was this referring to a Probe Request previously transmitted by the STA which is now receiving a Probe Request?

Unless an 11ad expert says otherwise, I’m going to suggest “and the Probe Request frame includes” was intended (see KJ4)

I agree with the intent.  But because I don’t understand this criterion,   need to defer to .11ad folks.

This seems really odd.

Assume for whatever reason that a multi-band capable STA receives one probe request, which includes a Multi-band element, and shortly afterwards a second probe request without a Multi-band element.  The last probre request prohibits the STA to send a probe response (last request was w/o a Multi-band element) but the STA might already have scheduled a probe response due to the formerly received probe request.  Is the STA now supposed to take this schedled reqsponse out of its transmission queue?  We had some similar discussions in TGai and a number of people said that such requirement would not be feasible to implement.  Maybe the issue can be solved by replacing "last received probe request" with "formerly received or previously received probe request".

Worth talking though.   IMHO a response should be only dependent on the probe request we are responding to.   I know that TGai might well change that,  but that’s as I understand it the rules currently are.

I think this is correct,  but it is an extrapolation from existing rules.

This added for symmetry with previous item.

Disagree Mark’s changes here.   “In an IBSS” is used more commonly than “IBSS STA”.

This criterion added to resolve Mark’s comment.

New condition to resolve Mark’s comment.

Resolve’s Mark’s comment.  This was the only place I found to configure a “STA’s HESSID”.

But the MIB variable says “used by an AP”, implying it’s not used by a non-AP STA

It’s a good point.  Strike the MIB variable.  Long live the SAP.

Previously was limited to non-DMG,  but there is nothing that permits a DMG AP to sleep,  only a DMG PCP.

I would move this sentence above / higher in the text.  This sentence is a critera for responding to a probe request while the current paragraph talks about sending (what to include in) probe responsens.

I think I disagree with this and have taken no action.

Inserted throughout this para.

Was “current BSSID”

As commented above, there is nothing that permits a DMG AP to sleep,  so the comment was misleading, althrough correct.

This is also true in an DMG infrastructure BSS.  There is nothing that allows a DMG AP to power-save.

This sentence has the same meaning as the sentence 5 lines above.

Perhaps,  but this entry follows a pattern of notes describing each type of BSS.

Inserted.

11ai envisages broadcast probe responses, no?

Perhaps.  That is their problem,  provided we haven’t done anything to make their life significantly harder.

I think we can avoid having to answer Mark’s question by deleting this sentence.   The point is that the standard shouldn’t describe how a device responds to “not ordered properly” requests.   It is up to a device to choose what to do. 
Note this is very different from handling future extension,  and if the purpose of this statement was to allow extension,  then it should say so,  ratehr than talk about improper things.

... but not if they’re part of the normal probe response body...

... which is Element ID value order.  But I’m trying to find the bit of the spec which clarifies whether if you’re asked for something which is already present anyway, you get it twice or not – didn’t this get addressed in REVma or REVmb?

I can’t remember it.  But it makes no sense to either request or provide duplicate info.

Why does this particular element need to be called out?

Additional semantics.   Or TGk thought it was a Really Important element.

Make a new subclause for the Criteria when to send a probe response

I would order them AP, IBSS, MBSS, DMG, PCP, MB since that’s the historical order

So a scanning DMG STA which is not in a BSS, or is the STA of a PCP, is required to respond (subject to Address and SSID etc. matches) while it is scanning?  That doesn’t seem right

Clause 10.1.4.3.2 provides the algorithm for scanning STA. There is no rules how to send the probe response.

Also it is not clear when the STA is preforming active scanning. The start and times or criteria should be clearly defined.

The words last received may not be needed here. The received probe request is already defined.

Is this the one just received?  Or was this referring to a Probe Request previously transmitted by the STA which is now receiving a Probe Request?

This seems really odd.

How about a PCP or a non-PCP in a PBSS?  And broadcast RA is OK for MBSS?

How about non-PCP in PBSS and MBSS?

I think this is correct,  but it is an extrapolation from existing rules.

What if there’s no Mesh ID in the PR?

What’s this?  Suggest deletion

STAs don’t have Mesh IDs.  Suggest change to “MBSS”

STAs don’t have SSIDs.  Suggest change to “BSS”

STAs don’t have BSSIDs.  Suggest change to “BSS”

STAs don’t have an HESSID.  Suggest change to “homogeneous ESS”

Terminating the STA seems a bit extreme, anyway

What’s this?  Suggest change to “a given requested element”

Should(n’t) this be a NOTE?

“and in a non-IBSS DMG BSS” (see other comments)?

This is confusing, since in an infraBSS only the AP sends Beacons.  Suggest deleting this and making next bullet start “In an infrastructure BSS, the AP shall [...]”

Missing “or DMG Beacon”

Missing “or DMG Beacon”

What’s this?  Suggest change to “BSSID of the IBSS”

This appears to contradict the first bullet, which appears to allow a DMG infrastructure AP to fall asleep (this is Wi-Fi Direct in disguise, right?)

And how about a PBSS?  Is the PCP required to be there to respond?

Suggest moving this to be part of the IBSS bullet, once that no longer mentions infraBSSes too

New sublause to describe what to do / to include in a probe response request when the critera above say a response should be sent

What’s this?  Suggest change to “a given requested element”

This seem logically correct but I feel this sentence is gramateically hard to understand.  I need a native English speaker to help me out here

This seems really odd.

This is untirely unncessary because it is alrady covered in the non-mesh-specific case.

# Text boxes

Abstract

This document contains some proposed resolutions to comments from LB199.

R0:  Pulled from document 11-13/1314R12 as per TGm telecon action for circulation and consideration.

R1: some consistency checking added.   Removed the non-AP instructure case,  as I can’t find any examples in the text of describing this.

R2: some issue with download of R1

R3: updated during TGmc meeting

R4: Partly re-written by Mark,  Updated by Jarkko. Restructured by Marc Emmelmann