## Slide 1: Integrated System Level Simulation
Date: 2014-01
Authors:
Name | Affiliations | Address | Phone | Email
Luo Jun | Huawei Technologies Co., Ltd. | No. 2222, Xin Jinqiao Rd. Pudong, Shanghai, China |  | jun.l@huawei.com
Zhang Jiayin |  | No. 2222, Xin Jinqiao Rd. Pudong, Shanghai, China |  | zhangjiayin@huawei.com
Ma Chixiang |  | No. 2222, Xin Jinqiao Rd. Pudong, Shanghai, China |  | machixiang@huawei.com
Edward Au |  | Kanata, ON |  | edward.au@huawei.com
Kong Xueli |  | F1-17, Bantian Huawei Base, Shenzhen, China |  | kongxueli@huawei.com
Peter Loc |  |  |  | 
Yakun Sun | Marvell Semiconductor | 5488 Marvell Ln, Santa clara, CA 95054 |  | 
Hongyuan Zhang |  |  |  | 

## Slide 2: Abstract
An integrated system level simulation that takes into consideration PHY and MAC features is recommended for HEW system performance evaluation of real-world usage scenarios.

## Slide 3: Background
Three types of simulation methodologies are presented in [1]:
  PER simulation
    Evaluate PHY link level performance (point to point)
  PHY System simulation
    Evaluate multi-BSS performance
    Accurate modeling of PHY, e.g., channel model, MIMO configuration, SU OL/BF, MU.
    Simplified MAC, e.g., random AP/STA transmission, CCA
  MAC System simulation
    Evaluate multi-BSS performance
    Accurate modeling of MAC, e.g., CSMA/CA, aggregation policy, usage of RTS/CTS/CTS-to-self, configuration of EDCA parameters, use of beacon and management frames.
    Simplified PHY, e.g., SISO over AWGN

## Slide 4: Limitations of Standalone PHY and MAC System Simulations
While we understand there are benefits of standalone PHY and MAC system simulations, e.g.,
  Speed up simulator development by simplifying some of the MAC and PHY details,
PHY System simulation
  Fails to automatically provide accurate real-world performance based on accurate MAC access
  Cannot provide any insight on the impact of dynamic MAC overhead
  Cannot show tradeoff between PHY rate enhancement and MAC efficiency
MAC System simulation
  Lacks the capability of showing the impact of fluctuating wireless channels
  Cannot show the impact of PHY techniques on MAC, e.g. Beamforming, MU-MIMO, …

## Slide 5: Requirement
Recall one main objective of HEW is to consider realistic performance evaluation [2].
Obtaining strong insights on PHY/MAC interworking
  Some techniques may require both accurate PHY and MAC details, e.g. BF/MU-MIMO, …
  Some performance gain may be expected from the joint effects of both PHY and MAC
  Important to understand performance tradeoff, e.g. some PHY rate enhancements may sacrifice MAC efficiency [3]

## Slide 6: Our Recommendation
We recommend developing an integrated system level simulation that would help to provide an overall system-wise (multi-BSS) real-world performance assessment.

## Slide 7: Integrated System Level Simulation
Integrated SLS incorporates PHY and MAC details in one simulator
    Accurate modeling of PHY, including channel model, MIMO configurations, SU OL/BF, MU, …
    Accurate modeling of MAC, including CSMA/CA, aggregation policy, usage of RTS/CTS/CTS-to-self , EDCA, use of beacon and management frames, …
    Accurate traffic modeling, e.g. FTP, HTTP, video, gaming, VDI …
    Accurate evaluation of multi-BSS performance

## Slide 8: Proposed Feature Set of Integrated SLS
 | Full feature list | 
 | Minimum feature list | Nice-to-have Features
MAC | CCA | Multiple channels
 | Control frame (RTS/CTS/ACK/Block ACK) | Control frame (CTS2self)
 | EDCA | Management frame
 | Aggregation (A-MPDU in 11ac) | …
 | Link Adaption | 
PHY | SU-OL, Beamforming | MU-MIMO
 | MMSE | …
 | PHY Abstraction | 
 | Energy detection | 

## Slide 9: How to do integrated SLS? (1)
    Mostly based on discrete event-driven simulation (e.g. NS2/3, OPNET, …)

## Slide 10: How to do integrated SLS? (2)
Transmission flow between simulation entities (AP/STA)

## Slide 11: How to do integrated SLS? (3)
MAC modeling
  Send packets from upper layer to PHY
  Receive packets from PHY and collect statistics, or notify upper layer(optional)
  Perform detailed MAC design, including EDCA, CCA, Aggregation, Control frame(RTS/CTS/ACK), …

## Slide 12: How to do integrated SLS? (4)
PHY modeling
  Send packets from MAC to channel
  Receive packets from channel and notify MAC
  Perform detailed PHY design, including SINR calculation, PHY abstraction, Energy detection, …

## Slide 13: How to do integrated SLS? (5)
Event-driven based procedures of integrated SLS
Event List
traffic_event | Create | Create traffic according to different traffic models
 | Process | MAC procedure (CCA, EDCA, Aggregation, RTS/CTS, ...)
transmission_ event | Create | Create a event when channel access is successful, and wait PHY process
 | Process | PHY procedure (receiver algorithms, SU OL, SU BF, MU, ED, SINR, PHY abstraction, ...)
trans_complete_event | Create | Create an event when a packet transmission is completed after PHY process, and wait for sending ACK in MAC
 | Process | Send ACK and collect statistics

## Slide 14: Comparison of Standalone & Integrated System Simulation
 | PHY SLS | MAC SLS | Integrated SLS
Automatically provide accurate real-world performance | weak | medium | good
Support PHY/MAC interworking | weak | medium | good
Modeling/Evaluation Capabilities | PHY only techniques | MAC only techniques | Both PHY and MAC techniques
Insight on source of gain (PHY or MAC) | good | good | medium
Simulation run time | good | medium | weak

## Slide 15: Summary
An integrated system level simulation to incorporate PHY and MAC is recommended for real-world performance evaluation.

## Slide 16: Reference
[1] 11-13-1051-01-0hew-evaluation-methodology
[2] 11-13-1410-01-0hew-802-11-hew-draft-par-and-5c
[3] 11-07-2431-00-0vht-analysis-on-ieee-802-11n-mac-efficiency