## Slide 1: Removing FILS IP Address Configuration
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | Allied Telesis R&D Center | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Date: 2014-01-19
Authors:

## Slide 2: Abstract
This document describes the reason why I intend to remove the FILS IP Address Configuration.
The related CIDs are 2090, 2164 and 3178.

## Slide 3: CID2090
Comment
  “The choice is determined by the STA based on what IP Address assignment methods are supported by the AP.” This smacks of multiple options for political rather than technical reasons. If there is genuinely no good technical reason, expect the market to be confused and support neither of them.
Proposed Change
  Either justify why there are two optional methods, or make one of them mandatory.

## Slide 4: CID2164
Comment
  I really question the wisdom of doing L3 work at L2. L3 will evolve ... IPv9, IPv99. By adding these fixed fields in billions of deployed products in the wrong layer we make it VASTLY harder to upgrade the network. We run the risk of forcing the network to ossify. Related, the video I have seen for poor discovery performance without FILS (~10sec) must have used the worst DHCP server in the world since IMHO most users in most environments have a completely different & better experience; so I am not yet convinced of the technical need for this layer violation. (OK, Proxy ARP has already gone here ...)
Proposed Change
  Remove the encapsulated IPv4/v6 address assignment at L2 (just rely on encapsulated HLPs, or - require that ALL FILS STAs shall support the HLP encap mechanism so that IPv9 or v99 (and other-than-IP address assignment) can be supported without ANY future change to L2 devices built in 2014/15. Else, as a minimum, a) provide a survey of high density networks using properly desinged DHCP servers and show that this is a genuine problem needing an IEEE solution, and b) review this layer violation with ARCH and 802.1.

## Slide 5: CID3178
Comment
  "using FILS IP address assignment method" No reference to this method is provided. Assuming the intended reference is to subclause 10.44.4.2 (IP address assignment using FILS IP Address Configuration), then I have the following additional comment: as an IP address assignment protocol definition, this procedure is unnecessary and inadequate. Unnecessary because it does not differentiate itself in any way from widely implemented protocols that achieve the same purpose (DHCP and IPv6 autoaddress configuration). Inadequate because it does not address failure cases, address revocation, exchange timeouts, address renewal, conflict resolution, mobility within an ESS, etc.
Proposed Change
  Remove subclauses 8.4.2.186.2, 8.4.2.186.3 and 10.44.4.2

## Slide 6: Discussion Summary
I discussed with George Cherian about the benefits of FILS IP Address Configuration.
Main topics
  Performance
  DAD for IPv6
  Implementation Complexity

## Slide 7: FILS IP Address Configuration
FILS specific IP address configuration mechanism.
No IP address continuity between APs.
  Each AP has its own IP address pool.
  Existing WLAN network has IP address continuity in a ESS.
The IP address of the non-AP STA is assigned by the AP, not by the DHCP server.
The request and response are carried by Association/Reassociation frames.
The information carried by the mechanism is
  IP address and netmask of non-AP STA
  IP address and MAC address of the gateway
  IP address (and MAC address if it’s in the same network) of the DNS server

## Slide 8: Performance
FILS IP Address Configuration
  Configuration can be done in 1-roundtrip between STA and AP.
  IP address assignment is fast because the IP address assignment function is in the AP.
DHCP in HLP encapsulation
  Configuration can be done in 1-roundtrip between STA and AP with RCO.
  IP address assignment can be fast with the DHCP server located in the AP.

## Slide 9: Configuration Parameters
FILS IP Address Configuration
  IP address and netmask of the STA
  IP address and MAC address of the gateway
  IP address (and MAC address if it’s in the same network) of the DNS server
DHCP in HLP encapsulation
  IP address and netmask of the STA
  IP address of the gateway
  IP address of the DNS servers
  And any DHCP options
Gratuitous ARP in HLP encapsulation
  MAC address of the gateway
  MAC address of any node in the same network, not limited to DNS servers.

## Slide 10: Sequence
STA
AP
Association Request
FILS IP Address Request
Association Response
FILS IP Address Rsponse
FILS IP Address Configuration
STA
AP
Association Request
DHCPDISCOVER w/RCO
Association Response
DHCPACK w/RCO
Gratuitous ARP
HLP encapsulation

## Slide 11: IPv6
IPv6 specification has autoconfiguration mechanisms.
We should use these mechanisms, because
  Both ai and non-ai devices (including wired devices) are attached to the same network.
  Non-ai devices use IPv6 autoconfiguration including DAD.
  How to avoid conflict?
  IPv6 specification is still improving.
  How can we guarantee that ai specification never confilict with IPv6 specification in the future?
HLP encapsulation can carry any higher layer packets, such as RA and DHCPv6.

## Slide 12: Implementation
FILS IP Address Configuration
  New IP address configuration function must be implemented from scratch for both server and client.
HLP encapsulation
  Modify existing DHCP client.
    DHCP server modification will not be required if RCO is already implemented or RCO is not used.
  Or, new ai-optimized DHCP client and server can be implemented from scratch as same as FILS IP Address Configuration if you want.
    I think it’s not good way.

## Slide 13: Operation (single AP)
AP
FILS
DHCP
Pool
Pool
ai
STA
non-ai
STA
AP
DHCP
Pool
ai
STA
non-ai
STA
FILS IP Address Configuration
HLP encapsulation

## Slide 14: Existing Typical WLAN Network
Consider to replace the APs to ai-capable APs.
AP
AP
AP
AP
AP
AP
DHCP
Server

## Slide 15: Replacing with HLP encapsulation AP
Just replace.
Mixture of ai APs and non-ai APs is not a matter.
ai AP
non-ai
AP
DHCP
Server
ai AP
non-ai
AP
non-ai
AP
non-ai
AP

## Slide 16: Replacing with FILS IP Address Configuration AP
non-ai
AP
DHCP
Server
ai AP
Pool
non-ai
AP
non-ai
AP
non-ai
AP
non-ai
AP
DHCP server must remain to support
non-ai AP
non-ai STA
IP address pool may be modified.
Assign new IP address pool.
DHCP
Server
ai AP
Pool
DHCP server must remain to support
non-ai STA
ai AP
Pool
ai AP
Pool
ai AP
Pool
ai AP
Pool
ai AP
Pool
Manage the IP address pools of all APs and DHCP server.
If the operator assumes 100 STAs connect to the network, the operator should assign at least 100 IP addresses to each IP address pool.

## Slide 17: Conclusion
I could not find any technical benefits of FILS IP Address Configuration.
I propose to remove FILS IP Address Configuration from the draft.
  Remove “FILSIPAddressRequestData”, “FILSIPAddressAssignmentData” and “FILSDNSInformationData” in clause 6.3 (MLME SAP Interface).
  Remove “IP Address Assignment Method” in clause 8.4.2.185 (FILS Indication eleent)
  Remove clause 8.4.2.186.2 (FILS IP Address Request TLV), 8.4.2.186.3 (FILS IP Address Assignment TLV) and 8.4.2.186.4 (FILS DNS Information TLV)
  Modify clause 10.44.3 (Higher layer setup during association/reassociation procedure)
  Merge clause 10.44.3.1 (Higher layer setup using higher layer packet encapsulation) to clause 10.44.3.
  Remove clause 10.44.3.2 (IP address assignment using FILS IP Address Configuration)
  (Clause numbers are based on D1.2)

## Slide 18: Questions & Comments

## Slide 19: Straw poll
Do you support to remove FILS IP Address Configuration from the draft?
Result (Y/N/Don’t care):