## Slide 1: Removing FILS IP Address Configuration
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | Allied Telesis R&D Center | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Date: 2014-05-12
Authors:

## Slide 2: Abstract
This document describes the reason why I intend to remove the FILS IP Address Configuration.
The related CIDs are 4502 and 4429.

## Slide 3: CID4502
Comment
  FILS IP Address Configuration is not required. Because the HLP encapsulation can perform all functions supported by the FILS IP Address Configuration. The duplication will make confusion.
Proposed Change
  Remove clause 10.44.3.2, 8.4.2.181 and 8.6.24. And modify rerated part in other clauses.

## Slide 4: FILS IP Address Configuration
FILS specific IP address configuration mechanism.
No IP address continuity between APs.
  Each AP has its own IP address pool.
  Existing WLAN network has IP address continuity in a ESS.
The IP address of the non-AP STA is assigned by the AP, not by the DHCP server.
The request and response are carried by Association/Reassociation frames.
The information carried by the mechanism is
  IP address and netmask of non-AP STA
  IP address and MAC address of the gateway
  IP address (and MAC address if it’s in the same network) of the DNS server

## Slide 5: Benefit of FILS IP Address Configuration
FILS IP Address Configuration is used to reduce the overhead caused by using the DHCP for the IP address assignment.

## Slide 6: CID4429
Comment
  what overhead is reduced? It looks just a personal opinion and meaningless.
Proposed Change
  Remove the sentence "FILS IP Address Configuration is used to recude the overhead caused by using the DHCP for tha IP address assignment."

## Slide 7: Performance
FILS IP Address Configuration
  Configuration can be done in 1-roundtrip between STA and AP.
  IP address assignment is fast because the IP address assignment function is in the AP.
DHCP in HLP encapsulation
  Configuration can be done in 1-roundtrip between STA and AP with RCO.
  IP address assignment can be fast (equivalent to FILS IP Address Configuration) with the DHCP server located in the AP.

## Slide 8: Configuration Parameters
FILS IP Address Configuration
  IP address and netmask of the STA
  IP address and MAC address of the gateway
  IP address (and MAC address if it’s in the same network) of the DNS server
DHCP in HLP encapsulation
  IP address and netmask of the STA
  IP address of the gateway
  IP address of the DNS servers
  And any other DHCP options
Gratuitous ARP in HLP encapsulation
  MAC address of the gateway
  MAC address of any node in the same network, not limited to DNS servers.

## Slide 9: Sequence
STA
AP
Association Request
FILS IP Address Request
Association Response
FILS IP Address Rsponse
FILS IP Address Configuration
STA
AP
Association Request
DHCPDISCOVER w/RCO
Association Response
DHCPACK w/RCO
Gratuitous ARP
HLP encapsulation

## Slide 10: Operation (single AP)
AP
FILS
DHCP
Pool
Pool
ai
STA
non-ai
STA
AP
DHCP
Pool
ai
STA
non-ai
STA
FILS IP Address Configuration
HLP encapsulation

## Slide 11: Existing Typical WLAN Network
Consider to replace the APs to ai-capable APs.
AP
AP
AP
AP
AP
AP
DHCP
Server

## Slide 12: Replacing with HLP encapsulation AP
Just replace.
Mixture of ai APs and non-ai APs is not a matter.
ai AP
non-ai
AP
DHCP
Server
ai AP
non-ai
AP
non-ai
AP
non-ai
AP

## Slide 13: Replacing with FILS IP Address Configuration AP
non-ai
AP
DHCP
Server
ai AP
Pool
non-ai
AP
non-ai
AP
non-ai
AP
non-ai
AP
DHCP server must remain to support
non-ai AP
non-ai STA
IP address pool may be modified.
Assign new IP address pool.
DHCP
Server
ai AP
Pool
DHCP server must remain to support
non-ai STA
ai AP
Pool
ai AP
Pool
ai AP
Pool
ai AP
Pool
ai AP
Pool
Manage the IP address pools of all APs and DHCP server.
If the operator assumes 100 STAs connect to the network, the operator should assign at least 100 IP addresses to each IP address pool.

## Slide 14: Conclusion
I could not find any technical benefits of FILS IP Address Configuration.
I propose to remove FILS IP Address Configuration from the draft.
  Remove clause 10.44.3.2, 8.4.2.181 and 8.6.24. And modify related part in other clauses

## Slide 15: Questions & Comments

## Slide 16: Motion
Move to remove FILS IP Address Configuration from TGai draft.
Moved:
Seconded:
Result (Y/N/A):

## Slide 17: IPv6
IPv6 specification has autoconfiguration mechanisms.
We should use these mechanisms, because
  Both ai and non-ai devices (including wired devices) are attached to the same network.
  Non-ai devices use IPv6 autoconfiguration including DAD.
  How to avoid conflict?
  IPv6 specification is still improving.
  How can we guarantee that ai specification never confilict with IPv6 specification in the future?
HLP encapsulation can carry any higher layer packets, such as RA and DHCPv6.

## Slide 18: Implementation
FILS IP Address Configuration
  New IP address configuration function must be implemented from scratch for both server and client.
HLP encapsulation
  Modify existing DHCP client.
    DHCP server modification will not be required if RCO is already implemented or RCO is not used.
  Or, new ai-optimized DHCP client and server can be implemented from scratch as same as FILS IP Address Configuration if you want.
    I think it’s not good way.