## Slide 1: High Efficiency WLAN Overview
Date: 2014-02-06
Authors:

## Slide 2: Introduction and problem statement
The vast majority of deployments will evolve towards high density scenarios in the near future
  usage models in such scenarios are likely to suffer bottlenecks in the coming years, with inefficiencies in transforming the multi-Gbps peak capacity into real throughput experienced by users
HEW aims to achieve a very substantial increase in the real-world throughput achieved by users in such scenarios, with improved power efficiency for battery powered devices
  Creating an instantly recognizable improvement in User Experience of the major use cases
IEEE 802.11 HEW SG is proposing a PAR for a TG to create an amendment to 802.11 for operations in frequency bands between 1 GHz and 6 GHz
  focused primarily on 2.4 GHz and the 5 GHz frequency bands
Expected MAC and PHY modifications in focused directions:
  (1) To improve efficiency in the use of spectrum resources in dense networks with large no. of STAs and large no. of APs
  (2) To improve efficiency and robustness in outdoor deployments
  (3) To improve power efficiency

## Slide 3: Market Drivers
  Various market segments require enhancement of average throughput and user experience in dense deployment scenarios
Operators desire cellular offload to lighten traffic explosion
Annual global IP traffic will pass the Zetabyte threshold by end of 20161).
PC/Mobile/CE vendors desire higher user experience
100% Wi-Fi attach-rate for smart phones, which requires improved power-efficiency
Video traffic will be 55% of all consumer Internet traffic by 20161), which demands improved satisfaction of latency, jitter, and packet loss requirements of delay sensitive applications
Attach-rate for smart pad/TV/appliances is substantially increasing
Automotive is increasingly using Wi-Fi for in-car entertainment
Chip/AP vendors desire successive Wi-Fi market evolution after 11ac
Operator
Manufacturer
Chip/AP vendor
1) Source: Cisco VNI Global Forecast, 2011-2016
Need a standard to enhance average throughput and user experience in real world
Notes: doc.: IEEE 802.11-07/2090r0
July 2007
        Eldad Perahia (Intel)
Page 3

## Slide 4: Need for the Project
Very dense deployments
  Enterprise, residential, operator hotspots, retail and ad-hoc scenarios
  Characterized by the existence of many access points and non-AP stations in geographically limited areas
  Increased interference from neighboring devices gives rise to performance degradation
Growing use of WLAN outdoors
Better support of real-time applications with improved power efficiency
  Video traffic is expected to be the dominant type of traffic in many high efficiency WLAN deployments
  WLAN users demand improved performance in delivering their real-time applications
  Operators expect sufficient user experience to offload traffic on WLAN
Focusing on improving metrics that reflect user experience in typical conditions
  Improving the average per station throughput, the 5th percentile of per station throughput, and area throughput, etc.
  Evaluation with a set of typical deployment scenarios representative of the main expected usage models

## Slide 5: Environments
From Wi-Fi Alliance liaison report:
  Airport / Train station
  E-education
  Public transportation
  Dense apartment building
  Pico-cell street deployment
Additional environments from HEW SG submissions:
  Enterprise
    On desk and in cubicle
    Conference room
    Dense deployment
  Small Office
  Hotspot in public places (Exhibition halls, Shopping malls)
  Outdoor hotspots
    park, streets, stadium, special crowded events
    co-location with cellular base stations (small cell deployments) or user equipment (e.g. private mobile APs such as mobile routers) in dense zones
  Hospital
Environments discussed in the study group include:

## Slide 6: New and Enhanced Applications:
Cellular Offloading
Cloud Computing - including VDI (Virtual Desktop Infrastructure)
Display Sharing - 1-to-1 (Phone - TV), 1-to-many (classroom), Many-to-1 (security)
Interactive Multimedia & Gaming
Progressive Streaming
Real-time Video Analytics & Augmented Reality
Support of wearable devices
Unified Communications - Including Video conferencing
User Generated Content (UGC) Upload & Sharing
Video conferencing/tele-presence
Video distribution at home – new video resolution (VHD, UHD)
Wireless docking

## Slide 7: HEW Differentiating Features
 | Previous 802.11 Amendments | HEW Amendments being considered
Objectives | Increase the per-link peak throughput | Increase the average per STA throughput in dense environments
Scenarios | Single application for a single client in indoor situations | Dense deployment environments with a mix of clients/APs and traffic types including outdoor situations
KPIs/ Metrics | Peak rate driven - Link throughput, - Aggregate throughput | User Experience Driven Average per station throughput, 5th %ile per station throughput, Area throughput Power efficiency
February 2014

## Slide 8: Technologies
HEW will consider MAC and PHY technologies that improve WLAN efficiency in focused directions:
  Make more efficient use of spectrum resources in scenarios with a high density of STAs per BSS.
  Significantly increase spectral frequency reuse and manage interference between neighboring overlapping BSS (OBSS) in scenarios with a high density of both STAs and BSSs.
  Increase robustness in outdoor propagation environments and uplink transmissions.
  Maintain or improve the power efficiency per station
The next few slides show some examples
  These example slides do not represent technologies agreed for inclusion in the standard

## Slide 9
Possible Technologies (1 of 3)
Freq.
802.11a
802.11n
(40 MHz)
802.11ac
(80 MHz)
802.11ac
(160 MHz)
Freq.
802.11a
802.11n
(40 MHz)
802.11ac
(80 MHz)
OFDMA
Capable
STA
OFDMA
Capable
STA
OFDMA
Capable STA
OFDMA
Capable
STA,
or
802.11ac
STA
(160 MHz)
Ch.1
Ch.2
Ch.3
Ch.4
Ch.5
Ch.6
Ch.7
Ch.8
Guard Band
Guard Band
Guard Band
UL MU-MIMO
Interference
management
Dynamic Sensitivity Control (DSC)
DL MU-MIMO
(802.11ac)
Spatial domain techniques for dense reuse of spectrum:
Frequency domain techniques for a more effective channel utilization

## Slide 10: Possible Technologies (2 of 3)
Present: Either Tx or RX
Simultaneous Tx & Rx
AP
AP
Wireless devices either transmit or receive, but not both
Low Spectral Utilization!
AP
AP
~2x throughput improvements!
On the same time and frequency resource
PHY/MAC mechanisms for enabling In-Band simultaneous Tx and Rx to improve spectral efficiency

## Slide 11
Possible Technologies (3 of 3)
Technologies to mitigate the impact of management frames
  Many management frames impact the throughput of WLANs.
    Beacons, Probe Responses induced by a Probe Request.
  Those frames are usually transmitted using the lowest MCS.
An example of captured frames in Tokyo area
Chart: Categorized by frame type (Data/Control/Management)
| Data | Control | Management | Others
Packets | 36434 | 48927 | 74287 | 926
Chart: Categorized by frame format (802.11/b/g/n)
| 11/11b | 11g | 11n 20MHz | 11n 40MHz
All Packets | 118421 | 29338 | 12345 | 0
Efficient handling of management frames to minimize overhead
Reference: A. Kishida, et. al., 11-13-0818-01-0hew-Issues of Low-Rate Transmission.pptx

## Slide 12: HEW PAR Scope
Four times improvement in the average throughput per station in a dense deployment scenario
  Throughput is measured at the MAC data service access point
  Expected to provide improvements of 5 – 10x
Maintaining or improving the power efficiency per station
Indoor and outdoor operations in frequency bands between 1 GHz and 6 GHz
Enabling backward compatibility and coexistence with legacy IEEE 802.11 devices operating in the same band

## Slide 13: Related Submissions
11-13/0657r6, “HEW SG usage models and requirements - Liaison with WFA”
11-13/1443r0, “Liaison from Wi-Fi Alliance on HEW Use Cases”
11-13/1001r6, “Simulation Scenarios Document Template”
11-13/1000r2, “Simulation Scenarios”
11-13/331r5, “High efficiency WLAN”
11-13/339r10, “High efficiency WLAN straw poll”
11-13/1122r1, “Considerations for In-Band Simultaneous Transmit and Receive (STR) feature in HEW”
11-14/169r0, “IEEE 802.11 HEW SG Proposed CSD”
11-14/165r0, “802.11 HEW SG Proposed PAR”