## Slide 1: High Efficiency WLAN Overview
Date: 2014-02-18
Authors:

## Slide 2: Introduction and problem statement
The vast majority of deployments will evolve towards high density scenarios in the near future
  usage models in such scenarios are likely to suffer bottlenecks in the coming years, with inefficiencies in transforming the multi-Gbps peak capacity into real throughput experienced by users
HEW aims to achieve a very substantial increase in the real-world throughput achieved by users in such scenarios, with improved power efficiency for battery powered devices
  Creating an instantly recognizable improvement in User Experience of the major use cases
IEEE 802.11 HEW SG is proposing a PAR for a TG to create an amendment to 802.11 for operations in frequency bands between 1 GHz and 6 GHz
  focused primarily on 2.4 GHz and the 5 GHz frequency bands
Expected MAC and PHY modifications in focused directions:
  (1) To improve efficiency in the use of spectrum resources in dense networks with large no. of STAs and large no. of APs
  (2) To improve efficiency and robustness in outdoor deployments
  (3) To improve power efficiency

## Slide 3: Market Drivers
  Various market segments require enhancement of average throughput and user experience in dense deployment scenarios
Operators desire cellular offload to lighten traffic explosion
Annual global IP traffic will pass the Zetabyte threshold by end of 20161).
PC/Mobile/CE vendors desire higher user experience
100% Wi-Fi attach-rate for smart phones, which requires improved power-efficiency
Video traffic will be 55% of all consumer Internet traffic by 20161), which demands improved satisfaction of latency, jitter, and packet loss requirements of delay sensitive applications
Attach-rate for smart pad/TV/appliances is substantially increasing
Automotive is increasingly using Wi-Fi for in-car entertainment
Chip/AP vendors desire successive Wi-Fi market evolution after 11ac
Operator
Manufacturer
Chip/AP vendor
1) Source: Cisco VNI Global Forecast, 2011-2016
Need a standard to enhance average throughput and user experience in real world
Notes: doc.: IEEE 802.11-07/2090r0
July 2007
        Eldad Perahia (Intel)
Page 3

## Slide 4: Need for the Project
Very dense deployments
  Enterprise, residential, operator hotspots, retail and ad-hoc scenarios
  Characterized by the existence of many access points and non-AP stations in geographically limited areas
  Increased interference from neighboring devices gives rise to performance degradation
Growing use of WLAN outdoors
Better support of real-time applications with improved power efficiency
  Video traffic is expected to be the dominant type of traffic in many high efficiency WLAN deployments
  WLAN users demand improved performance in delivering their real-time applications
  Operators expect sufficient user experience to offload traffic on WLAN
Focusing on improving metrics that reflect user experience in typical conditions
  Improving the average per station throughput, the 5th percentile of per station throughput, and area throughput, etc.
  Evaluation with a set of typical deployment scenarios representative of the main expected usage models

## Slide 5: Environments
Environments discussed in the study group include:
Airport/Train Station*
Public Transportation*
Enterprise
Small Office
e-Education*
Hospitals
Dense Apartment Buildings*
Pico-cell Street Deployments*
Hotspot in Public Places
Outdoor Hotspots
* Environments prioritized in the Wi-Fi Alliance Liaison response report
Represents outdoor deployments

## Slide 6: New and Enhanced Applications:
Cellular Offloading
Cloud Computing - including VDI (Virtual Desktop Infrastructure)
Display Sharing - 1-to-1 (Phone - TV), 1-to-many (classroom), Many-to-1 (security)
Interactive Multimedia & Gaming
Progressive Streaming
Real-time Video Analytics & Augmented Reality
Support of wearable devices
Unified Communications - Including Video conferencing
User Generated Content (UGC) Upload & Sharing
Video conferencing/tele-presence
Video distribution at home – new video resolution (VHD, UHD)
Wireless docking

## Slide 7: HEW Differentiating Features
 | Previous 802.11 Amendments | HEW Amendments being considered
Objectives | Increase the per-link peak throughput | Increase the average per STA throughput in dense environments
Scenarios | Single application for a single client in indoor situations | Dense deployment environments with a mix of clients/APs and traffic types including outdoor situations
KPIs/ Metrics | Peak rate driven - Link throughput, - Aggregate throughput | User Experience Driven Average per station throughput, 5th %ile per station throughput, Area throughput Power efficiency
February 2014

## Slide 8: Technologies (1 of 2)
HEW will consider MAC and PHY technologies that significantly improve WLAN efficiency and robustness:
  Make more efficient use of spectrum resources in scenarios with a high density of STAs per BSS.
  Significantly increase spectral frequency reuse and manage interference between neighboring overlapping BSS (OBSS) in scenarios with a high density of both STAs and BSSs.
  Increase robustness in outdoor propagation environments and uplink transmissions.
  Maintain or improve the power efficiency per station
The next slides lists technology discussions
  The list does not represent technologies agreed for inclusion in the standard
  Technologies, not listed on the next slide, could also be considered for inclusion in the standard.

## Slide 9: Technologies (2 of 2)
Technologies discussed in the study group include:
Edge Throughput Enhancement
MAC Enhancements
MIMO/Beamforming
Multiplexing Schemes
Simultaneous Transmit and Receive
Overlapping BSS Handling
HARQ
Larger CP
Basic Access Mechanism enhancements
Dynamic Sensitivity Control
Traffic Prioritization, QoE
Multicast transmissions
Massive MIMO, MIMO Precoding
DL/UL MU-MIMO
Beamforming for OBSS
Beamforming for Interference Handling
OFDMA, SDMA, OFDM-IDMA, FFR
TD-uCSMA
Channel Bonding
Interference management, Antenna pattern nulling
Efficient resource utilization
Control frame transmission reduction
MAC/PHY mechanisms for enabling In-Band STR
Enhancements for enabling out-Band STR

## Slide 10: HEW PAR Scope
Four times improvement in the average throughput per station in a dense deployment scenario
  Throughput is measured at the MAC data service access point
  Expected to provide improvements of 5 – 10x
Maintaining or improving the power efficiency per station
Indoor and outdoor operations in frequency bands between 1 GHz and 6 GHz
Enabling backward compatibility and coexistence with legacy IEEE 802.11 devices operating in the same band

## Slide 11: PAR/CSD Related Submissions
11-13/0657r6, “HEW SG usage models and requirements - Liaison with WFA”
11-13/1443r0, “Liaison from Wi-Fi Alliance on HEW Use Cases”
11-13/1001r6, “Simulation Scenarios Document Template”
11-13/1000r2, “Simulation Scenarios”
11-13/331r5, “High efficiency WLAN”
11-13/339r10, “High efficiency WLAN straw poll”
11-14/169r0, “IEEE 802.11 HEW SG Proposed CSD”
11-14/165r0, “802.11 HEW SG Proposed PAR”

## Slide 12: Technology Related Submissions
11-13/1105r0 Discussion on Access Mechanism for HEW
11-13/1122r1 Considerations for In-Band Simultaneous Transmit and Receive (STR) feature in HEW
11-13/1126r0 Beamforming under OBSS Interference
11-13/1154r0 DL-MU-MIMO Transmission with Unequal Bandwidth
11-13/1155r0 Space Division Multiplex for OBSS Interference Suppression
11-13/1156r0 TXOP Redundancy NAV Clear
11-13/1157r3 Feasibility of Coordination Transmission for HEW
11-13/1169r0 WLAN Cellular Offload in High Speed Moving Environment
11-13/1290r0 Dynamic Sensitivity Control for HEW SG
11-13/1349r0 Access Control Enhancement
11-13/1377r0 DL efficiency enhancement in high density network
11-13/1382r0 Discussion on OFDMA in HEW
11-13/1386r2 Improving WLAN Efficiency and QoE – A Top Down Approach
11-13/1388r0 UL MU-MIMO transmission
11-13/1395r2 Simultaneous Tx Technologies for HEW
11-13/1421r1 STR Radios and STR Media Access
11-13/1440r0 Argos | Practical Masive-MIMO
11-14/0095r0 OFDM-IDMA Uplink Communication
11-13/0558r1 Coexistence and Optimization of WLAN: Time, Frequency, Space, Power, and Load
11-13/0712r1 A Brief Time of History
11-13/0758r0 Possible Approaches for HEW
11-13/0764r1 Full-duplex Technology for HEW
11-13/0765r2 CCFD for 802.11 WLAN
11-13/0768r0 TD-uCSMA
11-13/0801r1 Issues of Low Rate Transmissions
11-13/0843r0 Further Evaluation on outdoor Wi-Fi
11-13/0849r1 New Techniques: Enabling Real World Improvement By Exposing Internal MAC state
11-13/0852r0 Potential approach to improve WLAN BSS edge performance
11-13/0871r0 Discussion on Potential Techniques for HEW
11-13/0877r0 HEW Beamforming Enhancements
11-13/0878r0 Efficiency enht for dense WLAN env
11-13/1046r2 Discussion for Massive MIMO for HEW
11-13/1056r1 Enhancement on resource utilization in OBSS environment
11-13/1058r0 Efficient wider bandwidth operation
11-13/1061r0 Multicast Transmission for HEW
11-13/1073r1 Access Control Enhancement
11-13/1077r1 EDCA Enhancements for HEW
11-13/1089r1 D2D Technology for HEW
11-13/1090r2 Non-linear pre-coding MIMO Scheme for next generation WLAN