## Slide 1: Scanning Optimization By Using Reduced Neighbor Report IE
Date: 2014-03-03
Authors:

## Slide 2: Abstract
This submission proposes a scanning optimization using “Reduced Neighbor Report IE”.

## Slide 3: Recap
Reduced Neighbor Report (RNR) IE is defined for faster AP discovery.
It will be included in Beacon, Probe Response and FD frame optionally.
The primary purpose of RNR is optimizing 5GHz scanning. The current 5GHz scanning is regularly passive. It’s slower than active scanning.
This figure was the starting point of discussion for faster AP discovery.
Ref. : IEEE802.11-11/1510r0 (FOKUS)
Single Device / Box
2.4 GHz AP
5 GHz AP
Internal Mgmt. Not accessible by user
Non-AP STA 2.4 & 5 GHz operation
Active scan  receive 5GHz channel list
Optional passive scan on channel for verification
Link-Set Up

## Slide 4: Assumed behaviors
11ai supported APs may inform operating channels of neighbor APs by RNR IE included in Beacon, Probe Response and FD frames.
11ai supported STAs expect operating channels information of surrounding APs by receiving RNR IE for scanning optimization.
<Case 1>
1, 2, 3, 4, …. 10, 11  (RNR IE received)  36, 100
<Case 2>
1  (RNR IE received)  6, 11, 36, 100
Scanning sequence examples
* Numbers below are channels which STA will scan on.
5GHz
5GHz
RNR consists of 2.4GHz info also.
It may be used 2.4GHz scanning optimization.
RNR consists of operating 5GHz channels of neighbor APs.

## Slide 5: 11ai D1.1 definitions of MLME SAP interface (6.3.3.2 MLME-SCAN.request)
MLME-SCAN.request(
BSSType,
BSSID,
SSID,
ScanType,
ProbeDelay,
ChannelList,
MinChannelTime,
MaxChannelTime,
RequestInformation,
SSID List,
ChannelUsage,
AccessNetworkType,
HESSID,
MeshID,
DiscoveryMode,
FILSRequestParameters,
ReportingOption,
APConfigurationChangeCount,
VendorSpecificInfo
)
Semantics of
the service primitive
As Case 1 in Slide 4, the optimized scan can skip scanning on some channels. Default channels which should be scanned essentially will be identified in ChannelList.

## Slide 6: 11ai D1.1 definitions of MLME SAP interface (6.3.3.3 MLME-SCAN.confirm)
MLME-SCAN.confirm(
BSSDescriptionSet,
BSSDescriptionFromMeasurementPilotSet,
BSSDescriptionFromFDSet,
ResultCode,
VendorSpecificInfo
)
Semantics of
the service primitive
It can include RNR information optionally, already defined in D1.1
It may include RNR information also, not defined yet.
RNR is supposed to include in result of 2.4GHz channels scan.

## Slide 7: Issue
When RNR IE received, how can STA behave based on it?
Reduced Neighbor Report IE
What should
I do?
Neighbor AP Info #1
Neighbor AP Info #2
Neighbor AP Info #n
Length
Element ID
Header
CH Info
TBTT Info #1
TBTT Info #2
TBTT Info #n
* Simplified figure
Format of Reduced Neighbor Report IE

## Slide 8: Options
(a) Add normal passive scanning procedure on 5GHz channels specified by RNR IE
(b) Add optimized passive scanning procedure on 5GHz channels and timing specified by RNR IE
2.4GHz band
scanning procedure
RNR received
CH36
CH100
100ms
100ms
Passive scanning
Passive scanning
t
t
t
2.4GHz band
scanning procedure
RNR received
CH36
CH100
Passive scanning
Passive scanning
t
t
t
Reduced scanning duration
Option (b) is preferable. But how can the scanning timing be specified on SCAN.request?
SCAN.request
SCAN.request
Re-execution based on the received RNR

## Slide 9: Proposal
To have a mode of executing additional automatic scanning based on information of RNR IE if preferred.
Not to define STA’s behaviors when the STA receive RNR IE on 11ai standard. TGai should leave it as the matter of implementation. It will be very complicated to define contexts like scanning timing, order or channels on SCAN.request.

## Slide 10: Proposal Detail (MLME-SCAN.request)
MLME-SCAN.request(
BSSType,
BSSID,
SSID,
ScanType,
ProbeDelay,
ChannelList,
MinChannelTime,
MaxChannelTime,
RequestInformation,
SSID List,
ChannelUsage,
AccessNetworkType,
HESSID,
MeshID,
DiscoveryMode,
FILSRequestParameters,
ReportingOption,
APConfigurationChangeCount,
VendorSpecificInfo
)
Add a semantic:
ScanOption
Insert a row containing the following contents to the primitives table:
Name: ScanOption
Type: Enumeration
Valid range:
  NONE,
  FILS_OPTIMIZED_SCAN
Description:
Indicates the additional scan execution. This parameter is optionally present when dot11FILSActivated is true.

## Slide 11: Proposal Detail (MLME-SCAN.confirm)
MLME-SCAN.confirm(
BSSDescriptionSet,
BSSDescriptionFromMeasurementPilotSet,
BSSDescriptionFromFDSet,
ResultCode,
VendorSpecificInfo
)
No changes
When ScanOption is set to FILS_OPTIMIZED_SCAN, BSSDescriptionSet will include result of FILS optimized scanning automatically in addition to result of scanning on channels specified in MLME-SCAN.request.
Additional scanning behavior by ScanOption will depend on vendor’s implementation.

## Slide 12: Example Figures of Scanning Sequence
<Case 1>
<Case 2>
Aggressive sequence
t
SCAN.request
ScanChannel = 1,2,3….11
ScanOption = FILSOptScan
CH1
2
3
4
5
6
11
36
100
….
Additional
t
SCAN.request
ScanChannel = 1,2,3….11
ScanOption = FILSOptScan
CH1
6
11
36
100
RNR included
Optimized
Additional
RNR included
Intermediate Scan Result
Intermediate Scan Result
SCAN.confirm
Result Code = Success
SCAN.confirm
Result Code = Success

## Slide 13: Remaining Issues
This optimization will bring cause side effects. Some BSSIDs may become invisible because scanning on the rest channels is omitted.
  Hybrid behavior with regular scanning may be a solution. Hybrid algorithm should be on implementation.

## Slide 14: Summary
This submission proposes optimized scanning by using information of Reduced Neighbor Report IE.
Semantics of MLME-SCAN.request is proposed for that purpose.
Related descriptions in the 11ai draft (specifications) should be modified.
Hybrid Scanning algorithm should be considered to mitigate side effects of the optimized scanning in accordance with real use cases. It will be an implementation matter.