## Slide 1: Instantaneous SINR Calibration for System Simulation
Date: 2014-03-17
Authors:
Name | Affiliations | Address | Phone | email
Yakun Sun | Marvell Semiconductor | 5488 Marvell Ln, Santa Clara, CA 95054 | 1-408-222-3847 | yakunsun@marvell.com
Jinjing Jiang | Marvell Semiconductor |  |  | 
Yan Zhang | Marvell Semiconductor |  |  | 
Hongyuan Zhang | Marvell Semiconductor |  |  | 

## Slide 2: Overview
A step-by-step calibration was proposed in [1,2] with high level descriptions.
The first step of static radio statistics (long-term SINR) calibration has been presented in [3].
More companies have been worked together on the step-1 calibration [4].
We follow up on the next step of SLS calibration.
Simulation Scenario
Static Radio statistics
(S/I distribution)
PHY statistics
(Freq-domain SINR distribution)
PHY Tput calibration
MAC calibration

## Slide 3: Instantaneous SINR calibration
The objective is to align physical layer receiver characteristics in a dynamic environment.
  Dynamic physical layer receiver characteristics reflect the frequency domain SINR calculation, small-scale fading channel generation, and equalization.
Option 1: Instantaneous receiver-output SINR per tone
  Includes fading channels from both the desired transmitter and interferers
  Includes the MIMO receiver algorithms such as MMSE for MIMO cases
  Includes Doppler effects of channel generations
  Includes antenna correlation for MIMO cases
Option 2: Effective SINR per frame
  Also include all the physical layer factors as in option 1
  Essential value for later PER decision
  Less number of values to save
  Aligning effective SINR implies aligning PER/throughput (to some extent)

## Slide 4: Instantaneous SINR calibration (2)
Option 2a: alternative to option 2, use Ф(SNReff)
  Given the convergence to an upper bound (RBIR, MMIB), effective SNR is sensitive to mapping offsets (in different implementation) at high SNR region.
  Avoid the ambiguity at high SNR by using Ф(SNReff) as a bounded value,

## Slide 5: Comparison of Option 1 and 2
Option 1:
  Pro: to avoid using the same PHY abstraction method, easier to agree and implement
  Con: less strong physical meaning
Option 2:
  Pro: strong physical meaning (effective SNR per frames can be easily translated to PER, and infer throughput).
  Con:
    Need a unified PHY abstraction method (lack of consensus at this moment)
    Need to watch out the mapping offsets at high SNR (avoided by option2a)

## Slide 6: Procedure of Statistics Collection
Detailed PHY is assumed
  Fading channel models, Doppler spectrum, and antenna correlation (if MIMO) are defined by the scenarios
  Receiver algorithm is reflected (MMSE for MIMO, or MRC for single stream)
  Effective SNR per frame (mapping can be done for an agreed modulation level other than the MCS of the frame)
  PER decision is not required at this step (always successfully decoding the packet)
Some simplest MAC is assumed.
  CCA-only, basic CSMA, or EDCA with the same AC for all STAs/APs.
  Full buffer traffic
  Each AP and STA transmits a packet of a fixed (and equal) size at a fixed MCS.
Multiple drops of AP/STAs are simulated for a scenario
In each drop, collect the physical layer receiver characteristics observed at each STA/AP for each packet.
  Only collect the data frame (exclude beacons, etc.)
Generate the distribution (CDF) of dynamic physical layer receiver characteristics at STAs (downlink) and APs (uplink) over multiple drops.

## Slide 7: Simulation Setup
Simulation is based on scenario 1 to 4 in [5].
  Distribution of uplink instantaneous SINR are plotted as an example.
  We can select only one scenario for calibration.
Detailed/optional simulation assumptions:
  2.4GHz Channel with 20MHz Bandwidth
  No antenna gain, no cable loss
  1 Tx and 1 Rx are assumed (other than defined in [5])
  EDCA with AC2 for all STAs/APs (using default parameters)
  MCS 7, each packet of 1584 bytes
  STAs and APs are dropped and associated based on scenario [5]

## Slide 8: Simulation Assumptions (Scenario 1)
Parameter | Value
Number of STAs | 4 STAs per apartment
Channel Model | TGn B (AP-AP, STA-STA, AP-STA)
Penetration Loss | Wall 12dB, Floor 17dB, linear for multiple walls/floors
BW | 20MHz at 2.4GHz. Each BSS randomly selects one channel out of 3.
TX Power | AP: 23dBm, STA: 17dBm
Association | 100% STA in an apartment associated with the AP in the room.

## Slide 9: Instantaneous UL SINR Per Tone
A large portion of STAs’ frames come with high received SINR  a high probability of successful packet.
Also a long tail of low SINR

## Slide 10: Effective SINR Per Frame
RBIR is used for effective SNR mapping.
We truncate the SNR vs. RBIR mapping at 27dB for 64QAM and 30dB for 256QAM.

## Slide 11: Simulation Assumptions (Scenario 2)
Parameter | Value
Number of STAs | 4 STAs per cubicle, 4 AP per BSS
Channel Model | TGn D (AP-AP, STA-STA, AP-STA)
Penetration Loss | Wall 7dB, linear for multiple walls
BW | 20MHz at 2.4GHz. Each AP selects one channel out of 4 in a BSS. (BSS4k+1,BSS4k+2,BSS4k+3,BSS4k+4)= (ch1,ch2,ch3,ch4)
TX Power | AP: 24dBm, STA: 21dBm
Association | 100% STA in a BSS associated with an AP in the BSS by RSSI, no P2P STA
Based on [2] before the document was updated at the meeting.

## Slide 12: Instantaneous UL SINR Per Tone

## Slide 13: Effective SINR Per Frame

## Slide 14: Simulation Assumptions (Scenario 3)
Parameter | Value
Environment | BSSs in Hexagon (figure 5), simulated BSS in 1 channel (figure 6) BSS radius: R=7m
Number of STAs | 30 STAs per BSS
Channel Model | TGn D (AP-AP, AP-STA), TGn B (STA-STA)
Penetration Loss | None
BW | 20MHz at 2.4GHz. Each simulated BSS selects the same channel.
TX Power | AP: 17dBm, STA: 15dBm
Association | 100% STA associated with the strongest AP

## Slide 15: Instantaneous UL SINR Per Tone

## Slide 16: Effective SINR Per Frame

## Slide 17: Simplification of Interference Modeling
Explicitly modeling each interferer’s channel is costly.
Suggest to approximate some interference as Gaussian channel.
  Skip generating a large amount of the fading channels
  Without introducing inaccuracy on received SINR and PHY performance.
  A common practice for complexity reduction. [6]
Question: how to select an interference to be approximated?
  Long Term SIR thresholding
    If the long term received power from an interferer relative to that of the desired transmitter is lower than a threshold, approximate its signal to be Gaussian.
  A static decision for each drop

## Slide 18: Simplification of Interference Modeling (2)
Specifically, the interference on a particular tone
  Delta = inf :
    explicitly model the fading channels of all seen interferers for the frame
  Delta = 10dB:
    explicitly model the fading channels of all seen interferers whose received power is within 10dB of the desire transmitter, model the rest of seen interferers as AWGN by their received power
Step-2 calibration is a perfect stage to study the threshold
  Choose a threshold that does not impact the SINR distribution.
  Use scenario3 and 4 as an example.

## Slide 19: Simulation Assumptions (Scenario 3)
Parameter | Value
Environment | BSSs in Hexagon (figure 5), simulated BSS in 1 channel (figure 6) BSS radius: R=7m
Number of STAs | 30 STAs per BSS
Channel Model | TGn D (AP-AP, AP-STA), TGn B (STA-STA)
Penetration Loss | None
BW | 20MHz at 2.4GHz. Each simulated BSS selects the same channel.
TX Power | AP: 17dBm, STA: 15dBm
Association | 100% STA associated with the strongest AP

## Slide 20: Instantaneous UL SINR Per Tone
Reasonably small deviation between complete interference modeling and SIR thresholding of 30 and 10dB .
  Using 10dB threshold put 96% channels into AWGN
  Using 30dB threshold put 65% channels into AWGN

## Slide 21: Effective SINR Per Frame

## Slide 22: Simulation Assumptions (Scenario 4)
Parameter | Value
Environment | BSSs in Hexagon (figure 8), ICD = 130m
Number of STAs | 30 STAs per BSS (50% outdoor, 50% indoor)
Channel Model | UMi (AP-AP, AP-STA, STA-STA)
Penetration Loss | 20dB (outdoor-indoor)
BW | 20MHz at 2.4GHz. Each simulated BSS selects the same channel.
TX Power | AP: 30dBm, STA: 15dBm
Association | 100% STA associated with the strongest AP

## Slide 23: Instantaneous UL SINR Per Tone

## Slide 24: Effective SINR Per Frame

## Slide 25: Summary
Two options of instantaneous SINRs calibration are proposed.
Suggestion1:
  Use Option 1 (SINR per tone) given its convenience and readiness.
  Option 2/2a can be revisited in the latter steps of calibrations.
Suggestion2:
  Using SIR-thresholding to approximate some interference as AWGN
  Exact threshold can be also chosen through calibration.

## Slide 26: References
[1] 11-13-1392-00-0hew-methodology-of-calibrating-system-simulation-results
[2] 11-14-0053-00-0further-considerations-on-calibration-of-system-level-simulation
[3] 11-14-0116-01-0Long-Term-SINR-Calibration-for-System-Simulation
[4] 11-14-0336-00-0Calibration-of-Long-Term-SINR-for-System-Simulation
[5] 11-13-1001-06-0hew-HEW-evaluation-simulation-scenarios-document-template
[6] 11-13-0043-02-0PHY-abstraction-in-system-level-simulation-for-HEW-study