## Slide 1: Discussion on power save mode for real time traffic
Date: 2014-03-16
Authors:

## Slide 2: Abstract
This presentation discusses on power save mode with real time traffic for High Efficiency WLAN.

## Slide 3: Characteristics on Real Time Traffic (1/3)
1.1 Buffered Video streaming [1, 2]
  Video streaming is typically unidirectional traffic
  Video streaming applications have lenient QoS requirements
    Delay tolerable (the video can take several seconds to cue up)
    Jitter tolerable (because of application buffering).
  Uses buffer time that is the amount of video content in seconds to cache on the user’s computer or device before playback of the video can begin.
    After playout, buffering is highly dependant on network speed.
  Protocol stack: TCP
    Provides additional reliability
1.2 Live Video streaming [1, 2]
  Unidirectional traffic
  Not lenient QoS requirements
    Delay sensitive
    Jitter sensitive
  Protocol stack: TCP/UDP
    Depending on implementation (using either TCP or UDP), reliable transmission can be supported.

## Slide 4: Characteristics on Real Time Traffic (2/3)
2. Video Conferencing [1, 2]
  Two-way traffic
  Typical protocol: UDP/IP
  Require lower packet loss ratio at MAC since UDP does not provide additional reliability
    Loss should be no more than 1 percent.
  Delay and Jitter sensitive
    One-way latency (mouth to ear) should be no more than 150ms.
    Average one-way jitter should be targeted at less than 30ms.

## Slide 5: Characteristics on Real Time Traffic (3/3)
3. Voice over IP [1, 2]
  Two-way traffic
  Typical protocol: UDP/IP
  Require lower packet loss ratio at MAC since UDP does not provide additional reliability
    Loss should be no more than 1 percent.
  Delay and Jitter sensitive
    One-way latency (mouth to ear) should be no more than 150ms.
    Average one-way jitter should be targeted at less than 30ms.
  In general, On-Off Model is used for VoIP Traffic Modeling.
    Because, Human speech consists of talk-spurts (on period) and silence gaps (off period).

## Slide 6: Recap: 802.11 Power Save Mode (1/4)
Power Save Poll (PS-Poll)
  During sleeping periods, access points buffer any unicast frames or broadcast frames for sleeping stations.
  To retrieve buffered frames, newly awakened stations use PS-Poll frames.
Figure 1. Power Save Poll

## Slide 7: Recap: 802.11 Power Save Mode (2/4)
Unscheduled automatic power-save delivery (U-APSD)
  When an AP delivers downlink frames to STAs operation with power saving mode including U-APSD, it has to confirm that they are awake. An uplink data or null-data frame is used to trigger downlink frames.
Figure 2. Traffic flow with U-APSD

## Slide 8: Recap: 802.11 Power Save Mode (3/4)
Scheduled automatic power-save delivery (S-APSD)
  QoS-STA negotiates a APSD schedule with QoS AP.
  QoS AP start transmitting the frames at Service Start Time.
  QoS-STA must wake up at Service Start Time and the following periods to receive frames.
Figure 3. Traffic flow with S-APSD

## Slide 9: Recap: 802.11 Power Save Mode (4/4)
Power Save Multi-Poll (PSMP)
  AP will send a schedule during its own TXOP as to when to be awake to receive data and also schedule as to when to transmit.
  Since this schedule is known Stations can sleep more and also at the same time not miss any frames.
Figure 4. Power Save Multi-Poll

## Slide 10: Summary (1/2)
 |  | Application | Characteristics | 802.11 power save mode1
Video Streaming | Buffered Video Streaming |  | Delay and Jitter tolerable Reliable transmission is supported (using TCP) | Power Save Poll (PS-Poll)
 | Live Video Streaming |  | Delay and Jitter sensitive Depending on implementation (using either TCP or UDP), reliable transmission can be supported. | There may not be proper power save mode. Non-AP STA can be awake while receiving this type of service.
Video Conferencing |  |  | Delay and Jitter sensitive Reliable transmission is not supported2 (using UDP) | APSD (U-APSD/S-APSD)
1 This column shows 802.11 power save mode which is generally used for each type of traffic.
2 When using UDP, lower packet loss ratio in WLAN is required than using TCP.

## Slide 11: Summary (2/2)
 |  | Applications | Characteristics | 802.11 Power save mode
VoIP | VoIP (without silence suppression3) |  | Delay and Jitter sensitive Reliable transmission is not supported (using UDP) Not support silence suppression function | APSD (U-APSD/S-APSD) Power Save Multi Poll (PSMP)
 | VoIP (with silence suppression) |  | Delay and Jitter sensitive Reliable transmission is not supported (using UDP) Support silence suppression function | Current power save mode does not consider the operation of VoIP with silence suppression.
3The term silence suppression is used in telephony to describe the process of not transmitting information over the network when one of the parties involved in a telephone call is not speaking, thereby reducing bandwidth usage.

## Slide 12: Conclusion
We introduced all types of real time traffic and 802.11 power save mode in this contribution.
We analyzed that real time traffic such as live video streaming and VoIP with silence suppression may not be efficiently supported by the current 802.11 power save mode.
Even other traffic such as buffered video streaming, video conferencing, and VoIP without silence suppression may also be needed to be enhanced as environments become dense.
In conclusion, we need to study 802.11 power save mode enhancement for real time traffic in high efficiency WLAN.

## Slide 13: References
[1] Lync Conference 2013, Lync Mobile Devices and Wi-Fi
[2] 11-13-1162-01-0hew-video-categories-and-characteristics
[3] Cisco, Quality of Service Design Overview
[4] Cisco, Real-Time Traffic over Wireless LAN Solution Reference Network Design Guide
[5] ACM CoNEXT 2011, Network Characteristics of Video Streaming Traffic
[6] Harkirat Singh,“Enhanced Power Saving in Next Generation Wireless LANs”, IEEE 2006
[7] 11-10-1054-00-00ac-wide-band-obss-friendly-psmp
[8] IEEE 802.11™-2012