## Slide 1: Proposed Resolution to Comments Pertaining to Section 9.33.11 in CC12 Date: 2014-3-20

## Slide 2: Introduction
This presentation proposed the resolutions to the comments to Tgaj draft specifications D0.01 section 9.33.11 in CC12.
The resolutions addressed the following comments in the comments database IEEE 802.11-14-0332r0.
CID 19 | CID 28
CID 20 | CID 29
CID 21 | CID 30
CID 22 | CID 31
CID 23 (part of) | CID 32
CID 24 | CID 65
CID 25 (part of) | 

## Slide 3: Response to CID 19 (1/2)
Comment
  "During the scan phase, which lasts for at least aMaxBIDuration, devices scheduled to operate in the alternative channel shall scan the channel to determine whether the alternative channel is occupied by another network.”
  What is the action related to "shall scan"? How is the start and stop of this phase determined?
  Normative verbs require precise definitions of all the conditions and all the actions.

## Slide 4: Response to CID 19 (2/2)
Suggested Remedy
  Replace undefined terms "shall scan" and "the scan phase" with precise definitions related to observable actions or on-the-air signalling.
Accept in principle.
Revised Text
The spectrum access in the alternative channel is divided into three phases: monitor phase, transmission phase and suspension phase. Scheduled transmission in the alternative channel shall start with the monitor phase and then the three phases rotate cyclically until all the scheduled transmissions in the alternative channel are completed.
The monitor phase shall last for aMaxBIDuration. During the monitor phase, a CDMG STA that is scheduled to operate in the alternative channel shall listen for the transmission of DMG or CDMG Beacon frames in the alternative channel.

## Slide 5: Response to CID 20 (1/2)
Comment
  “all the devices shall”
  You cannot write a normative statement across more than one device.
Suggested Remedy
  Replace in the singular using the template form: "A <entity> that <conditions> shall <actions>“,

## Slide 6: Response to CID 20 (2/2)
Accept in principle.
Revised Text
During the suspension phase, a CDMG STA that is scheduled to operate in the alternative channel shall switch to the dedicated channel and be ready to receive transmission from the AP or PCP in the dedicated channel. The CDMG STA may receive the CDMG Beacon frame or Announce frame transmitted by the AP or PCP to maintain synchronization with the AP or PCP during the suspension phase. If a CDMG STA receives a DELTS frame from the AP or PCP during the suspension phase, the CDMG STA will cease opportunistic transmission in the alternative channel.

## Slide 7: Response to CID 21
Comment
  “A picture is worth a thousand words.”
Suggested Remedy
  A figure to explain the various phases might be helpful.
Propose to Accept.
Include figure below
Figure 9-46a—Opportunistic Transmission in Alternative Channels for CDMG STAs

## Slide 8: Response to CID 22 (1/2)
Comment
  “The PCP/AP shall also ensure”
  "Ensure" is a bad word, i.e. is deprecated by IEEE-SA.
Suggested Remedy
  Express the normative behaviour in what the AP shall do. i.e. "The AP shall schedule time for its communications with each associated STA during the AT."

## Slide 9: Response to CID 22 (2/2)
Accept in principle.
Revised Text
The AP or PCP should (shall) send a DMG CTS-to-self frame in the ATIs (9.33.3) during the suspension phase to each of the CDMG STAs scheduled to operate in the alternative channel. If a CDMG STA receives one or more valid DMG or CDMG Beacon frame with a BSSID different from its own during the monitor phase, the CDMG STA shall response with a DELTS frame to the AP or PCP with the Reason Code field (8.4.1.7) set to 68 (the alternative channel is occupied) upon the reception of a DMG-CTS-to-self frame from the AP or PCP during the ATI. If a transmission link in the alternative channel cannot be established during the transmission phase, the CDMG STA shall response with a DELTS frame to the AP or PCP with the Reason Code field set to 67 (transmission link establishment in alternative channel failed).
If the AP or PCP received a DELTS frame with the Reason Code field (8.4.1.7) set to 68 in a ATI, the AP or PCP will transmit a DELTS frame to each of the CDMG STAs scheduled to operate in the alternative channel in the same ATI or the subsequent ATI.

## Slide 10: Response to CID 23
Comment
  “pair of devices”
  We have a whole lot of different names for devices. All communicating devices are at least STAs.
  There is no need to use a generic term when a more precise one is suitable, even if the more precise .”
Suggested Remedy
  Review all 55 instances of "device" and replace by an appropriate term, such as "non-PCP/non-AP STA“.
Accept in principle.
Devices is no longer used in revised text for section 9.33.11

## Slide 11: Response to CID 24
Comment
  “shall assume”
  This is always wrong. AP's don't assume anything, they are pieces of electronic kit.
  My cats assume things, and rarely understand normative verbs..”
Suggested Remedy
  Express it in terms of what the AP does (i.e. observable actions), not in terms of what it assumes.
Accept in principle.
Revised Text (Please see CID 22)

## Slide 12: Response to CID 25
Comment
  “the devices are expected to transmit“
  Passive voice is dangerous. Exactly who or what expects them to transmit? Exactly what does this un-identified entity do when they don't?
Suggested Remedy
  Remove all use of passive voice in the draft.
Accept in principle.
Revised Text (Please see CID 22)

## Slide 13: Response to CID 28 (1/2)
Comment
  "Otherwise, the devices are expected to transmit a DELTS frame (8.5.3.4) to delete the allocated schedule and report the reason for the inability to complete the transmission."
  Which part of the STA decides to do this? Sending a DELTS is a management action, not part of the data plane.
  Generally the SME knows about allocations and timing and the MLME is fairly dumb (i.e. has minimal retained state)?

## Slide 14: Response to CID 28 (2/2)
Suggested Remedy
  Consider moving this behaviour to Clause 10 where it can be described as another reason to delete a schedule. It can be referenced from here.
  Reword so that the identify of the entity making the decision is not obscured, and its relation to the MLME-DELTS.* primitives is explicitly stated.
Accept in principle.
  The sending of the DELTS frame is now explicitly linked to a set of the conditions.
Revised Text (Please see CID 22)

## Slide 15: Response to CID 29 (1/2)
Comment
  “"shall periodically return"
  Not enough detail. For every "shall" statement, there should be enough detail to create a test for it. So how do you determine if a STA is doing this periodically? What are the upper and lower bounds for the period. If the answer is "none" then a period of 10**10 years is compliant, but not very observable.
Suggested Remedy
  Turn requirement into one that can be tested.

## Slide 16: Response to CID 29 (2/2)
Accept in principle.
Revised Text
“If a CDMG STA is not the source or destination STA in an access period, it may switch to the dedicated channel to receive the CDMG Beacon frame or Announce frame send out by the AP or PCP to maintain synchronization with the AP or PCP.”
“During the suspension phase, a CDMG STA that is scheduled to operate in the alternative channel shall switch to the dedicated channel and be ready to receive transmission from the AP or PCP in the dedicated channel. The CDMG STA may receive the CDMG Beacon frame or Announce frame transmitted by the AP or PCP to maintain synchronization with the AP or PCP during the suspension phase. If a CDMG STA receives a DELTS frame from the AP or PCP during the suspension phase, the CDMG STA should (will) cease opportunistic transmission in the alternative channel.”

## Slide 17: Response to CID 30
Comment
  "shall return" - the normative effect of returning is not well defined.
Suggested Remedy
  Relate to observables, e.g., shall be able to receive from the PCP/AP in this channel during the scheduled slots.
Accept in principle.
Revised Text (Please see CID 29)

## Slide 18: Response to CID 31 (1/2)
Comment
  "If PCP/AP received the information that the alternative channel is occupied by another network"
  Relate to observables - i.e. fields and frames.
Suggested Remedy
  Reword to cite specific fields in specific frames that provide this information.

## Slide 19: Response to CID 31 (2/2)
Accept in principle.
Revised Text
“The AP or PCP shall send a DMG CTS-to-self frame in the ATIs (9.33.3) during the suspension phase to each of the CDMG STAs scheduled to operate in the alternative channel. If a CDMG STA receives one or more valid DMG or CDMG Beacon frame with a BSSID different from its own during the monitor phase, the CDMG STA shall response with a DELTS frame to the AP or PCP with the Reason Code field (8.4.1.7) set to 68 (the alternative channel is occupied) upon the reception of a DMG-CTS-to-self frame from the AP or PCP during the ATI. If a transmission link in the alternative channel cannot be established during the transmission phase, the CDMG STA shall response with a DELTS frame to the AP or PCP with the Reason Code field set to 67 (transmission link establishment in alternative channel failed).”

## Slide 20: Response to CID 32 (1/2)
Comment
  "" shall inform the rest of the devices"
  What form does this information take?"
Suggested Remedy
  Relate to specific fields in specific frames.

## Slide 21: Response to CID 32 (2/2)
Accept in principle.
Revised Text
“If the AP or PCP received a DELTS frame with the Reason Code field (8.4.1.7) set to 68 in a ATI, the AP or PCP shall transmit a DELTS frame to each of the CDMG STAs scheduled to operate in the alternative channel in the same ATI.”

## Slide 22: Response to CID 65
Comment
  Subclause 9.33 defined the rules for DMG STAs, But the subclause "9.33.11" is not for DMG device but for CDMG device.”
Suggested Remedy
  change the title to "Opportunistic Transmission in Alternative Channels for CDMG“
Accept with a slight modification to suggested remedy.
    change the title to "Opportunistic Transmission in Alternative Channels for CDMG STAs”
  Alternatively, Editor may create a new section that defines rules for CDMG STAs can be justified.

## Slide 23: Revised Text
The complete revised text proposal for section 9.33.11 is provided in IEEE 802.11-14-0408r1.
Suggest to replace Section 9.33.11 in TGaj draft specifications D0.01 with the revised text proposal.

## Slide 24
THANK YOU