## Slide 1: A Vastly Simpler Alternative for P802.11ak
Date: 2014-05-11
Authors:

## Slide 2: Abstract
Methods for accomplishing the primary goals of P802.11ak are presented that are vastly simpler than the current working proposal, which is defined in 11-14/0454r1. This simplicity is obtained at the expense of making optional the capability of directing a single transmission to multiple bridge / stations (usage of multicast RA).

## Slide 3: Concerns with Compatibility
How many prior 802.11 amendments have prohibited “mixed mode” operation (i.e. activating a new feature blocks simultaneous association of legacy)?
  Changes specific to new bands have
  As a configuration option at AP vendor’s/customer’s choice
The standard has striven for mixed mode compatibility in the past
  11g, 11e, 11n, 11ac, …
Lack of mixed mode is a barrier to entry / adoption
Lack of mixed mode causes more OTA overhead when needed
  Not +1 BSSID, rather up to *2 multiple BSSIDs
Lack of mixed mode obligates AP vendors to solve the problems
  Per Client vs Per BSS is only granularity of config, not simplifying the task
Users are offered SSID, not BSSID, so must they know their Bridging needs?
We can go down that path, if no practical alternative exists, but we are not there yet.

## Slide 4: Concerns with CBA-MSDU
Subverting of A-MSDU will degrade performance
  A-MPDU of A-MSDU is critical toward Gbps rates (1213 vs 933 Mbps Goodput @ 1.3 Gbps PHY rate)
  Not all Clients support A-MPDU of A-MSDU, so CBA-MSDU precludes A-MPDU (301 vs 933 Mbps @ 1.3 Gbps)
  Aggregation must be left available for link level optimization
Complexity of proposal
  CBA-MSDU format more suitable for Control Plane vs Data Plane
  Frames to Bridging function interleaved between interfaces / Flows
    Interleaved between destination list implies between CBA-MSDU
    Effective Egress Aggregation / queuing becomes high complexity
CBA-MSDU certainly not needed to Unicast RA

## Slide 5: Will all STA want/need to be GLK?
Most Clients don’t want to be a Bridge
  Only covering themselves will remain the typical case
  Why impact Battery Life from N/A Unicast Flooding?
  Would most battery powered devices want to Bridge traffic for others?
  Counter to Directed Multicast Service (desired for Battery Life)
In many venues non-AP GLK will be prohibited
  IT typically prohibit non-IT administered switches with justification
  Serious security issues not addressed by current draft
    AP today should validate SA to avoid MAC spoofing (A-MSDU/4Addr)
    How would 802.1x / 802.11i authenticate downstream device?
    What is the trust model?
    802.1ae is usually point to point, and would defeat QoS + Multicast pruning through GLK Bridges
  Scaling issues for AP, Switches, Controllers

## Slide 6: Concerns with use of Multicast (1 of 2)
Multicast RA in 802.11 has poor reliability
  Unicast depends on retries, not available to Multicast
    Ignoring mal-adopted 11aa (GCR)
  PER multiplies with each wireless Hops (1-(1-PER)N)
  PER increases with Client count due to CSMA-CA collisions
  Severity of PER increases with number of devices affected
Significantly lower rates are the norm for Multicast
  Rate adaptation strives for best trade off between Goodput vs PER
  Multicast is Least common denominator + SNR safety margin
  No beamforming Gain, and (adopted) STBC is single Spatial Stream
  No MU-MIMO
  Rarely leverages multiple SS, so not achieving Gbps rates
  Single “sticky” or 1SS Client could break Multicast for everyone

## Slide 7: Concerns with use of Multicast (2 of 2)
Increased Latency for dedicated Bridges in presence of a single Power Save GLK STA (due to DTIM)
AP’s usually have small (policed) Multicast queue sizes
  Due to higher overhead on channel
  Due to Power Save impact (DTIM)
  Due to QoS priority inversion of Power Save
Risks of frame reordering
  During Source learning or IGMP subscription changes
  When Multicast flows are partially filtered per path (ACL)
Bridging services should be layered on a reliable link
  Many protocols assume low PER Multicast -- IGMP, MRP, RIP, etc.

## Slide 8: How expensive is Multicast Replication?
Multicast RA vs Unicast replication costs misleading
  Replication costs increase with number of Clients (<linear)
    Somewhat offset by better aggregation, higher rates, MU-MIMO
    VLAN subscription and IGMP will prune Multicast per peer
  Channel collision rate increase with number of Clients (>linear)
Replication limited to Clients that need GLK
Replication is overhead to channel, not CPU
  Multiple references to same buffer vs buffer copies
Fully connected wireless Meshes not always favorable model
  Rate selection often favors sending to Bridge in the middle
  CP overhead not justified when DP bandwidth light between sub-trees
  More common to have a small list of reasonable peers

## Slide 9: Focus on what is needed (1 of 2)
LLC vs LPD
  Concern for any Hardware optimizations for this and/or A-MSDU formats, as driven by need for increasing speeds
  VLAN tagging dysfunctional in 802.11, but fixed by WMM
  Saving 6 bytes has nothing to do with Bridging or Gbps speeds
  More applicable to low speed WLAN (niche)
  Bridging doesn’t work well now over low speed links
  This is outside our PAR, so should be moved to different/new TG

## Slide 10: Focus on what is needed (2 of 2)
802.1D vs 802.1p
  Changes affect detection of CCI Voice traffic
  Changes affect Power Save modes, and will need WMM changes
  Honoring of 802.1p is not the same as marking of UP
  We can map PCP to UP easily without loss of function
  We can still keep PCP when VLAN tagging is used
Per hop Header conversion / manipulation is common
  Insertion/removal of VLAN tags and MACSEC headers + trailers
  NPU starting to appear in AP, usually HW optimized for this

## Slide 11: Recommendation (1 of 2)
Make GLK a role of associated peer vs role of BSS
  Allow vendor/customer decide if mixed mode is allowed?
  Allow roles to be negotiated by authentication / security policies
Use of Unicast 4 Address format Mandatory for GLK
  Use of 4 Address as originally designed (present in 802.11-1999)
  Leave use of aggregation to Link Level
Allow Multicast (RA), but only as an optional mode
  CBA-MSDU needs to be significantly simplified
  CBA-MSDU only used for Multicast RA
  BSSID that support mixed GLK / non-GLK Clients provides different Keys for each (voiding compatibility issue)
  Offset DTIM interval for Power Save Bridges vs non GLK
  Should CBA-MSDU support both directions? (not just AP to STA, so not based on AID)

## Slide 12: Recommendation (2 of 2)
Keep existing LLC format, even if not beautiful
  Fix Appendix P for carrying of all tagged frames, including VLAN
Don’t change meaning of UP or mapping to AC
  Do call out mapping of 802.1p PCP to UP
  Do pass down CPC to 802.1AC Convergence Function