## Slide 1: 802.11 Portal and 802.1AC Convergence Function
Date: 2014-05-05
Authors:

## Slide 2: Abstract
A model is presented for the IEEE 802.11 Portal Convergence Function to appear in IEEE P802.1AC-REV Clause 12.2.1, now being balloted in the IEEE 802.1 Interworking Task Group.

## Slide 3: This is an example of a physical network
802.3
Two physical boxes, commonly (but inaccurately) called “APs,” connected by an IEEE 802.3 link.
Two clients of “AP 1” shown, two wireless and one wired clients of “AP 2” not shown.
No VLANs.
“AP” 1
“AP” 2
802.3

## Slide 4: Layering
In the ISO layering model, a DATA.request is presented by a higher layer to a lower layer, and a DATA.indication is presented by a lower layer to a higher layer.
In all further diagrams in this deck, the “higher” layer is closer to the top of the slide, and the “lower” layer closer to the bottom.

## Slide 5: A standard view of that same network in 802.11 today
Distribution System (DS)
MAC
PHY
MAC
PHY
MAC
PHY
AP STA 1
Non-AP STAs
MAC
PHY
AP STA 2
unspecified
portal
AP
AP
MAC
PHY
802.3
This is similar to IEEE 802.11-2012, Figure R-1, but drawn with “request down indication up” rigorously applied.
The DS has three users, two APs and a portal, so is shown passing behind a MAC.

## Slide 6: One possible 802.1AC-to-portal architecture
A connecting link is required, because the portal uses a SAP; it does not provide one.
Therefore an 802.1AC convergence layer specific to 802.11 is not necessary.
Distrib. System (DS)
MAC
PHY
AP STA
unspecified
portal
AP
MAC
PHY
MAC
PHY
anything, e.g. 802.3
802.3
MAC
PHY
802.1Q bridge relay
MAC
PHY
MAC
PHY
Non-AP station
end station

## Slide 7: But, there is an alternate approach.
This interface is defined.
It is the DS_SAP, illustrated in IEEE Std 802.11-2011 Figure R-1.
Distrib. System (DS)
MAC
PHY
AP STA
unspecified
portal
AP
MAC
PHY
MAC
PHY
anything, e.g. 802.3
802.3
MAC
PHY
802.1Q bridge relay
MAC
PHY
MAC
PHY
Non-AP station
end station

## Slide 8: So, another representation could be …
That is, the 802.1AC Clause 12.2.1 “portal convergence function” is not an interface to a portal; .1AC 12.2.1, plus a bridge relay function, is an example of a portal.
.1AC 12.2.1 connects the ISS to the DS_SAP.
Distrib. System (DS)
MAC
PHY
AP STA
unspecified
AP
802.1Q bridge relay
MAC
PHY
Non-AP station
MAC
MAC
802.3
PHY
PHY
end station
.1AC
One example (of many) of a portal

## Slide 9: Tasks for 802.1AC
Rewrite 802.1AC Draft 0.2 Clause 12.2.1 to provide a convergence function that maps the 802.1AC ISS to the 802.11 DS_SAP.

## Slide 10: Tasks for 802.11
Perhaps none, perhaps …
802.11 should consider making the DS_SAP normative.
- Rationale would be so that .1AC can reference normative text in 802.11
Making the DS_SAP normative does not define the underlying distribution system.
Making the DS_SAP normative simply imposes a set of requirements on a distribution system.
- 802.11 has a precedent of stating such requirements in normative text