## Slide 1: PHY Abstraction for TGax System Level Simulations
Date: 2014-04-15
Authors:

## Slide 2: Introduction
ESM (effective SINR mapping) for PHY abstraction for 802.11ax:
  General concept of ESM for PHY Abstraction:
    Motivation: to predict the instantaneous packet error rate (PER) for the given channel realization
    Prior work in 802.11 HEW/ax [3-7] have shown several effective methods
      RBIR, RBIR/BICM etc.
    We conducted an internal study of a promising mapping method for BCC/LDPC, SISO, over channels B and D

## Slide 3: RBIR (Received Bit Information Rate)
M: number of constellation points for the MCS
U: complex Gaussian CN(0,1) random distribution
sk: constellation point with normalized energy
x: per-tone SINR

## Slide 4: Simulation Setup
11ac, SISO
  MCS 0-6
  BCC and LDPC
  AWGN and Fading Channel B/D
  20 MHz, FFT size 64
  ESM mapping method: RBIR
  Tuning
    Beta = 1; alpha tunable
    Examined both fixed and MCS-dependent tuning for channels B and D
Effective SNR vs. PER curves are compared against AWGN PER curves
  The closer the better

## Slide 5: MCS Dependent Tuning
 | MCS | 0 | 1 | 2 | 3 | 4 | 5 | 6
a (dB, BCC) |  | 1 | 1 | 0.9 | 0.7 | 0.7 | 0.5 | 0.3
a (dB, LDPC) |  | 0.3 | 0.2 | 0.2 | 0.2 | 0.2 | 0 | 0

## Slide 6: MCS Independent Tuning
 | MCS | 0 | 1 | 2 | 3 | 4 | 5 | 6
a (dB, BCC) |  | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7
a (dB, LDPC) |  | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1

## Slide 7: Summary
PHY abstraction for SISO simulation results for MCS 0-6
  RBIR is effective in predicting instantaneous PER results
  RBIR works more effectively for LDPC than BCC
  RBIR mapping is generally channel independent
  Tradeoff between mapping complexity and accuracy
    If simple mapping is desired, alpha may be chosen as MCS-independent
    If more accurate mapping is desired, alpha may be chosen as MCS-dependent
Results for higher MCS and MIMO to be shown later
Need to account for implementation margin
  Explicit modeling of impairments in SINR definition [LGE, 6]
  Alternatively, a simple implementation loss in the link budget

## Slide 8: References
IEEE 802.16m-08/004r5, “IEEE 802.16m Evaluation Methodology Document (EMD)”
3GPP R1-040089, “OFDM Exponential Effective SIR Mapping Validation, EESM Simulation Results for System-Level Performance Evaluations, and Text Proposal for Section A.4.5 of TR 25.892”.
J. Zhang et. al., “PHY Abstraction for HEW System Level Simulation”, IEEE 802.11-13/1131r0.
D. Lim et. al., “PHY abstraction for HEW evaluation methodology”, IEEE 802.11-13/1059r0.
Y. Sun et. al., “PHY Abstraction for HEW System Level Simulation”, IEEE 802.11-14/0117r0.
D. Lim et. al., “ Suggestion on PHY Abstraction for Evaluation Methodology ”, IEEE 802.11-14/0353r0.
F. Tong et. al., “PHY abstraction in system level simulation for HEW study”, IEEE 802.11-14/0043r2.
S. Vermani et. al, “PHY Abstraction”, IEEE 802.11-14/0330r3.