## Slide 1: PHY Abstraction for TGax System Level Simulations
Date: 2014-05-05
Authors:

## Slide 2: Abstract
In an earlier revision, RBIR (Received Bit Information Rate) based mapping was shown to be effective in predicting instantaneous PER for IEEE 802.11 SISO PHY.
Updates since last revision: simulations were re-run for the SISO case with ideal filtering and reduced number of LDPC iterations; simulation results for 2x2 MIMO added.
New results presented here show that RBIR is an excellent candidate for PHY abstraction : effective for both SISO and MIMO PHY, for both BCC and LDPC, different channel types, and different MCSs.

## Slide 3: Introduction
ESM (Effective SINR Mapping) for PHY abstraction for 802.11ax:
  General concept of ESM for PHY Abstraction:
    where SINRn is the post processing SINR at the nth subcarrier, Φ is the ESM function, a and b are tuning factors
Motivation: to predict the instantaneous packet error rate (PER) for a given channel realization.
Prior work in 802.11 HEW/ax [3-7] has shown several effective methods (RBIR, RBIR/BICM etc.).
In this contribution we verify the RBIR method for BCC/LDPC, SISO/MIMO, over channels B and D.

## Slide 4: RBIR (Received Bit Information Rate)
M: number of constellation points for the MCS
U: complex Gaussian CN(0,1) random distribution
sk: constellation point with normalized energy
x: per-tone SINR

## Slide 5: ESM for MIMO
Where:
  Nss is the number of spatial streams
  SINRn,nss is the post-MMSE equalization SINR for:
    the nth tone (n = 1, …, N), and
    the nssth stream (nss = 1, …, Nss)
Simulation results based on 2x2 MIMO, i.e. Nss = 2.

## Slide 6: Simulation Setup
802.11ac compatible link level simulations
  MCS 0 – 8, BCC and LDPC
  AWGN (reference) and fading Channels B and D
  20 MHz, FFT size 64
  ESM mapping method: RBIR
  No tuning (a = 1, b = 1) unless explicitly mentioned
  SISO and MIMO (2 x 2 MIMO with Nss= 2)
  No impairments, ideal channel estimation, MMSE equalization
  Block sizes 250/500/1000/1000 bytes for QPSK/ 16QAM/ 64QAM/ 256QAM
  Slight simulator parameter change since last revision
    Ideal filtering, number of LDPC iterations = 10

## Slide 7: SISO for LDPC
RBIR is effective in predicting instantaneous PER for SISO/LDPC
  Offset (relative to AWGN reference curve) is generally less than 0.2dB
  RBIR mapping is generally channel independent: Channels B and D mostly overlap

## Slide 8: SISO for BCC
RBIR is effective in predicting instantaneous PER for SISO/BCC
  Offset (relative to AWGN reference curve) is generally less than 0.6dB
  RBIR mapping is generally channel independent: Channels B and D mostly overlap

## Slide 9: 2x2 MIMO (Nss = 2) for LDPC
RBIR is effective in predicting instantaneous PER for MIMO/LDPC
  Offset (relative to AWGN reference curve) is generally less than 0.2dB
  RBIR mapping is generally channel independent: Channels B and D mostly overlap

## Slide 10: 2x2 MIMO (Nss = 2) for BCC
RBIR is effective in predicting instantaneous PER for MIMO/BCC
  Offset (relative to AWGN reference curve) is generally less than 0.6dB
  RBIR mapping is generally channel independent: Channels B and D mostly overlap

## Slide 11: BCC/SISO with Tuning
When using BCC/SISO, RBIR accuracy may be improved by tuning
  a = 1.15 , b = 1 for all MCSs, for both SISO/MIMO, for Channels B/D

## Slide 12: BCC/MIMO with Tuning
When using BCC/MIMO, RBIR accuracy may be improved by tuning
  a = 1.15 , b = 1 for all MCSs, for both SISO/MIMO, for Channels B/D

## Slide 13: Summary
  RBIR is an excellent candidate for PHY abstraction
  Effective in predicting instantaneous PER results
  Generally channel independent
  Applicable for both SISO and MIMO
  Works very well with LDPC, for all channel types and MCSs
    Offsets are generally less than 0.2dB; no tuning required
  Works well with BCC, for all channel types and MCSs
    With simple, fixed tuning (a = 1.15, b = 1), offsets are generally less than 0.2dB
    With no tuning, offsets are generally less than 0.6dB

## Slide 14: References
IEEE 802.16m-08/004r5, “IEEE 802.16m Evaluation Methodology Document (EMD)”
3GPP R1-040089, “OFDM Exponential Effective SIR Mapping Validation, EESM Simulation Results for System-Level Performance Evaluations, and Text Proposal for Section A.4.5 of TR 25.892”.
J. Zhang et. al., “PHY Abstraction for HEW System Level Simulation”, IEEE 802.11-13/1131r0.
D. Lim et. al., “PHY abstraction for HEW evaluation methodology”, IEEE 802.11-13/1059r0.
Y. Sun et. al., “PHY Abstraction for HEW System Level Simulation”, IEEE 802.11-14/0117r0.
D. Lim et. al., “ Suggestion on PHY Abstraction for Evaluation Methodology ”, IEEE 802.11-14/0353r0.
F. Tong et. al., “PHY abstraction in system level simulation for HEW study”, IEEE 802.11-14/0043r2.
S. Vermani et. al, “PHY Abstraction”, IEEE 802.11-14/0330r3.
P. Xia et. al., “PHY Abstraction for TGax System Level Simulations”, IEEE 802.11-14/0527r0.