## Slide 1: 802.11ak and 802.1AC Convergence Function
Date: 2014-05-05
Authors:

## Slide 2: Abstract
Building upon a model being proposed for the IEEE 802.11 Portal Convergence Function, this presentation carries that concept into the 802.11ak concepts, and 802.1AC considerations for these extended concepts.

## Slide 3
Following are several slides from the 802.11 portal presentation (being considered in ARC, and 802.1AC) – 11-14/497 …

## Slide 4: This is an example of a physical network
802.3
Two physical boxes, commonly (but inaccurately) called “APs,” connected by an IEEE 802.3 link.
Two clients of “AP 1” shown, two wireless and one wired clients of “AP 2” not shown.
No VLANs.
“AP” 1
“AP” 2
802.3

## Slide 5: Layering
In the ISO layering model, a DATA.request is presented by a higher layer to a lower layer, and a DATA.indication is presented by a lower layer to a higher layer.
In all further diagrams in this deck, the “higher” layer is closer to the top of the slide, and the “lower” layer closer to the bottom.

## Slide 6: A standard view of that same network in 802.11 today
Distribution System (DS)
MAC
PHY
MAC
PHY
MAC
PHY
AP STA 1
Non-AP STAs
MAC
PHY
AP STA 2
unspecified
portal
AP
AP
MAC
PHY
802.3
This is similar to IEEE 802.11-2012, Figure R-1, but drawn with “request down indication up” rigorously applied.
The DS has three users, two APs and a portal, so is shown passing behind a MAC.

## Slide 7: One possible 802.1AC-to-portal architecture
A connecting link is required, because the portal uses a SAP; it does not provide one.
Therefore an 802.1AC convergence layer specific to 802.11 is not necessary.
Distrib. System (DS)
MAC
PHY
AP STA
unspecified
portal
AP
MAC
PHY
MAC
PHY
anything, e.g. 802.3
802.3
MAC
PHY
802.1Q bridge relay
MAC
PHY
MAC
PHY
Non-AP station
end station

## Slide 8: But, there is an alternate approach.
This interface is defined.
It is the DS_SAP, illustrated in IEEE Std 802.11-2011 Figure R-1.
Distrib. System (DS)
MAC
PHY
AP STA
unspecified
portal
AP
MAC
PHY
MAC
PHY
anything, e.g. 802.3
802.3
MAC
PHY
802.1Q bridge relay
MAC
PHY
MAC
PHY
Non-AP station
end station

## Slide 9: So, another representation could be …
That is, the 802.1AC Clause 12.2.1 “portal convergence function” is not an interface to a portal; .1AC 12.2.1, plus a bridge relay function, is an example of a portal.
.1AC 12.2.1 connects the ISS to the DS_SAP.
Distrib. System (DS)
MAC
PHY
AP STA
unspecified
AP
802.1Q bridge relay
MAC
PHY
Non-AP station
MAC
MAC
802.3
PHY
PHY
end station
.1AC
One example (of many) of a portal

## Slide 10
New for 802.11ak consideration…

## Slide 11
MAC
PHY
MAC
PHY
PHY
MAC
AP STA 2
PHY
MAC
AP STA 1
Non-AP STAs
802.3
Extending this to P802.11ak + P802.1Qbz
MAC
PHY
802.1Q bridge relay
AP
AP
Conv.
Funct
CF
CF
SAP[ ]
SAP
SAP
CF
CF
SAP[ ]
SAP
SAP
That is, 802.1AC/802.11ak can define a SAP and a convergence function that supports multiple, logical links as seen by the Bridge, to each of the 11ak-aware non-AP endpoints.

## Slide 12: Tasks for 802.1AC
Rewrite 802.1AC Draft 0.2 Clause 12.2.1 to provide a convergence function that maps multiple, logical ports visible to the bridge, to the vector-of-endpoints SAP provided by an 11ak AP.

## Slide 13: Tasks for 802.11ak
Define the SAP presented by an 11ak AP to include the vector-of-endpoints parameter, which identifies links to each of the 11ak-aware non-AP STAs.