## Slide 1: Calibrating MAC Simulator Through Function Test
Name | Affiliations | Address | Phone | email
Jinjing Jiang | Marvell Semiconductor | 5488 Marvell Ln, Santa Clara, CA 95054 | 408-222-8651 | jinjing@marvell.com
Yakun Sun | Marvell Semiconductor |  |  | 
Liwen Chu | Marvell Semiconductor |  |  | 
Yan Zhang | Marvell Semiconductor |  |  | 
Hongyuan Zhang | Marvell Semiconductor |  |  | 
Lei Wang | Marvell Semiconductor |  |  | 
Hui-Ling Lou | Marvell Semiconductor |  |  | 
Date: 2014-05-11

## Slide 2: Status of Simulator Calibration: PHY
There has been a lot of progress in the calibration of PHY
  Details are already defined in [1]
  Long-term SINR calibration [2] aligned the implementation across different companies on
    Topology generation
    Generation of large-scale fading, shadowing
  Instantaneous SINR calibration is underway [3][4]
    Small-scale fading generation
    Simple MAC mechanism modeling: CCA or DCA

## Slide 3: Status of Simulator Calibration: MAC
Details and results are less discussed for MAC due to the complexity introduced by the network dynamics and options related to PHY
Existing proposed metrics:
  CDFs (throughput, the number of concurrent transmissions, etc.), event traces, PER logs [5][6]
Existing proposed setup:
  Starting from the simple setting [6], such as
    1 BSS with 2 STAs, and add more STAs later on
    Only with the simplest channel, fixed TxVector, etc
  Use the real scenario [1][5]

## Slide 4: A Reflection on Performance-Based MAC Calibration
Existing proposal: MAC calibration using system performance as a metric for a comprehensive or a simplified scenario.
Pros
  Easy to read and understand: %5 percentile throughput, mean throughput, …
Cons
  Time consuming to agree on the common set of parameters and calibration scenarios, and the final performance.
    How to abstract PHY? Who is right and who is wrong? And many etc…
  Cannot disentangle the mixing effects of various modeling method or modeling granularity
    Hard to identify the cause of possible differences.
  The system performance metrics could hide miscues of buggy implementation of MAC mechanism
    Two close curves do not necessarily mean two identical MAC behaviors.
    How to compare two numbers or two curves?  Need to answer how close, how much difference is tolerable, etc.

## Slide 5: An example: hard to tell whether 3 simulators are aligned/correct or not!
Who is right and who is wrong?  take a long time to debate
Are they close enough to be all right (aligned)?
Even they are aligned (with reasonable gaps), can we say MAC layers are calibrated?
Many more…

## Slide 6: Performance vs. Functionality
To ensure whether MAC works correctly (as close as possible), it is necessary to do function testing before looking at the performance metrics suggested by [5][6]
Our proposal: define tests restricted to MAC mechanisms to show it functions as expected
  Deterministic MAC test cases with deterministic test metrics.
  No need to run a full/lengthy simulation but only a small number of predefined events related to the function to test.
Testing tool: various traces such as
  Event timing traces (time stamps, sequence number, etc)
  MAC state traces
  Other types of traces: buffer/queue content…

## Slide 7: What is MAC simulator?
A piece of software controlled by simulator’s scheduler and MAC’s finite state machine (FSM)
IDLE
TX
BACK
OFF
Collision Detection/RETRY
CCA/NAV Wait
Medium is not busy during Access Request
TX is finished
Busy during backoff
Idle for IFS time
All other transmitted frames whether successful or not
Still in sequence and last step is successful
Backoff successful after AccessRequest
ACK is transmitted
Backoff successful after last TX

## Slide 8: Calibrating via MAC FSM
Calibrating MAC functionalities via MAC FSM test
  FSM states transition works as expected  MAC works properly in the network simulator.
Benefit of FSM-based MAC calibration:
  Minimum effort in defining the test cases and the desired metrics.
  Isolate MAC functions from PHY implementation and randomness in the system level
    NO need to configure the network (PHY, MAC, Application, Scenario)
    NO need to run a real simulation  NO lengthy waiting and data analysis
  Minimum effort in programming  reuse the existing ones that control the MAC FSM
Methodology of FSM test:
  A test case as a pre-configured series of virtual TX and RX event, for example:
    TX Event: Access Request function
    RX Event: RxStart and RxEnd function
    Backoff state: Initial Backoff counter, UpdateBackoff function
  Calibrating by checking related MAC FSM states at each time slot.
  One test case to cover one key MAC function

## Slide 9: Possible Test Targets
To constrain the workload of MAC test, design function test on key legacy MAC functions.
Example of key legacy MAC functions:
  CSMA
  Block Ack Mechanism
  A-MPDU
  ……

## Slide 10: Test Examples
Test Targets:
  CSMA backoff procedure
    Case 1: when the medium is busy in the middle of a backoff slot, the backoff counter should not decrease
    Case 2: when the packet is transmitted/received and NAV is set accordingly, …
    Case N: when…
  BlockAck procedure
    Case 1: BlockAck initialization
    Case 2: packet buffering at the receiver under BlockAck
    Case N: …
  A-MPDU
    Case 1: packet size after aggregation at the sender
    Case 2: …
  ……

## Slide 11: A Test Example using Timing Traces [7]
Slot Time | 9us
SIFS | 16us
AIFSN | 1
EIFS | 94us
An example for CSMA Backoff Procedure (Case 1)
  Suppose there are two receiving events and one channel access request
  It is important to design the backoff period to overlap with the two Rx events
Test setup:
  The following assumption on event time (us) and time unit satisfy the previous requirement
  Initial backoff counter = 4 slots
Event | Start Time (us) | Duration (us)
Rx | 20 | 40
Rx | 105 | 20
Access Request | 30 | 2
Test metric:
  The correct Tx time should be 168us
  The backoff counter should stop at 105us, restart at 150us

## Slide 12: A Test Example using Timing Traces (cont.)
Pseudo Code for the Test
The expected event traces are visualized as the following (us)
Rx
SIFS
AIFSN
Backoff 1
Rx
Backoff 2
SIFS
AIFSN
Backoff 3
Backoff 4
Tx
20
60
76
85
94
103
105
125
141
150
159
168
170
At 30ms, there is a request access, backoff counts are 4
Set SlotTime 9
Set SIFS 16
Set AIFSN 1
Set EIFS 94
AddRxEvent(20, 40) //(startTime, duration)
AddRxEvent(105, 20)
AddTxEvent(30, 2) //(startTime, duration)
SetBackoffCounter(30, 4)//(startTime, backOffSlots)
StartTest()
AIFS
Check point 1
Check point 2
Check point 3

## Slide 13: A More Complicated EDCA Test Example
An example test case for both CW evolution and NAV
  Correct behavior under NAV setting
  Correct CW and retry counter changes
Test setup
  One Tx events
    The first Access Request is unsuccessful with Ack Timeout
    The second Access Request is successful but deferred due to Rx
  Two Rx events, one for a packet, the other for the ACK for the previous packet
    To test the behavior under NAV, add NAV when each RX event happens

## Slide 14: An EDCA Test Example (cont.)
Test setup
  The assumption on event time (micro seconds) and time unit
Slot Time | 9us
SIFS | 16us
AIFSN | 1
Initial CW | 7
Initial Backoff | 0
Second Backoff | 2
Initial Retry Counter | 0
Event | Start Time (us) | Duration (us) | Ack Timeout (us)
Access Request | 0 | 20 | 20
Packet Rx | 55 | 20 | n/a
Ack Rx | 91 | 5 | n/a
Access Request | 94 | 20 | n/a

## Slide 15: An EDCA Test Example (cont.)
Test metrics
  CW values: 715
  Retry counter values: 01
  The correct timing under NAV: the AIFS starts at 96us
  * The above parameters can be set to test other cases such as the ssrc/slrc is reached

## Slide 16: An EDCA Test Example (cont.)
Pseudo Code for the Test
The expected traces are visualized as the following (us)
Tx
ACK
Rx
Backoff 1
SIFS
AIFSN
Backoff 2
Tx
0
20
40
56
55
75
112
91
96
130
139
159
Check point 1
Check point 2
Check point 3
Set SlotTime 9
Set SIFS 16
Set AIFSN 1
SetBackoffCounter(0, 0)//(startTime, backOffSlots)
AddTxEventWithAckTimeout(0, 20, 20) //(startTime, duration, timout)
AddRxEvent(55, 20) //(startTime, duration)
AddNavStart(65, 15) //(startTime, duration)
AddRxEvent(91, 5) //(startTime, duration)
AddNavStart(96, 0)//(startTime, duration)
SetBackoffCounter(40, 2)//(startTime, backOffSlots)
Print CW, RetryCounter
StartTest()
Override backoff counter instead of random drawing in [0, CW]
Ack Timeout
SIFS
121
NAV1 = 15
NAV2 = 0
At 55ms, receive a packet
Check point 4

## Slide 17: Observations…
Similar tests can be designed to check whether mechanisms such as EDCA behave as expected to a very detailed level using
  Timing traces
  SequenceNum traces, etc
Easy to check
  Purely model and feature oriented
      Verification according to the IEEE 802.11 specification
      Validation based on specific modeling requirement
  No randomness
  Independent of the selection of system parameters

## Slide 18: Summary
Suggestion 1: test MAC functionalities before testing system performance for MAC calibration.
Suggestion 2: MAC functionalities calibration via testing the MAC FSM states (and transitions).
Open to discussions on the idea and invite inputs on the test case design.

## Slide 19: Reference
[1] 11-13-1359-01-0hew-hew-evaluation-methodology
[2] 11-14-0336-00-0hew-calibration-of-long-term-sinr-for-system-simulator
[3] 11-14-0335-00-0hew-instantaneous-sinr-calibration-for-system-simulation
[4] 11-14-0307-00-0hew-phy-calibration-results
[5] 11-14-0356-00-0hew-calibration-of-system-level-simulators
[6] 11-14-0385-00-0hew-simulation-methodology-and-calibration
[7] ns-3 wifi test at http://code.nsnam.org/