## Slide 1: PHY Abstraction for and IEEE 11ax PHY System Simulation and Integrated System Level Simulation
Date: 2014-04-08
Authors:

## Slide 2: PHY Abstractions
ESM should not be correlated with channel types
  Pre-defined tables for different channels is not a viable solution because in a lot of scenarios, there is no pre-defined channels, i.e., beamformed channels, OFDMA.
  RBIR methods shown little correlation with channels [1-7]
ESM Accuracy
  PER v.s. effective SNR/SNR curves for different channels and bandwidths show that RBIR method is pretty accurate [1-7]
  Packet length can be derived from one typical packet length
  Modeling of practical (channel estimation etc.) loss will be discussed in the future
Implementation complexity
  Modulation dependent look-up tables require minimal additional complexity
  Complexities of all frequency domain processing ESM methods are similar

## Slide 3: Straw poll
Do you agree to use RBIR ESM as the PHY abstraction for PHY system simulation and integrated system level simulation for 11ax?
Y/N/A

## Slide 4: Reference
[1] “PHY Abstraction for HEW System Level Simulation”, IEEE 802.11-13/1131r0, Zhang Jiayin, etc.
[2] “PHY Abstraction for HEW System Level Simulation”, IEEE 802.11-13/0117r0, Yakun Sun, etc.
[3] “Suggestion on PHY Abstraction for Evaluation Methodology ”, IEEE 802.11-14/0353r0, Dongguk Lim, etc.
[4] “PHY abstraction comparison”, IEEE 802.11-14/0647, Tianyu Wu, etc.
[5]”PHY Abstraction for TGax System Level Simulations”, IEEE 802.11-14/0527, Ron Murias , etc.
[6]” Further Discussions on PHY Abstraction” IEEE 802.11-14/0581, Yakun Sun, etc.
[7]” PHY Abstraction for TGax System Level Simulations”, IEEE 802.11-14/0527, Ron Murias , etc.