## Slide 1: Spectrum allocation of 5.8/5.9 GHz band in Japan
Date: 2014-5-9
Authors:

## Slide 2: Abstract
This presentation provides current status of spectrum
allocation in 5770-5925 MHz in Japan.
5770-5850 MHz has been allocated for DSRC.
In this band, more than 60 million On Board Units (OBU) for Electronic Toll Collection (ETC) systems have been installed with vehicles.
RLAN is not permitted to operate in this band.

## Slide 3: 5.8/5.9 GHz band in Japan ETC + ITS Spot (5.8 GHz)
Source: Ministry of Land, Infrastructure, Transport and Tourism (Home page)
0
10
20
30
40
50
60
70
FY1999
2000
2001
2002
2003
2004
2005
2006
2007
2008
2009
2010
2011
2012
FY2013
ETC + ITS Spot
OBU: 60.5 million
ETC Utilization of highways:
89.2 ％ （7.4 million vehicle/day）
92.2 % Metropolitan Expressway
million
60,459,629
2,311

## Slide 4: 5.8/5.9 GHz band in Japan Spectrum allocations
Amateur
RLAN
Radar
Telecommunication Service
(Fixed Service)
Broadcasting
Service
(Fixed and
Mobile)
Telecommunication Service (Fixed Satellite)
RLAN
ISM
DSRC
Meteorological Radar
5150 MHz
5350
5850
5925
6425
5250
5470
5725
5770
5850
5875
6485
5650
Broadcasting Service
(Fixed and Mobile)
5372.5
Source: Ministry of Internal Affaires and Communication, April 2014

## Slide 5: 5.8/5.9 GHz band in Japan Channel allocations: ETC and ITS spot
Down Link
Up Link 0

## Slide 6: 5.8/5.9 GHz band in Japan Technical characteristics: ETC and ITS spot
Item | Technical characteristic | 
Carrier frequencies | 5.8 GHz band for downlink and uplink | 
RF carrier spacing (channel separation) | 5 MHz | 10 MHz
Allowable occupied bandwidth | Less than 4.4 MHz | Less than 8 MHz
Modulation method | ASK, QPSK | ASK
Data transmission speed (bit rate) | 1 024 kbit/s/ASK, 4 096 kbit/s/QPSK | 1 024 kbit/s
Data coding | Manchester coding/ASK, NRZ/QPSK | Manchester coding
Duplex separation | 40 MHz in case of FDD | 
Communication type | Transceiver type | 
Source: Recommendation ITU-R M.1453-2, June 2006

## Slide 7: 11ac on 5.8GHz
There is not any mechanism to prohibit the transmission by geographical location.
Country code is specified in .11, however the country code is not dynamically changed especially in the case of mobile router ( tethering on smart phone).
We may need some mechanism to use the 5.8GHz /5.9GHz capable product in Japan to protect existing DSRC.
Option 1
  Prohibit the use of 5.8GHz /5.9GHz capable product by law.
  In practice it is not possible to restrict user's operation by law.
Option 2
  Introduce dynamic changing mechanism of the country code. ( same as the TV White Space DB)
Option 3
  Introduce mandatory CCA on 5.8/5.9G band.

## Slide 8: Reference
11-13-0090-02-0reg-spectrum-allocation-for-wireless-lan-and-its-in-japan.pptx