## Slide 1: 11ah Tx Reference Code
Date: 2014-05-13
Authors:

## Slide 4: Introduction
Goal: to clear up any spec interpretation ambiguity and provide reference for implementation
  Tx Vectors can analyzed for correctness (spec compliance) and used for interoperability testing
  Vectors can be treated as Rx waveforms and be fed in to simulators for Rx processing and SIG/Data decoding verification
  Approach: Focus only on basic or mandatory 11ah modes (and deltas from 11ac system)
  1 and 2 MHz, short and long preamble formats
  BCC coding only
  Basic MCS set (up to 16QAM, MCS4), and especially MCS10 which is new 11ah feature
  Small and large packet size to cover separate length calculation formulas
  Include Ntx=2 case for long preamble to cover spec-mandated CSDs on Omni-part of preamble.
  See Appendix for table outlining proposed coverage
        Note that reference code published with this presentation is to be compatible to the spec as of 802.11ah Draft 1.1

## Slide 5: Interface description: Input to the waveform generation function
Use command line options to configure transmission; this can give a user flexibility to define various specific transmission configurations
  Minimum input parameter set to cover all the test-suites in the proposed coverage table
Input Parameter | Possible Value
BW_mode | '11ah_1MHz'or '11ah_2MHz'
IsShortPreamble | 1 : short preamble format, 0 : long preamble
MCS_idx | 0 - 10
pkt_size_bytes | 0 - … , can be any allowed packet size in spec
Ntx | 1 or 2
Nfft | must be larger than or equal to the base FFT size of the transmission BW, e.g. for 1 MHz mode, it can be 32/64/96 ..

## Slide 6: Interface description: Output to the waveform generation function
tx_params - derived parameters used in the packet generation
tx_packet - time domain baseband waveform after IFFT, adding GI, and windowing
  tx_testvector - test vector structure, which contains info bits or time domain symbols logged at each field along the Tx packet generation chain

## Slide 7: Interface description: Test Vector Structure for 1 MHz
Sub-fields name | Data and format
stf_t | 160 us time domain waveform of 1 MHz STF
ltf_t | 160 us time domain waveform of 1 MHz LTF
sig_bits | Information bit sequence of 1 MHz SIG field, dim of 1x36
sig_rep2 | Bit sequence after encoding and frequency repetition, dim of 6x24
sig_intlv | Bit sequence after interleaving, dim of 6x24
sig_t | 240 us time domain waveform of 1 MHz SIG

## Slide 8: Interface description: Test Vector Structure for 2 MHz Short Preamble
Sub-fields name | Data and format
short_stf_t | 80 us time domain waveform of 2 MHz STF with short preamble
short_ltf_t | 80 us time domain waveform of 2 MHz LTF with short preamble
short_sig_bits | Information bit sequence of 2 MHz SIG field with short preamble, dim of 1x48
short_sig_intlv | Bit sequence of 2 MHz SIG field with short preamble after interleaving, dim of 2x48
short_sig_t | 80 us time domain waveform of 2 MHz SIG with short preamble

## Slide 9: Interface description: Test Vector Structure for 2 MHz Long Preamble
Sub-fields name | Data and format
omni_stf_t | 80 us time domain waveform of 2 MHz omni-STF with long preamble
omni_ltf_t | 80 us time domain waveform of 2 MHz omni-LTF with long preamble
omni_siga_bits | Information bit sequence of 2 MHz omni SIGA field with long preamble, dim of 1x48
omni_siga_intlv | Bit sequence of 2 MHz omni SIGA field with long preamble, after interleaving, dim of 2x48
omni_siga_t | 80 us time domain waveform of 2 MHz omni SIGA with long preamble
d_stf_t | 40 us time domain waveform of 2 MHz data STF with long preamble
d_ltf_t | 40 us time domain waveform of 2 MHz data LTF with long preamble
sigb_t | 40 us time domain waveform of 2 MHz SIGB with long preamble

## Slide 10: Running the generator
This code has been tested with MATLAB v2011a. If you have any problems running it with different versions of MATLAB please let us know
Before running, you need to unzip the package ieee_tx11ah.zip attached in this document onto your working space.
Generate waveform: the function tx_waveform_11ah generates the baseband waveform.
  Example 1:
    % 1 MHz, MCS10, 32 bytes packets, 1 Tx antenna, 64-pt IFFT
    [tx_packet,tx_testvector] = tx_waveform_11ah('11ah_1MHz', 1, 10, 32, 1, 64)
  Example 2:
    % 2 MHz, long preamble, MCS3, 32 bytes packets, 2 Tx antenna, 64-pt IFFT
    [tx_packet,tx_testvector] = tx_waveform_11ah('11ah_2MHz', 0, 3, 32, 2, 64)
  Example 3:
    % 2 MHz, short preamble, MCS0, 512 bytes packets, 1 Tx antenna, 128-pt IFFT
    [tx_packet,tx_testvector] = tx_waveform_11ah('11ah_2MHz', 1, 0, 512, 1, 128)

## Slide 11: Code
Current as of TGah Draft 1.3
  Updated May 2014 to correct bug in Pilot Scrambling for Data field of 2MHz SU-MIMO Long frame.
    Pilot scrambling sequence index should start at “2” for SU-MIMO and “3” for MU-MIMO frames (Equation 24-50 in Draft 1.3).
    Previous version of code used “3” for both SU-MIMO and MU-MIMO frames
Embedded here as a zip file.

## Slide 12: Strawpoll
Do you agree to include the attached code with the next draft of the TGah specification as the Tx Reference code?
  Y - 11
  N - 0
  A - 0

## Slide 13: Appendix: Proposed Test-Suite Coverage
Frame Type | Nss | Nsts | MCS | Coding | Pkt Size (bytes, pre-padding) | GI Type | Ntx | Spatial Exp? | Comments
2MHz Short Data Frame | 1 | 1 | {0, 1, 3} (BPSK, QPSK, 16QAM) | BCC | 32, 512 | Reg. | 1 | N/A | Two packet sizes (small, large) to cover separate length calculation formulas
2MHz Long SU Data Frame | 1 | 1 | {0, 1, 3} | BCC | 32 | Reg. | 1, 2 | Yes, but no TxBF (i.e. Q=I) | Ntx=2 case: included to cover spec-mandated CSDs on Omni-part of preamble.
1MHz Data Frame | 1 | 1 | {10, 0, 1, 3} | BCC | 32 | Reg. | 1 | N/A | Cover new 11ah-specific MCS10 2xRepetition encoding/decoding