## Slide 1: Discussion of LB201 CID4609
Date: 2014-05-12
Authors:

## Slide 2: Abstract
Discussion of LB201 CID4609
The presentation compiles the LB198 comments that are quoted in LB201 CID4609.
The presentation is intended to stipulate a discussion in TGai on how to resolve the comment LB201 CID4609.
The presentation does not provide any suggested resolution text.
Revision 1 contains a proposed resolution as drafted by the task group on 2014-05-14 AM-2 slot.

## Slide 3: LB201 CID4609
Comment:
  My previous comments to D1.0 were not answered nor there was attempt to reconciliate the following CID to the commenter: 2762, 2763, 2764, 2766, 2767, 2769, 2773, 2774, 2775, 2776, 2777, 2779, 2783, 2786, 2787, 2792,
Proposed change
  <Proposed change field left blank. The commenter did not a proposed resolution.>

## Slide 4: Summary of LB198 (on D1.0) comments referred to in the new comment

## Slide 5: LB198 CID2762
Comment
  the filtering behavior described in the FILS Request Parameters is non indicative of the AP ability to support the probing STA connection's QoS requirements, it does limit the probability of other STA's relaying on the same Probe Req thus conflicting to the Probe Rsp broadcast add.
Proposed Resolution
  have all APs respond and select from within those and have the AP indicate the FILS criteria in the Probe Rsp, attempt association only to APs that qualifies. A multiple session can be executed to shorten time to association e.g. give a temporary add. or identifier to associate Probe Req, Rsp and association to a single STA.
Approved Resolution
  REJECTED. The Probe Response criterion is reducing the number of probe response messages and avoiding probe response storms and heavy large overhead. The STA has possiblity to request Probe response from all APs, but it may also reduce the probe response transmissions from APs that it is not interested.

## Slide 6: LB198 CID2763
Comment
  The type of PHY (HT/VHT) is non indicative of the AP ability to support the probing STA connection's QoS requirements, it does limit the probability of other STA's relaying on the same Probe Req thus conflicting to the Probe Rsp broadcast add. what happens when the next PHY is available? what about 11ad? what about the DS limitations as these may be (and in many time are) more limmiting than the last hop?
Proposed Resolution
  define resource requirement instead of PHY layer type.
Approved Resolution
  REJECTED. The 802.11ai saw value of keeping the HT and VHT fields. The commenter is not providing details of hte resource requirement mechanism.

## Slide 7: LB198 CID2764
Comment
  the usage model and use cases of 11ai are dense deployment and heavy load signaling and/or traffic. as a result a power measurement such as RCPI is not indicative and a CINR is more appropriate value.
  Regardless of that, the Active Scanning scenario is limited in statistics which to a couple of dozens of DB (+10DB) in pedestrian environments making it highly undesirable as metric for response conditioning.
  Please also note that in many of the PHYs the link budget changes drastically between discovery/association and actual data transfer thus using the RCPI metric of a single transmission is non indicative.
Proposed Resolution
  Remove RCPI as metric of channel conditions to when responding to Probe Req
Approved Resolution
  REJECTED (TGai General: 2013-09-19 11:34:46Z) - REJECTED. The RCPI value indicates that the AP is in proximity. Estimation of the interference is complicated and requires longer estimation time that is available in scanning.
  Typically the interference is in busy channel that may be detected from BSS Load and other values.
  The responding AP cannot know the interference level of the STA that transmitted the probe request. It is more essetial to know the interference in STA, because there are more DL traffic.
  However, the interference at the STA is less dependent on the selected AP, and therefore does not need to be taken into account.
  In summary, it is highly likely that the AP with strongest RCPI of the probe message also gives best channel quality for the communication

## Slide 8: LB198 CID2766
Comment
  Some of the conditions for response are not "information" but are conditions thus using the terminology "same information" is not well defined
Proposed Resolution
  clarify what information refers to.
Approved Resolution
  REVISED. The commenter is right that the information that is referred is not accurately defined. The informaiton is defined to be the SSID and the 10.1.4.3.3 conditions allow more responses to be transmitted as written in the submission https://mentor.ieee.org/802.11/dcn/13/11-13-1269-06-00ai-active-scanning-text.docx .

## Slide 9: LB198 CID2767
Comment
  Different STA may have drastic different channel conditions to a an AP while some of the conditions are spatial/channel related e.g. RCPI,
  minimum data rate. it is not possible to infer from the conditions of one STA to another.
Proposed Resolution
  Exclude spatial and channel related parameters for consideration as conditioing Probe Rsp from other parameters
Approved Resolution
  REJECTED (TGai General: 2014-01-20 21:50:18Z) --- 802.11ai task group has discussed extensively on the possibility to reduce the number of unnecessarily transmitted scanning frames, like Probe Requests and especially Probe Responses. The conclusion of these discussions is that avoiding Probe Response storms and improving the system performance of the WLAN is highly desireable.Especially in the dense deployments the number of Probe Response frame transmissions from the APs that have poor link to the requesting STA may be very high.
  The criteria to respond with Probe Response set rules on which responses the requesting STA is interested. The rules may define a link performance threshold, congestion threshold or capability thresholds. The use of the criteria depends on the scanning STA. It is likely that scanning STA uses the criteria, if it is aware of better candidate.
  The RCPI value indicates that the AP is in proximity. Estimation of the RCPI value from the Probe Request frame is already part of the 802.11 standard. In 802.11 standard the transmitter of the Probe Request may request that RCPI measurement is included to the Probe Response frame. The response criteria uses the very same assessment for RCPI.
  Also it should be noted that estimation of the interference is complicated and requires longer estimation time that is available in scanning. The interference based scanning or the transmission rate estimation have been deleted from the 802.11ai for the sake of clarity.
  Typically the interference is in busy channel that may be detected from BSS Load and other values.
  The responding AP cannot know the interference level of the STA that transmitted the probe request. It is more essetial to know hte interference in STA, because there is more DL traffic.However, the interference at the STA is less dependent on the selected AP, and therefore does not need to be taken into account. In summary, it is highly likely that the AP with strongest RCPI of the probe message also gives best channel quality for the communication

## Slide 10: LB198 CID2769
Comment
  the usage of "may" makes it possible for any of the following behaviors: 1.) Transmittal under dot11FILSActivated false. 2.) non trasmittal 3.) Other
Proposed Resolution
  clarify that the AP STA with dot11FILSActivated True has to transmit a probe response per 10.1.4.3.7 or per the behavior where dot11FILSActivated equal false.
Approved Resolution
  REVISED. The criteria when the FILS STA may transmit a Probe Response are defined in the 10.1.4.3.8. The clauses are simplified and made more clear by starting the clause 10.1.4.3.7 by defining which rules the responding STA should follow. The may in response condition was a general term and not precise enough. Similar to CID 2712.The text is shown in https://mentor.ieee.org/802.11/dcn/13/11-13-1269-06-00ai-active-scanning-text.docx .

## Slide 11: LB198 CID2773
Comment
  "the response" is non specific, e.g. if 2 or more Probe Requests received, which of the associated responses is refered to as "the response"?
Proposed Resolution
  Replace "the response" w/ one or more of the responses.
Approved Resolution
  REVISED. This CID can be superceeded by CID 2849. Proposed text is covered by contrution 1269r6. See merged text in https://mentor.ieee.org/802.11/dcn/13/11-13-1269-06-00ai-active-scanning-text.docx.

## Slide 12: LB198 CID2774
Comment
  paragraph section 10.1.4.3.8 allows for the omission of Probe Rsp even when the content of the Probe Rsp may not be identical due to different information requested by the Probe Req originator.
Proposed Resolution
  the text should reflect that omission of Probe Rsp is allowed only if the cancelled Probe Rsp messages are contained within the transmitted Probe Rsp message.
Approved Resolution
  REVISED.
  This CID can be superceeded by CID 2775. Proposed text is covered by contrution 1269r6. See merged text in https://mentor.ieee.org/802.11/dcn/13/11-13-1269-06-00ai-active-scanning-text.docx.

## Slide 13: LB198 CID2775
Comment
  This mechanism prevents the STA from discovering the AP with the best link budget conditions simply because another AP STA within the same SSID responded faster due to temporary medium and scheduling behavior. The AP has no ability to identify the link budget and channel conditions between STA transmitting the Probe Req and neighbor AP STA responding with Probe Rsp.
Proposed Resolution
  Remove mechanism
Approved Resolution
  REVISED.
  Commentor have a valid point that This mechanism prevents the STA from discovering the AP with the best link budget conditions.
  Proposed text is covered by contrution 1269r6. See merged text in https://mentor.ieee.org/802.11/dcn/13/11-13-1269-06-00ai-active-scanning-text.docx.

## Slide 14: LB198 CID2776
Comment
  At the AP side transmission Ques and scheduling makes it hard for the AP to follow, thus propose making it a MAY instead of a should.
Proposed Resolution
  Replace "should" with "may".
Approved Resolution
  REVISED
  Proposed text is covered by contrution 1269r6. See merged text in https://mentor.ieee.org/802.11/dcn/13/11-13-1269-06-00ai-active-scanning-text.docx.

## Slide 15: LB198 CID2777
Comment
  if the Probe Response Reception time element is not present the default value of MaxProbeResponseTime should be used. however this text is non specific as to what should the AP STA do in this case.
Proposed Resolution
  in case a the Probe Req from an 11ai STA did not include a Probe Response Reception Time Element, limit the AP to compare the time difference to the next TBTT to within the defualt MaxProbeResponseTime.
Approved Resolution
  REVISED (TGai General: 2014-01-22 05:21:15Z) - Revised.
  Note to commenter: Current text does not include behavior when the MaxChannelTime is not included in the Probe Request. The text is changed accordingly
  Instruction to editor: incorporate changes as specified in 11-14/0110r1 (Proposed resolution editing instructions, page 4-5)

## Slide 16: LB198 CID2779
Comment
  If the Probe Req included a Request Element and the AP STA responds with a Beacon instead of a Request Element the non AP STA does not receive fulfiling response.
Proposed Resolution
  if the request element is included in Probe Req, a directed Probe Rsp shall be used instead of the Beacon.
Approved Resolution
  REVISED.
  Comment is reasonable. Request element includes individual parameters as well as common parameters (e.g., RCPI)
  Proposed text is covered by contrution 1269r6. See merged text in https://mentor.ieee.org/802.11/dcn/13/11-13-1269-06-00ai-active-scanning-text.docx.

## Slide 17: LB198 CID2783
Comment
  Classify is not defined thus it is AP behavior not actionable.
Proposed Resolution
  Clarify what classify is in that context and the AP behavior as a result e.g. is there an indirect or direct indication of this?
Approved Resolution
  Revised.
  No action needed for editors, as the commented text was deleted by an accepted comment, #2851.

## Slide 18: LB198 CID2786
Comment
  Allowing the AP to classify other elements as dynamic makes the CCC mechanism obsolete as there is no indication/agreement between non AP STA and AP STA of what is a dynamic and static element in the beacon. As as result the a FILS STA receiving the CCC still has to compare each element within the beacon to identify which of the elements are preceived as dynamic or static by the AP.
Proposed Resolution
  Remove the lines 39,40 and/or specify the exact elements.
Approved Resolution
  Revised.
  No action is needed to resolve this comment, as the commented text is deleted as part of the comment resolution process.

## Slide 19: LB198 CID2787
Comment
  The procedure for FILS does not enable devices which are stringent on battery life to comply to the usage of FILS. Since most devices today are such, it 11ai misses on providing for its use cases.
Proposed Resolution
  Modify 10.1.4.3.2 to provide for AP discovery of PWR strangit devices
Approved Resolution
  REJECTED (TGai General: 2014-01-20 21:51:20Z) -- The comment fails to identify any problem or to propose any technical feature. 802.11ai is improving the scanning operation. Faster and more reliable scanning operation reduces the power consumption of the PWR strangit devices.
From Ad-Hoc-Notes:
  TGai General: 2013-11-11 23:34:59Z - Intensivly discussed. Group does not see that the comment does not provide a adoptable text that would satisfy the comment. The comenter was involved in the discussion and was asked to bring a presentation as a follow up to his comment which should identify why Tgai is not already solving the issue and what are the commenters technical ideas to address / solve his concerns.
  Tgai General: 2013-11-11 22:00:27Z - Discussed proposed resolutions during telecons on Oct. 8 & Oct. 15. Corresponding resolutions and text implementing the resolutions are contained in 11-13/1269r0 and in 11-13/1269r0 Feedback requested from the group to come up with a final revision for the next face-to-face meeting..

## Slide 20: LB198 CID2792
Comment
  There is no definition of what is the maximum duration between consecutive instance of FILS Dis. frame and between FILS Dis. and regular beacon. As a result a STA performing passive scanning cannot know what's the minimum duration it should expect for discovery of FILS AP.
Proposed Resolution
  Define the minimum duration either as fixed or as a set value Dot11MinFilsDiscDuration
Approved Resolution
  Reject.
  1. The proposed change of this comment is about define a min interval between FD-FD, and FD-Beacon. Actually, it is already defined, as dot11FILSFDframeBeaconMinimumInterval. See line 15 page 88 in 11ai/D1.0.
  2. the comment box of this comment is about definition of a max duration between FD-FD and FD-Beacon. It is actually not needed, as the max interval is bounded by beacon interval and the dot11FILSFDframeBeaconMinimumInterval.

## Slide 21: Summary

## Slide 22: Summary
All comments were addressed as part of the comment resolution process of LB198
Proposed resolutions provide of those CIDs that were rejected during LB198 contain the reasons for rejection and further explanation.
Some CIDs the current (LB201) comment quotes referred to text in TGai D1.0 that was deleted as part of creating D2.0
Exactly one comment made during LB198 was rejected for the reason that “The comment fails to identify any problem or to propose any technical feature. 802.11ai is improving the scanning operation. Faster and more reliable scanning operation reduces the power consumption of the PWR strangit devices.“ The corresponding ad-hoc notes indicate that the commenter was present in the discussion and was asked to provide a submission „as a follow up to his comment which should identify why Tgai is not already solving the issue and what are the commenters technical ideas to address / solve his concerns“. Such submission was not received.

## Slide 23: Proposed Resolution for LB201 CID4609
REJECT. All of the cited CIDs from the previous letter ballot were addressed and properly responded to (see document https://mentor.ieee.org/802.11/dcn/13/11-13-1076-34-00ai-tgai-lb-198-comments-for-d1-0.xlsx or https://mentor.ieee.org/802.11/dcn/14/11-14-0645-01-00ai-discussion-of-lb201-cid4609.pptx). For CID4609, no new suggested text or change was proposed.

## Slide 24: References