## Slide 1: AIDs Allocation for Relay
Date: 2014-06-17
Authors:

## Slide 2: Abstract
This presentation includes a proposal for Relay AID Allocation.

## Slide 3: Introduction
802.11ah supports two-hop relay operation.
Relay is assigned an AID by the associated Root AP ,and shall assign an AID to the non-AP STA associates with the Relay .
Relay must have assignable AIDs.
Relay may as well have different assignable AIDs from all other Relays and not in use at Root AP.

## Slide 4: Proposal
  Root AP manages globally the AIDs within its BSS ，and assigns operable AIDs to Relays associated to the Root AP.
  Root AP may assign unsolicited AIDs to Relays.
  Relay may request Root AP for more operable AIDs in the absence of AIDs；On the contrary，AIDs in surplus，Relay may return useless AID to Root AP.
  Root AP can retrieve the AIDs assigned to Relay.

## Slide 5: Operation procedure
When Relay STA associates with Root AP，Relay STA can request Root AP for operable AIDs，and Root AP assign AIDs to the Relay.
  If a non-AP STA associates with Relay AP, Relay AP assign an AID to the non-AP STA based on power management mechanism of the Relay、sleep mode of the non-AP STA.
After successful association , Relay may request Root AP for more operable AIDs；Root AP assign the most appropriate AIDs to the Relay base on previous assignment of AIDs to the Relay and currently assignable AIDs of the Root AP.
  Root AP may assign unsolicited AIDs to Relays.
  Relay may return useless AID to Root AP.
When Relay STA disassociates with Root AP，Root AP retrieves the AIDs assigned to Relay.

## Slide 6
This proposal designs one element and two Relay action frames，detailed format is as follows:
AID Pool Element
  When AID Pool Request/AID Pool Response subfield is set to 0，it indicates the request for AIDs and the subsequent subfield reserved ; set to 1, it indicates the AIDs assignment.
  Refer to hierarchical structure of traffic indication map[1].
Related Frame Format

## Slide 7
Relay AID Pool Request frame format：
Relay AID Pool Response frame format：
Frame Format cont.
Order | Information
1 | Category
2 | Relay action
3 | Dialog Token
Order | Information
1 | Category
2 | Relay action
3 | Dialog Token
3 | AID Pool element

## Slide 8
Straw Polls
SP1
  Do you support Root AP manages globally the AIDs within its BSS ，and assigns operable AIDs to Relays?
SP2
  Do you support the operation procedure of AIDs allocation?
SP3
  Do you support the related frame format?

## Slide 9: References
[1] IEEE P802.11ah™/D1.3, 2014