## Slide 1: P802.11REVmc Status and Overview
Date: 2014-06-24
Authors:

## Slide 2: Abstract
This document provides the status of work in IEEE 802.11 Task Group mc on P802.11REVmc (D3.0 as of June 2014) including
  A summary of amendment roll-in actions
  Added and updated functionality and
  Removed functionality
  Liaison activity

## Slide 3: TGmc status and Project Description
Slide 3
Status updates
  http://grouper.ieee.org/groups/802/11/Reports/tgm_update.htm
Revision Project Authorization Request (PAR)
  https://mentor.ieee.org/802.11/dcn/12/11-12-0594-02-0000-revision-par-proposal-for-802-11-2012.doc
Timeline
  http://www.ieee802.org/11/Reports/802.11_Timelines.htm
  Current publication date is Dec 2015; completion date very likely move into 2016
Notes: doc.: IEEE 802.11-10/0503r4
May 2010
        Michael Montemurro, Research in Motion
Page 3

## Slide 4: TGmc Plan of Record
Slide 4
20 July 2012 – 12 Sept 2012 – Call for Comment/Input
29-30 Aug 2012 – NesCom, SASB PAR Approval
Sept 2012 – Begin to process input
Sept 2012 – 11aa, 11ae integration
Jan – First WG Letter ballot - with 11aa, 11ae
Dec 2012 – March/May 2013 – 11ad integration
Sept 2013 – Letter ballot on D2.0
Dec 2013 – May 2014 – 11ac, 11af integration – D3.0 in May 2014
July 2014 – Mandatory Draft Review
Jul - Aug 2014 – Form Sponsor Pool (45 days)
Nov 14 – Initial Sponsor Ballot
July 2015– WG/EC Final Approval
Dec 2015 – RevCom/SASB Approval
Notes: doc.: IEEE 802.11-10/0503r4
May 2010
        Michael Montemurro, Research in Motion
Page 4

## Slide 5: P802.11REVmc is available in the IEEE Store
Publication | Draft in TechStreet | Draft in Members Area | Published in Get 802?
IEEE P802.11REVmc | D2.0 $500 pdf | 3.0 | 
IEEE Std 802.11af-2013 | $165 pdf |  | 
IEEE Std 802.11ac-2013 | $258 pdf |  | 
IEEE Std 802.11ad-2012 | $371 pdf |  | Yes
IEEE Std 802.11ae-2012 | $108 print |  | Yes
IEEE Std 802.11aa-2012 | $185 print |  | Yes
IEEE Std 802.11-2012 | $556 print |  | Yes
IEEE Std 802.11<x>: b, k, i, n, p, y, r, w, u, v, z, s | $100 - $309 |  | 
802.11-2007 |  |  | 
Notes: November 2011

## Slide 6: IEEE 802.11 Revisions
802.11k
RRM
802.11r
Fast Roam
a 54 Mbps
5GHz
b
11 Mbps
2.4GHz
d
Intl roaming
802.11V
Network
Management
802.11s
Mesh
802.11u
Interworking
External Networks
802.11Y
3650-3700 operation in USA
802.11n
High
Throughput
(>100 Mbps)
802.11W
Management
Frame
Security
802.11z
TDLS
802.11p
WAVE
802.11
-1999
PHY
MAC
802.11
-2012
802.11
-2007
802.11aa
Video Transport
802.11ae
QoS Mgt Frames
802.11ah
<1GHz
802.11ac
VHT
6Gbps @ 5GHz
802.11ai
FILS
802.11ad
VHT
6Gbps @ 60GHz
802.11af
TV Whitespace
802.11
-2003
g
54 Mbps
2.4GHz
e
QoS
i
Security
h
DFS & TPC
j
JP bands
f
Inter AP
802.11ak
General Link
802.11aj
40 & 60 GHz
802.11aq
Service Discovery
Notes: doc.: IEEE 802.11-11/0483r0
May 2011
        Bruce Kraemer (Marvell)
Page 6

## Slide 7: IEEE 802.11 Standards Pipeline
Slide 7
PHY
Sponsor
Ballot
MAC
Study
groups
Published
Standard
WG
Letter Ballot
802.11 -2012
802.11aa
Video Streaming
802.11ac
VHT 5GHz
TG without
Approved draft
Discussion Topics
Published
Amendment
802.11af
TVWS
802.11ai
FILS
802.11 ah
WNG
802.11ae
QoS Mgt Frames
802.11ad
VHT 60 GHz
PAD
802.11AQ
802.11aj
802.11-2015/6
GLK
802.11AK
802.11ax
60GHz
Enhancements
Notes: doc.: IEEE 802.11-11/0483r0
May 2011
        Bruce Kraemer (Marvell)
Page 7

## Slide 8: P802.11REVmc Amendment roll-in
IEEE Std 802.11aeTM-2012 Amendment 1: Prioritization of Management Frames
IEEE Std 802.11aaTM-2012 Amendment 2: MAC Enhancements for Robust Audio Video Streaming
IEEE Std 802.11adTM-2012 Amendment 3: Enhancements for Very High Throughput in the 60 GHz Band
IEEE Std 802.11acTM-2013 Amendment 4: Enhancements for Very High Throughput for Operation in Bands below 6 GHz
IEEE Std 802.11afTM-2013 Amendment 5: Television White Spaces (TVWS) Operation

## Slide 9: Changes other than amendment roll-in
Numerous editorial and style alignment changes
Numerous minor technical corrections, including to incorporated amendments
Updated MAC Data Service Architecture description, see clause 5.1.5 and https://mentor.ieee.org/802.11/dcn/13/11-13-0115-14-0arc-considerations-on-ap-architectural-models.doc
Addition of Fine Timing Measurement, an extension of Timing Measurement

## Slide 10: Process for removal and discouraging use of functionality
There is a staged removal process for functionality that is no longer used or recommended to be used (obsolete) and the ability to recommend non-use but still include definition (deprecate)
Remove: mark as obsolete in a revision
  “May be removed in a future revision of the standard.”
  Consider removal in subsequent revision
Recommend non-use: deprecate the functionality
  “Don’t use it unless you have a good reason to”

## Slide 11: Functionality marked “obsolete” in IEEE Std 802.11-2012
Frequency Hopping (FH) PHY (Clause 14)
Infrared (IR) PHY (Clause 15)
PBCC option in High Rate/DSSS PHY
ERP-PBCC option in Extended Rate PHY
SDL Formal Description (Annex J)
Term WDS (not removed in REVmc D3.0)

## Slide 12: Functionality present in P802.11REVmc and marked as obsolete
Use of Strictly Ordered Service Class
Point Coordinator Function (PCF mechanism)
Phased Coexistence Operation (PCO)
RIFS

## Slide 13: Functionality deprecated in P802.11REVmc
WEP, TKIP, Shared Key Authentication (deprecated in IEEE Std 802.11-2012)
Dual CTS protection mechanism
STBC Dual Beacon mechanism
Use of non-QoS CF-Poll frame by an AP to a QoS STA
Various MIB variables

## Slide 14: TGmc has discussed liaison related items
Liaison from IEEE 802.11 to WFA regarding use of non-OFDM rates, see https://mentor.ieee.org/802.11/dcn/14/11-14-0182-02-000m-liaison-to-wfa-on-reducing-use-of-cck-and-dsss.docx ; Liaison response from WFA expected for July 2014 meeting
Response from IEEE 802.11 to 3GPP liaison, see https://mentor.ieee.org/802.11/dcn/14/11-14-0519-00-0000-liaison-from-3gpp-on-rcpi.doc and https://mentor.ieee.org/802.11/dcn/14/11-14-0658-06-000m-liaison-response-to-3gpp-tsg-ran-wg2.docx

## Slide 15: Questions