## Slide 1: Dynamic Sensitivity Control Practical Usage
Date: 2014-June
Authors:

## Slide 2: Previous DSC Presentations
13/1012r4 Dynamic Sensitivity Control
13/1290r1 Dynamic Sensitivity Control
13/1487r2 Dense Apartment Complex DSC and CH Select
14/0045r2 E-Education
14/0058r1 Pico Cell
14/0294r2 DSC, Channel Selection and legacy sharing
14/0328r2 Dense Apartment Complex Throughput Calculations
14/0635r1 DSC Implementation

## Slide 3: Objectives
DSC basics
Interworking with Legacy networks/STAs
Practical aspects of setting DSC Margin and Upper Limit
How to use DSC

## Slide 4: Dynamic Sensitivity Control - DSC
Scheme where STA measures the RSSI of the AP Beacon (R dBm)
Sets RX Sensitivity Threshold at (R – M) dBm, where M is the “Margin”
  Example:
    STA receives Beacon at -50dBm, with Margin = 20dB STA sets RX Sensitivity Threshold to -70dBm.
Also set an Upper Limit, L, to Beacon RSSI to cater for case when STA is very close to AP.
  Need to ensure that all the STAs in the wanted area do see each other. Hence if one STA very close to AP, then it could set RX Sensitivity too high.
  Example:
    STA receives Beacon at -15dBm, L = -30dBm, M = 20dBm
    STA sets RX Sensitivity Threshold at -30 -20 = -50dBm (NOT –35dBm)
If the RX sensitivity threshold is higher than the CCA Threshold then CCA Threshold = RX Sensitivity Threshold

## Slide 5: DSC maintains full sensitivity
It is important to note the difference between DSC and simply setting the CCA Threshold or the RX sensitivity to a higher value
The chance of hidden STAs in the home network is greatly reduced
The DSC STA, maintains full range. The sensitivity will move towards lowest value as the STA moves away from the AP
See next Slide

## Slide 6: Hidden STAs – Fixed CCA vs DSC
DSC
Note NO hidden STAs

## Slide 7: DSC
ADVANTAGES
DSC can increase the area throughput by significant amounts
  296% improvement for Single Apartment Complex
  412% improvement for Double Apartment Complex
  800% improvement for Cell Structure network
DSC used in conjunction with channel selection can eliminate OBSS completely in dense apartment scenario
DSC does not require any hardware changes and is simple to implement
DSC can improve performance for all PHYs
DSC does not degrade the range of a STA
CONCERNS
Effect on legacy networks/STAs
How to set DSC parameters in unmanaged networks
  Avoid hidden STAs

## Slide 8
Legacy
(Discussed also in 14/0294)

## Slide 9: Legacy STAs and DSC STAs
A legacy STA in the same network as a DSC STA is completely unaffected by the DSC STAs.
The legacy STA may be held off from transmitting by STA in OBSS, but will compete equally with DSC STAs in same BSS
  As other DSC STAs will ignore OBSS STAs their traffic is often occurring during a time when the legacy STA cannot TX, and hence overall contention is lessened.

## Slide 10: Legacy DSC mix (11n 2SS 270Mbps 32k Agg, 100Mbps)
DSC Network with
2 DSC STAs
2 Legacy STAs
OBSS Network
4 Legacy STAs
DSC 100Mbps
Legacy ~22Mbps
Legacy ~22Mbps
Legacy STAs are not affected
BUT look at the DSC STAs!

## Slide 11: “Sharing” DSC and Legacy Networks
DSC
Legacy
Legacy Network
Overlaps with DSC Network
DSC Network does not
Overlap with Legacy Network

## Slide 12: DSC and Legacy STAs in apartment complex and cell cluster
DSC network sharing with a legacy network,
  DSC network does not see the legacy network
  Legacy network does see the DSC network
Legacy STAs will compete with own network STAs and with DSC STAs
DSC STAs just compete with DSC STAs
If Legacy STA wins it sends packet and completes even if DSC STA starts to transmit (DSC Margin is set to allow this)
If DSC STA starts a packet the Legacy STAs will hold off. As soon as DSC STA completes transmission all DSC and Legacy STAs will then compete for medium.
ALSO if DSC STA is transmitting when the Legacy STA completes its transmission, then the legacy STA will not hold off as CCA is now based on signal strength (i.e. -62dBm not -82dBm)

## Slide 13: Throughput Simulations
Legacy Sharing
DSC/Legacy Sharing
Legacy STAs unaffected
But look at the DSC!

## Slide 14: Throughput Simulations
Legacy Sharing
DSC/Legacy Sharing

## Slide 15: Legacy and DSC Simulation
Actually Legacy STAs are better off!!
DSC STAs are a lot better off
(incentive to use the feature, even by itself)
270Mbps 2SS 11n

## Slide 16
Unmanaged Networks

## Slide 17: Unmanaged Networks Questions
Can the AP know what the settings for Upper Limit and Margin should be?
How does a STA set its Upper Limit and Margin if AP does not provide the settings?
Points:
  DSC STA will revert to maximum sensitivity as it wanders away from its AP. DSC does not limit the range (unlike fixed CCA).
  Legacy AP will not be affected by having DSC STAs for DL traffic, BUT the Margin on the DSC STA will ensure that UL traffic can be coincidental with OBSS traffic.
  What is effect if DSC STA is outside the DSC contention area?

## Slide 18: DSC STA outside area
If All Legacy
Simply reverts to
‘legacy’ throughputs on
Overlapping STAs

## Slide 19: DSC STA outside of area (partially hidden)
Assuming legacy AP there is no undue effect if a DSC STA is outside the main area. It reverts to sharing with those it can see.
  It does get less traffic throughput
  BUT it equates to what it would get if all were legacy
Note: If DSC AP, then the DSC contention area may be defined and the “stray STA” is outside and hence not associated
Conclusion – there is no disadvantage (similar to a STA at range with CCA set at -82dBm)
This is important, as in an unmanaged network, it is possible to set DSC for a ‘general’ condition without undue danger

## Slide 20
Setting UL and Margin

## Slide 21: UL and Margin Settings
Enterprise or Managed Area Networks
  UL and M set the contention areas such that channel re-use provides for desired high data rates (as per the 7 segment analyses)
  Extremely powerful for the DSC STAs but, as shown, legacy STAs do not suffer c.f. what happens if no DSC STAs present.
  Good incentive for STA vendors to implement DSC

## Slide 22: UL and Margin Settings
Residential Service Provider
  In the dense apartment scenario DSC particularly useful, in this case relatively simple to know or preset the area. (DSC plus channel select effectively eliminates OBSS)
  In the house (townhouse or standalone) less chance of OBSS (assuming that channel select), and hence DSC settings can be lower.
  Could be preset based upon simple check list
    Size/type of property (e.g. apartment/house? Rooms? Floors?)
  Setting of UL and M may be set if prepared to carry out simple instructions
    Walk the (high data rate required) area.
    Walk the extremes (for DSC AP)
  Settings could be learnt - room for clever learning algorithms

## Slide 23: UL and Margin Settings
Dumb User, residential
DSC AP
  Learning algorithm?
    After say 1 week, AP ‘knows’ distribution of its STAs.
    May use DSC to ‘prioritize’, for example, its HD video STAs
    Use of internal Receive Sensitivity threshold probably ‘dangerous’
DSC STA
  No real danger to assume a setting such as -40dBm and 20dB. High probability of avoiding OBSS and always ‘in range’ as STA moves away from AP (this is a the major feature of DSC versus a fixed, higher, CCA threshold).

## Slide 24: Summary
For managed/enterprise area networks DSC has huge advantages and pretty simple to set up.
In residential networks DSC is particularly advantageous for the dense apartment scenario.
In practice the presetting of UL to -30/40dBm and Margin to 20/25dB would probably show significant advantages with respect to efficiency and OBSS.