## Slide 1: Proposed Resolution to CID 26, 27, 37, 38, 40-47, 49-53, 67-71, 114, 115, 118 and 124
Date: 2014-07-01

## Slide 2: Introduction
This presentation proposed the resolutions to Comment CID 26, 27, 37, 38, 40-47, 49-53, 67-71, 114, 115, 118 and 124 to Tgaj draft specifications D0.01 in CC12.
Incorporate changes to text proposal amendments after discussions during the presentation of IEEE 802.11-14/0862r0.

## Slide 3: Response to CID 26 (1/2)
CID 26
  "At the end of NP, the PCP/AP will switch from the large band to the intended small band." STAs don't have intentions. "Intend" is a bad word.
Suggested Remedy
  Reword in terms of specified state or signaling. For example: "At the end of NP, the PCP/AP will switch from the large band to the small band indicated by the xyz field in the abc frame.” Review all 14 instances of "intend" and reword to relate to specified states or signaling.
Accept in principle.

## Slide 4: Response to CID 26 (2/2)
Revised text
  “At the end of the GI (or the NP/BHI if the GI is not present), the AP or PCP shall be ready to transmit or receive frames on the 1.08 GHz operating channel indicated by the Channel Number field of the Dynamic Bandwidth Control element. ”

## Slide 5: Response to CID 27, 52 (1/2)
CID 27
  "Non-PCP/non-AP STAs that want to join". STAs don't have wants.
CID 52
  "and then follows the standard procedures" -- but this document will become part of the standard procedures!
  Suggested Remedy
  For CID 27: Express in non-anthropomorphic terms. e.g. "In order to do <x> a STA shall ...".
  For CID 52: Cite specific procedures or delete.
Accept in principle.

## Slide 6: Response to CID 27, 52 (2/2)
Revised text
  “If a non-AP or non-PCP CDMG STA receives a DMG Beacon frame from the CDMG AP or PCP with the BSSID equal to the BSSID of the BSS of which the STA is a member and with the DBC Option subfield of Dynamic Bandwidth Control element equal to 0, the STA shall switch to the 1.08 GHz operating channel indicated by the Channel Number field of the received Dynamic Bandwidth Control element to receive the DMG Beacon frame transmitted on the corresponding 1.08 GHz channel and follow the beamforming rules in 9.35 and the channel access rules in 9.33 within the 1.08 GHz channel. ”

## Slide 7: Response to CID 37
CID 37
  " fulfill individual logic channels" Eh? Clear as mud..
  Suggested Remedy
  Reword to intelligible English.
Accept in principle.
Revised text
  Delete this sentence in the revised text proposal.
  “A CDMG PBSS/infrastructure BSS shall use the following dynamic bandwidth control (DBC) mechanism when operating in the country which requires the support of variable bandwidth channels operation to mitigate interference between other CDMG and DMG BSSs.”

## Slide 8: Response to CID 38, 70 and 124 (1/2)
CID 38
  "each large frequency band" I think the terminology is wrong. Individual usable bits of a band are channels. I think you have channels of different width.
CID 70
  "Small Band" and "Large Band" is not a good way to name different bandwidth, 45GHz mmWave may use 540MHz bandwidth, beyond 11ad may use channel bonding to get a bandwidth >2.16GHz.
CID 124
  The terminology "small band" and "large band" is very confusing. Many people would consider 1.08 GHz a large band.

## Slide 9: Response to CID 38, 70 and 124 (2/2)
  Suggested Remedy
  For CID 38: Review terminology here. Small and large are poor names for things, because we always want smaller or larger in a later amendment. Consider using "single width channel" and "half width channel".
  For CID 70: change "Small Band" and "Large Band"to "CDMG 1.08GHz Band" and " CDMG 2.16GHz Band".
  For CID 124: Please find a more suitable terminology.
Accept in principle.
Revised text
  Replace “Large band” with “2.16 GHz channel”.
  Replace “Small band” with “1.08 GHz channel”.

## Slide 10: Response to CID 40
CID 40
  "the late coming" - not English.
  Suggested Remedy
  -> scanning.
Accept in principle.
Revised text
  Replace “the late coming” with “scanning”.

## Slide 11: Response to CID 41
CID 41
  "hearing" - wrong verb. STAs receive.
  Suggested Remedy
  -> "receiving“. Ditto throughout this subclause.
Accept in principle.
Revised text
  Replace “hearing” with “receiving”.

## Slide 12: Response to CID 42
CID 42
  " current frequency band " - there is no definition for this.
  Suggested Remedy
  -> "channel in which the PCP/AP operates".
Accept in principle.
Revised text
  “An AP or PCP operating the BSS on a 1.08 GHz channel shall periodically transmit DMG Beacon frames (8.3.4.1) on the 2.16 GHz channel that encompasses the 1.08 GHz channel on which the BSS is operating. ”

## Slide 13: Response to CID 43
CID 43
  " TSF timer to record" - timers don't record, but that aside, the sentence makes no sense to me.
  Suggested Remedy
  Reword in English.
Accept in principle.
Revised text
  “set a TSF timer to track the beacon interval (BI) on the encompassing 2.16 GHz channel (i.e. Channel 2).”

## Slide 14: Response to CID 44
CID 44
  "must set another“. Must is another bad word, disallowed by IEEE-SA except in certain contexts.
  Suggested Remedy
  Reword to avoid using this word. Do so throughout, except in the IEEE-SA boilerplate.
Accept in principle.
Revised text
  “The AP or PCP may also establish an independent beacon interval on its operating 1.08 GHz channel and set another TSF timer to track it.”

## Slide 15: Response to CID 45
CID 45
  " in order to not moving" - not English.
  Suggested Remedy
  reword.
Accept in principle.
Revised text
  Delete this expression in the revised text proposal.
  “The NPs/BHIs of the two APs or PCPs operating on adjacent 1.08 GHz channels within a 2.16 GHz channel may be arranged consecutively without interspaces to reduce the number of times they need to switch between transmitting and receiving frames on the 2.16 GHz channel and the 1.08 GHz channels.”

## Slide 16: Response to CID 46
CID 46
  " Note that due to the hardware diversity, different devices may have the different lengths of GIs." "may" is used to grant permission. "might" is used to express probability.
  Suggested Remedy
  Change "may" to "might".
Accept in principle.
Revised text
  “The determination of the length of the GI is implementation dependent.”

## Slide 17: Response to CID 47
CID 47
  "The synchronization can be fulfilled by TSF" - not English.
  Suggested Remedy
  Reword. Ditto at 27.07.
Accept in principle.
Revised text
  “maintain synchronization by adjusting its TSF to match the Timestamp field (8.4.1.10) in the received DMG Beacon frames transmitted in these NPs/BHIs.”

## Slide 18: Response to CID 49
CID 49
  " must abide the channel access mechanism " - not English.
  Suggested Remedy
  Reword.
Accept in principle.
Revised text
  “In the following medium time, the CDMG AP or PCP shall follow the rules in 9.33.6 to schedule the SPs or CBAPs for DMG non-AP or non-PCP STAs on the 2.16 GHz channel.”

## Slide 19: Response to CID 50
CID 50
  "After which, the PCP/AP confirms that the other one has ceased its services in the adjacent small band" - how does this have any normative effect?
  Suggested Remedy
  Delete cited sentence.
Accept in principle.
Revised text
  Delete this sentence in the revised text proposal because it is not a normative statement.

## Slide 20: Response to CID 51 (1/2)
CID 51
  "should also contain an Extended Schedule element to indicate the starting time and the length of the NP duration allocated for each PCP/AP within the large band, the length of BI duration after channel splitting, etc." You can't have a normative statement that includes "etc."
  Suggested Remedy
  Split into two statements, or delete the "etc."
Accept in principle.

## Slide 21: Response to CID 51 (2/2)
Revised text
  “The AP or PCP shall also send a Channel Splitting Response frame (8.5.23.5) or Extended Channel Splitting Response frame (8.5.8.30) to announce the target 1.08 GHz channel number to which it switches and the starting time of the first beacon interval on 2.16 GHz channel when the channel splitting begins through the New Channel Number field and the Channel Switching Count field of Channel Switch Announce element, the length of its beacon interval on 2.16 GHz channel after channel splitting through Beacon Interval field, and the time offset of the scanning AP’s or PCP’s beacon interval relative to the existing AP’s or PCP’s beacon interval on 2.16 GHz channel and the lengths of NP/BHI durations for both APs or PCPs on 2.16 GHz channel through the TBTT Offset field, the NP/BHI Duration and the Adjacent NP/BHI Duration fields of Dynamic Bandwidth Control element to the CDMG STA indicated in the Source AID field in the received Channel Splitting Request frame or Extended Channel Splitting Request frame.”

## Slide 22: Response to CID 53
CID 53
  " must abide two" - not English
  Suggested Remedy
  reword.
Accept in principle.
Revised text
  Delete this sentence in the revised text proposal.
  “the CDMG AP or PCP shall only schedule SPs or CBAPs with DMG non-AP or non-PCP STAs as the source or destination STAs in time periods which has been reported as available by the other CDMG AP or PCP through the Extended Schedule element in its DMG Beacon frames.”

## Slide 23: Response to CID 67
CID 67
  DBC mechanism is proposed only for CDMG
  Suggested Remedy
  change the title to "Dynamic Bandwidth Control Mechanism for CDMG".
Accept in principle.
Revised text
  “9.40 Dynamic bandwidth control mechanism for CDMG”

## Slide 24: Response to CID 68, 118 (1/2)
CID 68
  PBSS is a kind of BSS, it is better not to use "BSS/PBSS“
CID 118
  In many places in the doc, it is used "BSS or PBSS", "BSS/PBSS", etc. This notation is confusing, since a PBSS is also a BSS.
  Suggested Remedy
  For CID 68: change all the "BSS/PBSS" to "BSS" or" infrastructure BSS/PBSS". And apply the comments all over the spec.
  For CID 118: Please either use BSS if it includes all types of BSS, or PBSS (if it excludes infrastructure and IBSS).
Accept in principle.

## Slide 25: Response to CID 68, 118 (2/2)
Revised text
  Replace “BSS/PBSS” with “PBSS/infrastructural BSS” in the revised text proposal.

## Slide 26: Response to CID 69
CID 69
  can't find "option 1, 2, 3, 4" but "a, b ,c, d".
  Suggested Remedy
  change "option 1,2,3,4" to "option a, b, c, d".
Accept in principle.
Revised text
  Delete these expressions in the revised text proposal because we have restructured this section and will not to use these notations.

## Slide 27: Response to CID 71
CID 71
  The PCP/AP1 can reject the PCP/AP2's request for any reason, which is out of the scope of this spec. On the other side, is there any principle that the PCP/AP1 should follow to accept the request?
  Suggested Remedy
  please clarify.
Accept in principle.
Revised text
  We agree that the decision that the PCP/AP rejects the channel splitting request is implementation dependent. In the revised text proposal, we will not mention any reason for rejection.

## Slide 28: Response to CID 114
CID 114
  The CDMG Channel Bandwidth field only uses 1 bit?
  Suggested Remedy
  Make this field of 1 bit size, not 2. Better yet, define a new IE dedicated to 11aj behavior. See later comment.
Accept in principle.
Revised text
  We will define a new element called Dynamic Bandwidth Control element in the revised text proposal.

## Slide 29: Response to CID 115 (1/2)
CID 115
  Why is the CDMG Channel Bandwidth field needed? A STA that receives the DMG Beacon will automatically know the BW of the channel in which it received the DMG Beacon. Is it to indicate the BW after splitting? If so, this field is still incomplete, therefore unnecessary, since there is no signaling of the center frequency?
  Suggested Remedy
  Need to address the need of this field. It might be better to define a new IE specifically for 11aj. As part of that, a potentially better solution would be to use Channel Number instead of explicitly using BW+Center Frequency.
Accept in principle.

## Slide 30: Response to CID 115 (2/2)
Revised text
  We define a Channel Number field of Dynamic Bandwidth Control element contained in the DMG Beacon frame in the revised text proposal.
  The CDMG PCP/AP uses this field to notify the non-PCP/non-AP STAs the target 1.08 GHz channel on which it operates.

## Slide 31: Revised Text
The complete revised text proposal to resolve CID 26, 27, 37, 38, 40-47, 49-53, 67-71, 114, 115, 118 and 124 is provided in IEEE 802.11-14-0862r0.
Suggest to remove the changes in D0.01 and revised the text proposal according to IEEE 802.11-14-0862r0.

## Slide 32
THANK YOU