## Slide 1: Modifications to Simulation Scenarios and Calibration Process
Date: 2014-07-01
Authors:

## Slide 2: Overview
Proposed changes to simulation scenario details
  Discussions surrounding PHY calibration process led to identification of some unspecified details, as well as parameters requiring modification

## Slide 3: Antenna Gains
Current antenna gains are +2 dBi for AP and -4 dBi for STA
  Antenna gain reflects antenna efficiency and directionality
  Directionality is strongly dependent on link type (AP-STA, STA-STA, AP-AP) and implementation, so preference is to not include any directionality.
Proposal: Change antenna gains to +0 dBi for AP’s, -2 dBi for STAs
  Reflects lower efficiency at STA devices vs. AP devices, but not any directivity

## Slide 4: TX Power
Current TX powers are:
Proposal: Unified power levels of 15 dBm per STA antenna and 20 dBm per AP antenna, for all scenarios
  STA power limit also applies to STA device (i.e., phone) acting as soft AP
Scenario | STA TX Power | AP TX power
1 | 18 | 21
2 | 21 | 24 (total)
3 | 15 | 17
4 | 15 | 30 (total)

## Slide 5: Carrier Frequency
For the sake of simplicity we propose to ignore the minor path loss variation due to different carrier frequencies for different channels within a band (e.g., lower 5G versus upper 5G)
Proposal: For all channels within the 2.4 GHz band, the carrier frequency used to determine path loss shall be set to 2.4e9. Similarly, the carrier frequency shall be set to 5e9 for all channels within the 5 GHz band

## Slide 6: Wall Loss for Scenarios 1 and 2
Scenarios 1 and 2 specify loss per wall, but do not explicitly indicate how diagonally separated walls are to be treated
Proposal: total # walls = # walls in x-direction + # walls in y-direction
  i.e., diagonally separated apartments are considered to be separated by 2 walls

## Slide 7: Path Loss and Fading Model for Scenario 2
Currently 11nD and 11nB are listed as options for channel model, with 7 dB per office wall
  11nB and 11nD path loss models only differ in breakpoint distance: 5m vs 10m. 10m breakpoint appears more reasonable for a large office setting
  11nD fading model designed for a large office
Proposal:
  11nD path loss model (exponent of 2 up to breakpoint distance of 10m, exponent of 3.5 beyond), still with 7 dB per office wall
  11nD NLOS multipath model for all links, with iid log-normal shadowing (5 dB standard deviation) per link

## Slide 8: Path Loss and Fading Model for Scenario 3
Currently 11nB, 11nD, and ITU InH listed as options for channel model
  11nB and 11nD path loss models only differ in breakpoint distance: 5m vs 10m. 10m breakpoint appears more reasonable for a large office setting.
  ITU InH model may not be consistent with scenario
    Was designed for inter-site distance of 60m, compared to inter-site distance down to 17.3m for scenario
    Uses LOS up to 18 meters, and has 0.5 probability of LOS even for large distances
  11nD fading model designed for a large indoor space.
Proposal:
  11nD path loss model (exponent of 2 up to breakpoint distance of 10m, exponent of 3.5 beyond)
  11nD NLOS multipath model for all links, with iid log-normal shadowing (5 dB standard deviation) per link

## Slide 9: Minimum AP-STA distance
Scenarios 3 and 4 have a minimum x-y distance from AP of 1m and 10m respectively
  Minimum x-y distance to AP should be modeled only if physically motivated, e.g., assumption that AP tower prevents STAs from being directly underneath tower
  Minimum distance should be used in PL formulas to avoid negative path loss and to prevent unreasonably high RX powers
Proposal:
  Remove 1m minimum x-y distance for S3
  Distance-based PL always based on 3-D distance with minimum distance of 1 meter:
    PL(3-D distance) = max(PL at 1 meter, PL for 3-D distance)

## Slide 10: User dropping for scenarios 3 and 4, with reuse 1
Process for dropping STAs not precisely described for scenarios 3 and 4
  RSSI-based association means STAs do not necessarily associate to closest AP
Option 1: Get exact # of associated STAs per AP
  Drop STA randomly in 19 cell area and do RSSI based association
    If associated AP already has specified # of STAs, then throw away STA; else associate to that AP
  Repeat until every AP has correct # of STAs
Option 2: Variable # of associated STAs per AP, with average # equal to value in scenario document
  Drop all STAs in 19 cell area, and do RSSI based association per STA
  Each AP can have different # of associated STAs
Found that option 2 can lead to large variability in terms of # of STAs per AP
  Will likely require large # of drops in order to get different simulation results to match
  Distribution of RX power to associated AP same with either option 1 or 2
Proposal:
  Adopt option 1 for scenarios 3 and 4
  RSSI association performed based on distance-based path loss + loss + shadowing + antenna gain, but not on multipath

## Slide 11: User dropping for scenario 3, reuse3
Two options for dropping STAs in reuse 3 version of scenario 3:
  Option 1: drop STAs in full 61 cell area, perform RSSI-based association to one of 61 AP’s, only keep STAs that associate to one of 19 reuse3 cells. Repeat process until have desired # of STAs per 19 reuse3 cells.
  Option 2: drop STAs uniformly in 19 reuse3 cells, perform RSSI-based association to one of 19 reuse 3 AP’s. Repeat process until have desired # of STAs per 19 reuse3 cells.
Option 1 is consistent with an actual reuse3 deployment in which STA associates to any AP.
  Investigation showed that using option 2 rather than option 1 changes distribution of RX power and STA locations
Proposal: Adopt option 1 for reuse 3 version of scenario 3
BSS
BSS
BSS
BSS
BSS
BSS
BSS
BSS
BSS
BSS
BSS
BS
BSS
BSS
BSS
BSS
BSS
BSS
BSS

## Slide 12: System Simulation Calibration Details
Further detail on a few points regarding System Simulation Calibration section of 802.11-14/0571
Proposal: All calibration simulations shall be conducted in the 5 GHz band with 80 MHz channels (channelization specified within each scenario)
Proposal: Clarify that transmit power for Box 1 is the per-antenna power
  Box1 of system simulation calibration (in 571r2) is based on long-term path loss (distance-based path loss + shadowing + wall/floor/penetration loss), and should correspond to single antenna transmission by all devices
Proposal: Specify CCA level of -70 dBm for Box 2, Test 3, and that CCA is measured across the entire bandwidth.
  Value chosen to provide an intermediate level of interference
Proposal: Clarify that there is no notion of an un-associated STA (i.e., user that cannot bi-directionally sustain minimum MCS) for the purpose of calibration

## Slide 13: Summary of Proposed Changes
Antenna gains for all scenarios: +0 dBi for AP’s and -2 dBi for STAs
TX power levels for all scenarios: 15 dBm per STA antenna and 20 dBm per AP antenna
Carrier frequency used in path loss formulas: 2.4e9 for all channels within the 2.4G band, 5e9 for all channels within the 5G band
# Walls for Scenarios 1 and 2 = # of walls in the x-direction plus # of walls in the y-direction
Scenario 2 channel model
  11nD path loss model (exponent of 2 up to breakpoint distance of 10m, exponent of 3.5 beyond), with 7 dB per office wall
  11nD NLOS multipath model for all links, with iid log-normal shadowing (5 dB standard deviation) per link
Scenario 3 channel model
  11nD path loss model (exponent of 2 up to breakpoint distance of 10m, exponent of 3.5 beyond)
  11nD NLOS multipath model for all links, with iid log-normal shadowing (5 dB standard deviation) per link
Remove minimum x-y distance of 1 meter from scenario 3, and for all scenarios distance-based path loss evaluated based on the maximum of 1 meter and the actual 3-D distance?
STA dropping process for scenarios 3 and 4 with reuse 1
  Drop STA randomly in 19 cell area and do RSSI based association (RSSI association performed based on distance-based path loss + loss + shadowing + antenna gain, but not on multipath)
    If associated AP already has specified # of STAs, then throw away STA; else associate to that AP
  Repeat until every AP has correct # of STAs
STA dropping process for scenarios 3 with reuse 3
  Drop STAs in full 61 cell area, perform RSSI-based association to one of 61 AP’s, only keep STAs that associate to one of 19 reuse3 cells which have fewer than the specified # of associated STAs. Repeat process until have desired # of STAs per 19 reuse3 cells.
Calibration process:
  All calibration simulations in 5 GHz band with 80 MHz channels
  Add clarification that transmit power for Box 1 is the per-antenna power
  For Box 2 test 3, use CCA level of -70 dBm with CCA measured across the entire bandwidth.
  Add clarification that there is no notion of an un-associated STA for the purpose of calibration

## Slide 14: Straw Poll
Do you agree to the changes specified in slides 3-13?