## Slide 1: Packet Length for Box 0 Calibration
Date: 2014-07-14
Authors:

## Slide 2: Introduction
In evaluation methodology document [1], we have five boxes for system simulation calibration
  Particularly “Box 0” is for “PHY abstraction calibration”
During the May 2014 meeting, RBIR is agreed to be used as a PHY abstraction method [2]
RBIR method is utilizing AWGN reference curves for accurately predicting packet error rate (PER)
Remaining issue of “Box 0” or “PHY abstraction calibration” is how to estimate PER for various packet length in an efficient way

## Slide 3: Recap: PHY Abstraction Method [3]
Calculate the effective SINR (SINReff) based on PHY abstraction method
where SINRn is the post processing SINR at the n-th subcarrier, N is the number of symbols for a coded block or the number of data subcarriers used in an OFDM system, and Φ is Effective SINR Mapping (ESM) function
Reference the AWGN link performance of a transmitted packet length to obtain the mapping between SINR and packet error rate (PER)
Use the SINReff obtained in Step 1 and the mapping obtained in Step 2 to derive the mapping between SINReff and PER

## Slide 4: Various Packet Length
Different packet lengths provide different PER performances
Ideally, we need to have AWGN curves for all possible packet lengths
Practically, we can consider the following approach for simplicity
  Generate set of reference curves and perform interpolation for different packet sizes [4]
  Estimate PER based on a reference curve and estimation function [5] [6]
  estimation function: PERPL = 1-(1-PERPL0)PL/PL0

## Slide 5: Considerations on Length of Reference Curves (1/2)
  Small number of reference curves are always preferable
Function based approach can be used with smaller number of reference curves
However, function based approach has some problem when PL/PL0 is too small or too large, for example
  If PL/PL0 is 0.1 and PERPL = 0.9, then PERPL0 should be 0.9999999999 which requires at least several trillion simulations for reference curve generation
  If PL/PL0 is 100 and PERPL = 0.01, then PERPL0 should be 0.0001 which requires at least several million simulations for reference curve generation
As you can see from above examples, the accuracy of the estimation function is more vulnerable to smaller packet length

## Slide 6: Considerations on Length of Reference Curves (2/2)
  We propose two size reference curves for BCC and one reference curve for LDPC
    Note that usually BCC is used for small length packet
  For a short length BCC reference curve, we propose 32 byte to represent an ACK frame
  For a long length reference curve (both BCC and LDPC), we propose a number that will be more suitable for LDPC coding
  The smallest number of bits that avoids puncturing in the process of LDPC is 58320bits but it leads to a high number
  We propose to divide it by 5 to get 11664bits=1458bytes which leads to integer number of codewords for all but the 5/6 rate - [12 9 8 and 7.2] codewords for those coding rates
  Note that 1458 also nicely corresponds to an Ethernet packet length

## Slide 7: Impact of Reference Curve Length
  As you can see from the figure, 400 bytes is a good candidate for switching between 32bytes reference curve and 1458bytes curve
32bytes
400bytes
From low SNR inaccuracy
From high SNR inaccuracy, after this point, we need extrapolation for curves from 32bytes

## Slide 8: Performance Verification (MCS0)

## Slide 9: Performance Verification (MCS9)

## Slide 10: Conclusion
  In this contribution, we proposed reference packet length for “Box 0: PHY abstraction calibration”
  For packet length PL, estimating PERPL from following equation
  PERPL = 1-(1-PERPL0)PL/PL0
  In case of BCC, PL0 is 32bytes for less than 400bytes and 1458bytes for other sizes
  In case of LDPC, PL0 is 1458bytes for all packet sizes
  We showed that proposed reference packet lengths are accurately estimates performance for various packet size

## Slide 11: Motion
  Motion to include the following text in evaluation methodology document
  For packet length PL, estimating PERPL from following equation
  PERPL = 1-(1-PERPL0)PL/PL0
  In case of BCC, PL0 is 32bytes for less than 400bytes and 1458bytes for other sizes
  In case of LDPC, PL0 is 1458bytes for all packet sizes
  Yes:
  No:
  Abs:

## Slide 12: Reference
[1] 11-14/0571r2, “11ax Evaluation Methodology ”
[2] 11-14/0585r5, “PHY Abstraction for and IEEE 11ax PHY System Simulation and Integrated System Level Simulation”
[3] 80216m-08/004r5, “IEEE 802.16m Evaluation Methodology Document (EMD)”
[4] 11-13/1059r0, “PHY Abstraction for HEW Evaluation Methodology”
[5] 11-14/0043r2, “PHY abstraction in system level simulation for HEW study”
[6] 11-14/0647r2, “PHY abstraction method comparison”