## Slide 1: Overview on RBIR-based PHY Abstraction
Date: 2014-07-15
Authors:
Name | Affiliations | Address | Phone | email
Yakun Sun | Marvell Semiconductor | 5488 Marvell Ln, Santa Clara, CA 95054 | 1-408-222-3847 | yakunsun@marvell.com
Nihar Jindal | Broadcom |  |  | 
Ron Porat |  |  |  | 
Jiayin Zhang | Huawei |  |  | 
Fei Tong | Samsung |  |  | 
Wookbong Lee | LG |  |  | 
Jianhan Liu | MediaTek |  |  | 
Tianyu Wu |  |  |  | 
Bin Tian | Qualcomm |  |  | 
Bo Sun | ZTE |  |  | 

## Slide 2: Introduction
    Received Bit Mutual Information Rate (RBIR) ESM has been well studied for PHY abstraction [1-10].
    It has been agreed to use RBIR ESM as PHY abstraction for PHY and integrated system simulation [11].
    The current EMD [12] needs updates to provide RBIR PHY abstraction procedure and lookup tables.
    An overview on RBIR PHY abstraction is presented here (also included the RBIR lookup tables).

## Slide 3: RBIR ESM Function
RBIR ESM is the symbol level mutual information conditioned on the M-QAM.
ESM function is defined as (given the SINR for a tone)
  Assuming coded modulation (CM)
  where U is a zero mean complex Gaussian random variable with variance 1, i.e., U~CN(0,1).
RBIR is the average symbol level mutual information for a transmission of Nss spatial streams over N tones and T OFDM symbols.

## Slide 4: Procedure of RBIR PHY Abstraction
RBIR PHY abstraction is done by:
  Step 1: Generate (both desired and interfering) channels.
  Step 2: Calculate the equalizer-output SINR per spatial stream for the n-th tone/t-th OFDM symbol, SINR(iss,n,t), iss=1…Nss.
    Equalizer is MRC if Nss=1, or MMSE if Nss>1.
  Step 3: Map N×T×Nss SINRs to 1 RBIR
  Step 4: Reverse map 1 RBIR to 1 effective SNR

## Slide 5: Procedure of RBIR PHY Abstraction (2)
  Step 5: Estimate the PER for this transmission
    Selection of reference packet length is defined in [10].
  Step 6: Determine if this transmission is successfully received based on PER.

## Slide 6: Procedure of RBIR PHY Abstraction (3)
Step-by-step diagram of PHY abstraction (except for channel generation).
  Step 1-2 are more time-consuming and can be simplified; step 3-5 are very efficient.
  Note SINR per-OFDM symbol is calculated even for slow-fading channels if interference levels change across the duration of the transmission.

## Slide 7: Lookup Table for RBIR ESM
Real-time calculation of RBIR mapping (Φ function) is time consuming.
RBIR LUT can be used in this place for quick implementation.
  1 LUT for each modulation  5 LUTs for all current defined modulations.
For a PHY packet with a fixed MCS, only 1 LUT is loaded for PHY abstraction (PER prediction).

## Slide 8: RBIR PHY Abstraction Using LUT

## Slide 9: Link Adaptation Using LUT
Channel-aware link adaptation can also use RBIR-based PER prediction.
  Iterate over all MCS to predict performance for each MCS via RBIR.
For example, genie max-rate link adaptation:
  Suppose the SINR for each tone and each OFDM symbol is known.
  For mcs = 0 to 9
    Step 1: Map SINRs into SNReff for the corresponding modulation
      1 out of 5 RBIR LUTs each iteration
    Step 2: Predict PER based on SNReff for the corresponding MCS
      1 out of 10 PER LUTs each iteration
    Step 3: R(mcs) = (1-PER) * rate(mcs)
  Select MCS* = argmax_{mcs=0…9} R(mcs)

## Slide 10: What is Needed in EMD for RBIR?
LUT for RBIR ESM mapping and AWGN PER.
  5 RBIR LUTs
  10 PER LUTs for BCC/LDPC respectively for each reference packet length.
  LUTs are provided in [14].

## Slide 11: Further Works
Impact of implementation loss
  Channel estimation error (e.g., [5,13])
  Impact of excessive long channels for outdoor scenarios (ISI/ICI)
  Other practical impairments (CFO/timing/PN…)

## Slide 12: Straw Poll
Include the procedure of PHY abstraction in slide3-4 into EMD
Y:
N:
A:

## Slide 13: References
IEEE 802.16m-08/004r5, “IEEE 802.16m Evaluation Methodology Document”
3GPP TR 25.892 V2.0.0 “Feasibility Study for OFDM for UTRAN enhancement”, June 2004.
11-14-0117-00-0hew-PHY-abstraction-for-HEW-system-level-simulation
11-13-1131-00-0hew-phyabstraction-for-hew-system-level-simulation
11-14-0353-00-0hew-suggestion-on-phy-abstraction-for-evaluation-methodology
11-14-0043-02-0hew-PHY-abstraction-in-system-level-simulation-for-HEW-study
11-14-0335-00-0hew-instantenous-sinr-calibration-for-system-simulation
11-14-0581-00-00ax-further-discussion-on-phy-abstraction
11-14-0647-02-00ax-phy-abstraction-comparison
11-14-0803-01-00ax-Packet-Length-for-Box-0-Calibration
11-14-0585-05-00ax-phy-abstraction-types-for-11ax-system-level-simulation
11-14-0571-02-00ax-evaluation-methodology
11-14-0810-00-00ax-RBIR-based-phy-abstraction-with-channel-estimation-error
11-14-873-00-00ax-PHY-Abstraction-Tables-for-11ax-System-Level-Simulation