## Slide 1: Discussion on dual-link STR in IEEE 802.11ax
Date: 2014-07-13
Authors:

## Slide 2: Introduction
In-band STR is emerging as a novel technique which could lead a great throughput enhancement
In order to meet the level of enhancement in IEEE 802.11ax PAR, in-band STR is expected to play a key role
  4(~10) times greater
  However, feasibility and effective throughput enhancement need further study
Especially, Dual-link setup could be one of the most crucial procedure defining the time average throughput enhancement
Along with technical analysis, it is a good time to setup a plan for STR in 802.11ax

## Slide 3: Summary of Previous Contributions
A number of H/W level approaches implementing STR on 802.11.
  Up to ~110dB Self Interference Cancellation(SIC) was achieved by antenna, analog and digital cancellation. [1]
Reference | Cancellation (dB) |  |  | Total (dB)
 | Antenna | Analog | Digital | 
Rice | 39~45 | 31~33 |  | 78~80
Stanford(1) | 30 | 20 | 10 | 60
Stanford(2) |  | 60 | 50 | 110
NEC | 55 |  | 20 | 75

## Slide 4: Summary of Previous Contributions
MAC level approaches to solve potential problems in applying STR to 802.11 networks
  Protocol adjustment
    Modifying DCF[6], [2], [5], PPDU preamble[3]
    Proposing a new protocol[4]
    Modifying ACK mechanism
  Fairness problem between Legacy and STR devices
    Utilizing EIFS [5]
Considering the H/W and protocol level advances, STR could be feasible for IEEE 802.11ax.
Notes: Many protocol have been developed

## Slide 5: Dual-link setup for STR
Can STAs perform STR for every single transmission?
  depends on whether there exists any proper STR candidate
Conditions for dual-link setup
  One of the primary link members might initiate secondary link
  Secondary link must not interfere the primary transmission
  There must be an available pair-wise data between the secondary link members at the desired transmission time

## Slide 6: Expected form of dual-link
The Best dual-link setup is to decide the best secondary pair
  The efficiency of dual-link setup might determine the level of overall throughput enhancement of STR
Expected forms of dual-link setup
  Pair-wise form (A↔B, B↔A)
    Much simpler to initiate the secondary link
    All STR participants must be STR-capable (SIC)
  3-node form (A↔B, B↔C)
    Requires further information to setup the secondary link
    Not every STR participant have to be STR-available (but STR-awareness)
  Push & Pull
    Push: Primary RX initiates dual-link
    Pull: Primary TX initiates dual-link

## Slide 7: Pair-wise form (Push)

## Slide 8: Pair-wise form (Pull)

## Slide 9: 3-node form (Push)

## Slide 10: 3-node form (Pull)

## Slide 11: Insights for dual-link setup
APs are highly expected to be the second link initiator
  Considering functional difference between AP and mobile STA
2 phased approach can be expected
  Phase1) 3-node form (AP centric)
  Phase 2) Unrestricted form(3-node form + pair-wise)
Methods for designing dual-link setup schemes
  Coordination-oriented
    Feedback
  Opportunistic
  Hybrid

## Slide 12: STR Protocols in terms of dual-link setup
ContraFlow[2]: Unrestricted, Push, Opportunistic
  Weighted value table: Proportion of successful secondary transmission in the past
  Pros: no overhead, relatively simple
  Cons: table setup time, opportunistic dual-link setup, unstable at highly mobile and dense network

## Slide 13: STR Protocols in terms of dual-link setup
Simplified STR[3]: 3-node form, Push & Pull, Hybrid
  Coordination, when the primary link is DL
    Interference/buffer status feedback from STAs
  Opportunistic, when the primary link is UL
  Pros: relatively simple, little modification of existing MAC
  Cons: the amount of feedback could vary severely depending on the mobility and density of network(feedback mechanism is not specified

## Slide 14: STR Protocols in terms of dual-link setup
Janus[4]: Unrestricted, Pull, Coordination-oriented
  Probe & Collection
  Full scale feedback
    Polling, measured interference level, transmission length
  Pros: coordination gain
  Cons: high overhead, whole new signaling design, high variance of coordination gain, feedback delay

## Slide 15: STR Protocols in terms of dual-link setup
FD-MAC[5]: Pair-wise, Pull, Opportunistic
d-STR[6]: Pair-wise, Push & Pull, Opportunistic
  existing RTS/CTS, BA based opportunistic STR
  Pros: Simplest, no feedback
  Cons: pair limited, opportunistic

## Slide 16: Conclusion
Dual-link setup is important to fully exploit the spectral efficiency gain of STR
Categories of dual-link setup
  Form: (Pair-wise, 3-node, Unrestricted form), (Push, Pull)
  Method: (Coordination-oriented, Opportunistic, Hybrid)
There is no definite solution for dual-link setup, so far.
Further discussions are necessary to take advantage of STR in 802.11ax

## Slide 17: Straw Polls (1)
Should in-band STR feature be considered in 802.11ax (including adoption as an optional feature)? (Y/N/A)

## Slide 18: References
IEEE 802.11-13/1122r1, “Considerations for In-Band Simultaneous Transmit and Receive (STR) feature in HEW”
Singh, Nikhil, et al. "Efficient and fair MAC for wireless networks with self-interference cancellation." Modeling and Optimization in Mobile, Ad Hoc and Wireless Networks (WiOpt), 2011 International Symposium on. IEEE, 2011
IEEE 802.11-14/0340r0, “A Simplified Simultaneous Transmit and Receive MAC Proposal”
Kim, Jae Young, et al. "Janus: A novel MAC protocol for full duplex radio." CSTR July (2013)
Duarte, Melissa, et al. "Design and characterization of a full-duplex multi-antenna system for WiFi networks." (2012)
Choi, Y., and Hooman Shirani-Mehr. "Simultaneous transmission and reception: Algorithm, design and system level performance." (2013): 1-19