## Slide 1: Discussion on OFDMA in IEEE 802.11ax
Date: 2014-07-13
Authors:

## Slide 2: Introduction
OFDMA has been already studied as one of multiple access schemes in 802.11ac.
In IEEE 802.11ax PAR [1], IEEE 802.11ax should provide methods for efficient use of spectrum resources in dense STAs per BSS.
  Make more efficient use of spectrum resources in scenarios with a high density of STAs per BSS.
In IEEE 802.11ax PAR [1], IEEE 802.11ax should also support OBSS scenarios and increase spectral frequency reuse in dense STAs and APs environments.
  Significantly increase spectral frequency reuse and manage interference between neighboring overlapping BSS (OBSS) in scenarios with a high density of both STAs and BSSs.
Therefore, OFDMA should be studied in two aspects: efficient use of spectrum resources and spectral frequency reuse.

## Slide 3: Summary of OFDMA contributions
Legacy devices decrease channel usage in wideband 802.11 system.
[2] shows that OFDMA can solve channel usage problem in mixed clients environment
DL-OFDMA increase AP utilization and throughput dramatically
Feasibilities of OFDMA were discussed in [3].
Some issues are considered as feasible, but others need more discussion.
Feasible | Need more discussion
DL-OFDMA | UL-OFDMA
Primary channel based access | Preferred channel based access
20MHz sub-band | <20MHz sub-band
Minimize scheduling overhead | 
ETC | 

## Slide 4: Considerations on OFDMA
OFDMA is feasible and needed for IEEE 802.11ax
  however, there are some considerations and issues to adopt OFDMA
OFDMA techniques in unmanaged dense AP and STA environment
  Fairness among 802.11ax BSSs, fairness between 802.11ax BSSs and legacy BSSs
  Performance evaluation of mixed device(Legacy and 802.11ax)
  Overall performance and efficiency in multiple BSS and OBSS scenarios (throughput/area)
OFDMA scenarios
  Both AP and STA support OFDMA : channel access is main issue
  Only AP support OFDMA : channel access is main issue
OFDMA considerations in two aspects
  efficient use of spectrum resources: Consideration #1 ~ 6
  spectral frequency reuse: Consideration #7

## Slide 5: Considerations on OFDMA
Consideration #1: Channel access technique[3]
  Primary channel based access
  Preferred channel based access
Consideration # 2: UL-OFDMA[3]
  Time-synchronization : difficult to expect that users want to transmit simultaneously
  CCA : channel states couldn’t be easily guaranteed
Consideration # 3: Sub-band size[3]
  20MHz or smaller
Consideration # 4: CCA thresholds for OFDMA
  Different CCA thresholds level to OFDMA device or NOT
  CCA threshold level regarding discrete band and fairness problem[4]
Consideration # 5: New control signaling to support OFDMA
  New frame header or frames to support OFDMA
  For scheduling, CCA, time-synchronization, power saving, etc.

## Slide 6: Considerations on OFDMA
Consideration # 6: Legacy supporting of OFDMA
  Supporting 802.11ax STA only or not
  Fairness problem between 802.11ax devices and legacy device
Consideration # 7: High spectral frequency reuse
  Spectral frequency reuse in dense BSS scenario was not fully considered
  Using wideband by OFDMA could decrease spectral frequency reuse in dense BSS scenario
Cha1
Cha2
Cha3

## Slide 7: Conclusion
OFDMA is crucial technique for High Efficient WLAN
To achieve goal of 802.11ax, we need to consider not only just adopting OFDMA but also discussing about dense AP scenario OBSS environment
OFDMA for 802.11 should be designed under some considerations
  Channel access technique
  UL-OFDMA
  Sub-band size
  CCA thresholds for OFDMA
  New frame to support OFDMA
  Legacy supporting of OFDMA
  High spectral frequency reuse
  Etc.
Because using wideband and OFDMA can decrease real world performance and efficiency in dense AP scenarios, we need to evaluate the performances and find solutions if the problem is not negligible

## Slide 8: Straw polls and proposed text for Requirements
Straw Poll #1) Should DL-OFDMA be considered in IEEE 802.11 ax?
Requirement 1 : IEEE 802.11ax may support downlink OFDMA.
Requirement 2 : IEEE 802.11ax downlink OFDMA shall not degrade the performance of legacy BSSs.

## Slide 9: References
IEEE 802.11-14/0165r1 , “802.11 HEW SG Proposed PAR”
IEEE 802.11-10/0317r1 , “DL-OFDMA for Mixed Clients”
IEEE 802.11-13/1382r0 , “Discussion on OFDMA in HEW”
IEEE 802.11-07/3000r2 , “Simulation of 20 40 MHz CCA Unfairness”