## Slide 1: Analysis on Multiplexing Schemes exploiting frequency selectivity in WLAN Systems
Date: 2014-7-15
Authors:

## Slide 2: Abstract
We introduce frequency selective multiplexing using OFDMA for consideration in IEEE 802.11ax and provide an initial analysis that captures the gains that can be obtained through OFDMA.

## Slide 3: Multiplexing Techniques in 802.11
OFDM
MU-MIMO
Widely used in 802.11
Introduced in 802.11ac

## Slide 4: Considerations for introducing OFDMA
Already explored time and space multiplexing
  Frequency is another dimension in the triad
  Allows frequency sensitive multiplexing
Need to support large number of users in dense deployments
  Cellular standards use OFDMA in such deployment scenarios
  802.11ax contributions have proposed the use of OFDMA in such scenarios [2]
Extract scheduling gains/selection diversity by scheduling users not in outage
  Easily done at AP where channel state information is available for MU-MIMO
How to show gains from OFDMA?

## Slide 5: Quantifying gains from OFDMA
Insights from the literature [1]
  Per sub-carrier bit, power coupled with user selection outperforms per sub-carrier bit , power loaded OFDM with TDM among users
We are interested in finding out merits of OFDMA relative to 802.11 style OFDM with TDM among users
  Even in the absence of sophisticated scheduling algorithms
    In particular, assuming arbitrarily chosen users
MU-MIMO requires careful user selection
  Does the same hold true for OFDMA?
Notes: The blue square indicates that we will treat this first and then take up MU-MIMO

## Slide 6: Experiment Design
STAs -1 & 2 are arbitrarily chosen.
Assume channel is known at AP
Depends on Multiplexing technique
Compare time taken to transmit data MPDUs using
a) OFDM
b) OFDMA

## Slide 7: Time taken to transmit a packet
Use the Capacity formula to map instantaneous SNR per subcarrier to the rate
Compute the average rate
Use the average rate to compute
# of bits per OFDM Symbol
Compute # of OFDM Symbols per packet  time taken to transmit the packet

## Slide 8: OFDM

## Slide 9: OFDMA
Choose user with maximum rate for each segment
If the tranmission of one user’s data MPDU is complete, use the entire BW for the second user.

## Slide 10: Comparing OFDM with OFDMA
For a choice of two users (instantiated by random generation of channels)
   compute and
Plot CDF of computed at every instant over many instantiations
0
1
CDF
0
> 0
OFDMA is better
< 0
OFDM is better

## Slide 11: Comparing OFDM with OFDMA
Not apples-to-apples!
OFDM – 802.11 style is at a disadvantage.
OFDMA assumes per segment adaptation which is advantageous in a frequency selective channel

## Slide 12: Fairly comparing OFDM and OFDMA
Since rate is chosen per segment  segmented OFDM

## Slide 13: Comparing SEG-OFDM with OFDMA
Gains due to user selection still persists!

## Slide 14: Comparison with SDMA
Assume MRT transmission with the precoder set to the inverse of the concatenated channel.
Update AP to have 2 antennas
Measure total MPDU transmission time

## Slide 15: Sensitivity to user selection in SDMA
SDMA is better

## Slide 16: Observations
OFDMA can be considered as a multiplexing technique in 802.11ax
  There is a measurable advantage that can be extracted by frequency adaptive loading of users even in the absence of sophisticated user selection algorithms.
  This advantage persists even when 802.11 OFDM is *improved* to support the adaptive loading of subcarriers (slide #13)
  This advantage increases with an increasing frequency selectivity of the channel (as is likely to be the case in the outdoor scenario)
The channel frequently favors OFDMA over SDMA
  Both have similar channel state information requirements at the transmitter.
  Basic mechanisms that were incorporated to support MU-MIMO can be reused to support OFDMA.

## Slide 17: Next Steps
Scale up spatial dimensions at both AP and STAs to include results with MIMO
Evaluate assuming non-ideal CSI at AP
Update metric to include throughput evaluated using PHY abstraction
Discuss evaluation methodology to study techniques like OFDMA

## Slide 18: References
[1] C.Y. Wong, R. S. Cheng, K. B. Letaief and R. D. Murch, “ Multiuser OFDM with Adaptive Subcarrier, Bit and Power Allocation”, IEEE Journal on Selected Areas in Communications, Vol. 17, No.10 Oct 99
[2] Brian Hart, 11-14-0855-00-00ax-techniques-for-short-downlink-frames.pptx