## Slide 1: Proposing a Stadium Scenario
Date: 2014-07-01
Authors:

## Slide 2: Abstract
Stadium has been acknowledged as a important use case for the ax-technology. This document provides some reasons why Stadium should be included as one scenario in the Simulation scenario document

## Slide 3: About the Stadium concept
Presented in IEEE 11-14/0381r0, (Sony and Ericsson; March meeting)
  March meeting response summary : Further discussions if stadiums justify a separate simulation use case or are subsumed in outdoor
A stadium concept cover the aspects:
  Several hundreds of APs concentrated in small area
  High number of overheard STAs / APs
  50,000 – 100,000 potential users (and active)
  Very high interference levels and a raised noise floor
  One AP typically covers 25 – 150 seats
  Traffic demands are in the order of hundreds of GB/hour during an event
  Outdoor scenario
  Deployments using directional antennas

## Slide 4: About the Stadium concept
Thus it serves the purpose of evaluating a very difficult use case:
  Users ultra-close to each other (many STAs close to each other)
  LoS environment (increasing OBSS problem)
  High bandwidth demands
  UL/DL coverage asymmetry
    Directional at AP and Omni-antenna at STA
At last meeting some measurement results was presented IEEE 11-14/0682r0 showing some relevant issues related to stadium deployments

## Slide 5: Wi-Fi Alliance input
In the Liaison from Wi-Fi Alliance HEW Use Cases (IEEE 802.11-13/1443r0) the Stadium scenario had the highest ranking to create WiFi network bottlenecks in 2020 time frame.

## Slide 6: Current content (IEEE 802.11-14/0621r4)
Does the “Indoor Small BSSs Scenario” scenario cover “Stadium” aspects?
  Outdoor Large BSS Hotspot does not (since “large-sized” BSS)
 | Scenario Name | Topology | Management | Channel Model | Homogeneity | ~Traffic Model
1 | Residential | A - Apartment building e.g. ~10m x 10m apartments in a multi-floor building ~10s of STAs/AP, P2P pairs | Unmanaged | Indoor | Flat | Home
2 | Enterprise | B - Dense small BSSs with clusters e.g. ~10-20m inter AP distance, ~100s of STAs/AP, P2P pairs | Managed | Indoor | Flat | Enterprise
3 | Indoor Small BSS Hotspot | C - Dense small BSSs, uniform e.g. ~10-20m inter AP distance ~100s of STAs/AP, P2P pairs |  |  |  | Mobile
4 | Outdoor Large BSS Hotspot | D - Large BSSs, uniform e.g. 100-200m inter AP distance ~100s of STAs/AP, P2P pairs | Managed | Outdoor | Flat | Mobile
4a | Outdoor Large BSS Hotspot + Residential | D+A | Managed + Unmanaged |  | Hierarchical | Mobile + Home

## Slide 7: Comparing w/ Stadium scenario
Differences:
  Sector (directional) coverage of APs
  LoS channel model
  Users are placed within tens of centimeters between each other
  The overhearing overlap between BSSs is large, creating many OBSS and hidden nodes issues
 | Scenario Name | Topology | Management | Channel Model | Homogeneity | ~Traffic Model
3 | Indoor Small BSS Hotspot | C - Dense small BSSs, uniform e.g. ~10-20m inter AP distance ~100s of STAs/AP, P2P pairs | Managed | Indoor | Flat | Mobile
4 | Outdoor Large BSS Hotspot | D - Large BSSs, uniform e.g. 100-200m inter AP distance ~100s of STAs/AP, P2P pairs | Managed | Outdoor | Flat | Mobile
New proposed 5 | Stadium | E – Dense small BSSs, uniform distribution (at pre-defined seats) e.g.~10-20m inter AP distance ~100s of STAs/AP, P2P pairs | Managed |  | Flat | Mobile

## Slide 8: Issue: Directional antennas at APs
Non-symmetric coverage of APs and STAs
  Directional antennas at APs provides isolation between neighbour AP coverage areas;
  Omni-antennas at STAs spread radio signals in all directions
Uplink and downlink unbalances are introduced in the stadium case
Issue example: STA in another BSS cannot discover another BSS/AP DL transmission and may start an interfering transmission reducing overall spectrum efficiency
  RTS/CTS mechanism is not assumed as being used in practice
Overlapping BSSs issue STA to STA
STA1
STA2
AP2
AP1
AP2 coverage
AP1 coverage
Shape of STA coverage (Not showing “actual” coverage) UL and DL
STA1
STA2
Reference case: Regular, Omni antenna
AP1
AP2
STA may detect transmissions from other APs
STA may not detect transmissions from other APs

## Slide 9: Issues with other scenarios not being sufficient
1) Need for consideration of UL/DL imbalance
a) power
b) range
c) topology
d) carrier sensing range
2) Higher user density
3) Massive multicast usage
4) High UL traffic demand (photo uploads etc.)

## Slide 10: How to capture
Options:
Include a new scenario with typical stadium deployment.
  Supporting denser network, LoS channel model, many OBSS and hidden node effects
  Capturing also directional antenna deployment, UL/DL asymmetry coverage effects
Modify/include a channel model in scenario 3 “Indoor BSS Hotspot” that is more suited for stadium case (such as increase the LoS distance)
  The high level of OBSS interference may still not be covered; needs also high density STA placement within each BSS
  But, no sector/directional deployments; missing coverage asymmetry effects
A new scenario seems more appropriate to capture all effects within same test environment, creating a challenging test case to evaluate performance

## Slide 11: References
https://mentor.ieee.org/802.11/dcn/14/11-14-0381-00-0hew-stadium-scenario-for-hew.ppt
https://mentor.ieee.org/802.11/dcn/13/11-13-1443-00-0hew-liaison-from-wi-fi-alliance-on-hew-use-cases.ppt
https://mentor.ieee.org/802.11/dcn/14/11-14-0621-04-00ax-simulation-scenarios.docx
https://mentor.ieee.org/802.11/dcn/14/11-14-0682-00-00ax-in-situ-spectrum-reuse-measurements-in-indoor-20-000-seat-arena.pptx

## Slide 12: Straw poll
Do you agree to include the text in document 11-14/0860r0 in simulation scenario document?
Yes: 66
No: 25
Abstain: 48