## Slide 1: A Subsetting and EPD Approach
Date: 2014-07-13
Authors:

## Slide 2: Abstract
This presentation describes how to solve a number of 802.11ak (GLK) problems using synthetic Receiver MAC addresses.

## Slide 3: Problems Addressed in These Slides
AP specification of a subset of receivers for multi-destination frames.
Support for EPD (Ethertype Protocol Discrimination).
Support for mixed BSS – both GLK and non-GLK stations. GLKness should be a property of each pairwise link.
Frame abbreviation in light of VLAN tags, etc.

## Slide 4: Use a New OUI
Using a new global OUI, can create synthetic Receiver MAC addresses.
Can create Group Addresses and Individual Addresses
00-TB-D0
?
01-TB-D0
?
00-TB-D0
?

## Slide 5: Sub-setting Solution
Indicate excluded receiver(s) in the lower 24-bits:
  Supports sending to arbitrary subset of 3 GLK non-AP STAs without complexity or restriction on AID assignment:
    Send to 1 or 3 with individual address or no AID specified.
    Send to 2 by specifying the one AID to exclude.
  Support sending to an arbitrary subset of a larger number of non-AP STAs but requires restrictions on AID assignment or a bit assignment protocol.
01-TB-D0
AID
01-TB-D0
bits

## Slide 6: Support for EPD
Saves 6 bytes in the vast majority of data frames.
Use LPD (LLC Protocol Discrimination) for all MPDUs with current Receiver addresses.
Use EPD for all data frames with Receiver synthetic MAC address built with the new OUI.
Easy to make individually addressed synthetic MACs:
  Use special AID field value or flags in spare bits to indicate AP.
00-TB-D0
AID

## Slide 7: Support for Mixed BSS
A link (association) is GLK if and only if both STAs are GLK.
Legacy STAs still restricted to LPD and will ignore both individually and group addressed MPDUs to the new Receiver synthetic MAC addresses.
GLK STAs can use LPD or EPD as they choose. Zero wasted bytes for both Ethertype data and LLC data.
  For Individually addressed MPDUs, just use the real or synthetic MAC Receiver address.
  Group addressed case a bit more complex but could indicate LPD with subsetting by a flag in the synthetic Receiver MAC.

## Slide 8: Frame Abbreviation
Four bytes can be saved per MSDU because
  VLAN tags will be common – particularly due to the Priority Code Point ⇔ UP tweaking.
  A few Ethertypes account for almost all traffic.
Possible Individually addressed Receiver synthetic MAC:
Total savings possible over LPD: 10 bytes
OUI 00-TB-D0
Ethertype Index
Association ID
VLAN flag
other flags

## Slide 9: References
Draft 0.02 of 802.11ak and results of Comment Collection 17:
  http://www.ieee802.org/11/private/Draft_Standards/11ak/Draft P802.11ak_D0.02.pdf
  11-14/559r7, “TGak CC17 Comments”
Detailed amendment text:
  11-14/0826r0, “Frame Type Encoding”