## Slide 1: MAC calibration results
Date: 2014-07
Authors:

## Slide 2: Summary
Contribution [1][2] define the simulation scenarios and evaluation method for MAC system calibration
This contribution provides preliminary results on MAC calibration
  Test 1: MAC overhead test
  Test 2: Deferral test
  For test 4, we found the test case violates the basic 802.11ac MAC behavior, therefore we propose to modify the test case to fulfill the calibration purpose

## Slide 3: Test 1a: MAC overhead w/out RTS/CTS -Simulation Parameter-
AP1
STA 1
AP1
Assumptions:
  PER is 0
Parameters:
  MSDU length:[0:500:2000Bytes]
  RTS/CTS OFF
  MCS = [0,8] ( to clarify, run a sweep over MSDU length once for MCS 0, and once for MCS 8.

## Slide 4: Test 1a: MAC overhead w/out RTS/CTS -Check Points-
AP1
 | Simulation Log | Standard definition | Matching?
Frame duration | Tcp2-Tcp1= 3768 us | ceil((FrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | 
SIFS | Tcp3-Tcp2=16 us | 16 us | 
ACK duration | Tcp4-Tcp3=68 us | ceil((ACKFrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | 
Defer & backoff duration | Tcp5-Tcp4=142 us | DIFS(34 us)+backoff (CWmin) =34us+12*9us | 
s 0.012128065 _1_ MAC --- 1 cbr 3016 [54 0 1 0] Check point1 (CP1)
r 0.015896097 _0_ MAC --- 1 cbr 1472 [0 0 1 0] Check point2 (CP2)
r 0.015896097 _0_ MAC --- 2 cbr 1472 [0 0 1 0 Check point2 (CP2)
s 0.015912097 _0_ MAC --- 0 ACK 32 [0 1 0 0] Check point3 (CP3)
r 0.015980129 _1_ MAC --- 0 ACK 32 [0 1 0 0] Check point4 (CP4)
s 0.016122129 _1_ MAC --- 3 cbr 3016 [54 0 1 0] Check point5 (CP5)

## Slide 5: Test 1a: MAC overhead w/out RTS/CTS -Throughput Performance-
AP1

## Slide 6: Test 1b: MAC overhead w RTS/CTS -Simulation Parameter-
AP1
STA 1
AP1
Assumptions:
  PER is 0
Parameters:
  MSDU length:[0:500:2000Bytes]
  RTS/CTS ON
  MCS = [0,8] ( to clarify, run a sweep over MSDU length once for MCS 0, and once for MCS 8.

## Slide 7: Test 1b: MAC overhead w RTS/CTS -Check Points-
AP1
 | Simulation Log | Standard definition | Matching?
RTS duration | Tcp2-Tcp1=52 us | ceil((RTSFrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | 
CTS duration | Tcp4-Tcp3=44 us | ceil((CTSFrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | 
Frame duration | Tcp6-Tcp5= 3768 us | ceil((FrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | 
s 0.012229123 _1_ MAC --- 0 RTS 20 [f58 0 1 0] Check point1 (CP1)
r 0.012281154 _0_ MAC --- 0 RTS 20 [f58 0 1 0] Check point2 (CP2)
s 0.012297154 _0_ MAC --- 0 CTS 14 [f1c 1 0 0] Check point3 (CP3)
r 0.012341185 _1_ MAC --- 0 CTS 14 [f1c 1 0 0] Check point4 (CP4)
s 0.012357185 _1_ MAC --- 1 cbr 3016 [0 0 1 0] Check point5 (CP5)
r 0.016125216 _0_ MAC --- 1 cbr 1472 [0 0 1 0] Check point6 (CP6)
r 0.016125216 _0_ MAC --- 2 cbr 1472 [0 0 1 0] Check point6 (CP6)

## Slide 8: Test 1b: MAC overhead w RTS/CTS -Throughput Performance-
AP1

## Slide 9: Test 2a: Deferral Test 1 -Simulation Parameters-
AP1
STA 1
AP 2
AP1
STA 2
(AP1 and STA2 are essentially co-located)
Assumptions:
  devices are within energy detect range of each other.
  When AP1 and AP2 start to transmit on the same slot, both packets are lost (PER= 100%). Otherwise packets get through 100%. PER=0 %
Parameters:
  MSDU length:[0:500:2000Bytes]
  RTS/CTS [ OFF, ON]
  MCS = [0, 8]

## Slide 10: Test 2a: Deferral Test 1 -Throughput Performance-
AP1

## Slide 11: Test 2b: Deferral Test 2 -Simulation Parameters-
AP1
STA 1
AP 2
AP1
STA 2
Assumptions:
  AP1 and AP2 can not hear each other. ( ever)
  If MPDUs from AP1 and AP2 overlap, they both fail with 100% probability
  If an MPDU from AP1/AP2 is interference free, it succeeds with 100% probability.
  Parameters:
  MSDU length:[0:500:2000Bytes]
  RTS/CTS [ OFF, ON]
  MCS = [0, 8]

## Slide 12: Test 2b: Deferral Test 2 -Throughput Performance-
AP1

## Slide 13: Test 4: NAV deferral
AP1
Assumptions:
  All devices are within energy detect range of each other.
  When AP1 and AP2 start to transmit on the same slot, both packets are lost (PER= 100%). Otherwise packets get through 100%. PER=0 %
  APs send single MPDU, but sets NAV to txop= 4 ms
  APs should defer due to NAV setting..
STA 1
AP 2
AP1
STA 2
(AP1 and STA2 are essentially co-located)
Source from [1]
According to 802.11ac, STA doesn't stop transmitting frame in an allocated TXOP, sending one single frame and leaving the rest of TXOP open doesn’t look like a reasonable assumption
Propose to change the single MPDU to MPDUs

## Slide 14: Reference
[1] 11-14-0621-04-00ax-simulation-scenarios
[2] 11-14-0571-02-00ax-evaluation-methodology

## Slide 15: Annex

## Slide 16: Test1a + Test1b
Simulation results and theoretical calculation matches