## Slide 1: PHY Abstraction Tables for 11ax System Level Simulation
Date: 2014-07
Authors:
Name | Affiliations | Address | Phone | Email
Jiayin Zhang | Huawei Technologies | No. 2222 Xin Jinqiao Rd, Pudong, Shanghai |  | zhangjiayin@huawei.com
Jun Zhu |  |  |  | zhujun75@huawei.com
Yakun Sun | Marvell |  |  | 
Jianhan Liu | Mediatek |  |  | 
Tianyu Wu |  |  |  | 
Wookbong Lee | LG |  |  | 
Fei Tong | Samsung |  |  | 

## Slide 2: Abstract
In [1], RBIR was approved as PHY abstraction method for 11ax PHY and integrated system level simulation.
In [2], we agreed to use the effective SNR to PER curves of two typical packet length (32 and 1458bytes) to generate the PER of other packet length.
In this proposal, we provided the RBIR-CM curves and effective SNR to PER curves, which were calibrated by some companies.

## Slide 3: Post SINR to Mutual information (CM)
Chart: 
MI(bit)
SNR (dB)

## Slide 4: Effective SNR to PER Mapping Curves (32 bytes BCC)
Chart: 
PER
Effective SNR(dB)

## Slide 5: Effective SNR to PER Mapping Curves (1458 bytes BCC)
Chart: 
| -2 | -1.9000000000000001 | -1.8 | -1.7 | -1.6 | -1.5 | -1.4 | -1.3 | -1.2 | -1.1000000000000001 | -1 | -0.9 | -0.8 | -0.70000000000000018 | -0.6000000000000002 | -0.5 | -0.4 | -0.3000000000000001 | -0.2 | -0.1 | 0 | 0.1 | 0.2 | 0.3000000000000001 | 0.4 | 0.5 | 0.6000000000000002 | 0.70000000000000018 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9000000000000001 | 2 | 2.1 | 2.2000000000000002 | 2.2999999999999998 | 2.4 | 2.5 | 2.6
MCS0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.99999 | 0.99988 | 0.99951 | 0.99812 | 0.99447 | 0.98065 | 0.95605 | 0.91953 | 0.8648 | 0.79463 | 0.71254 | 0.61793 | 0.52948 | 0.43618 | 0.35485 | 0.28536 | 0.22445 | 0.17679 | 0.13528 | 0.1042 | 0.076665 | 0.057185 | 0.042898 | 0.031787 | 0.022715 | 0.016093 | 0.011898 | 0.0086625 | 0.005995 | 0.003985 | 0.0028925 | 0.0022375 | 0.00144 | 0.0011525 | 0.0006625 | 0.000415 | 0.0002225 | 0.00015333 | 5e-05
MCS1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.99997 | 0.99994 | 0.99965 | 0.99812 | 0.99373 | 0.98355 | 0.9619 | 0.92583 | 0.87169 | 0.80442 | 0.71947 | 0.62908 | 0.53584 | 0.4423 | 0.36127 | 0.29102 | 0.2318 | 0.18103 | 0.13809 | 0.1063 | 0.07983 | 0.058868 | 0.04286 | 0.032355 | 0.022728 | 0.016915 | 0.012072 | 0.0084 | 0.0060475 | 0.0038675 | 0.002695 | 0.0020075 | 0.001405 | 0.00057 | 0.00052 | 0.00031 | 0.0002 | 0.00012
MCS2 | 1 | 1 | 1 | 1 | 0.99997 | 0.99995 | 0.99969 | 0.99898 | 0.99593 | 0.98861 | 0.96341 | 0.9272 | 0.87055 | 0.79731 | 0.71223 | 0.61876 | 0.52531 | 0.43332 | 0.34824 | 0.2775 | 0.22008 | 0.17057 | 0.13206 | 0.099143 | 0.075913 | 0.05702 | 0.04216 | 0.030438 | 0.023055 | 0.016948 | 0.012125 | 0.0095675 | 0.0061525 | 0.005075 | 0.003315 | 0.0023975 | 0.0017375 | 0.0013 | 0.000825 | 0.00061 | 0.0004 | 0.00029 | 0.00016 | 0.00012 | 0.0001
MCS3 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.99999 | 0.99997 | 0.99988 | 0.99954 | 0.99788 | 0.99552 | 0.98577 | 0.9718 | 0.94735 | 0.91449 | 0.86465 | 0.8086 | 0.74271 | 0.66996 | 0.59551 | 0.51264 | 0.44678 | 0.38159 | 0.31839 | 0.26499 | 0.22027 | 0.17581 | 0.14679 | 0.11629 | 0.092542 | 0.075808 | 0.057315 | 0.046942 | 0.034582 | 0.027912 | 0.020792 | 0.01636 | 0.012967 | 0.0096967 | 0.00721 | 0.0055 | 0.0039033 | 0.00209 | 0.00167 | 0.00107 | 0.00075 | 0.00047 | 0.0003
MCS4 | 1 | 1 | 1 | 1 | 1 | 0.99993 | 0.99973 | 0.99876 | 0.9963 | 0.99076 | 0.97901 | 0.95699 | 0.92178 | 0.87116 | 0.81232 | 0.73973 | 0.66451 | 0.58381 | 0.50015 | 0.42184 | 0.35509 | 0.28905 | 0.2365 | 0.19228 | 0.15481 | 0.12294 | 0.09844 | 0.077035 | 0.059728 | 0.047275 | 0.035667 | 0.02802 | 0.02124 | 0.01621 | 0.01218 | 0.0091175 | 0.00685 | 0.0048975 | 0.00399 | 0.002815 | 0.00183 | 0.001455 | 0.0011975 | 0.00071 | 0.00034 | 0.00023 | 0.00019 | 0.00016
MCS6 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.99998 | 0.99989 | 0.99947 | 0.99807 | 0.9947 | 0.98756 | 0.97647 | 0.95756 | 0.92783 | 0.88855 | 0.83822 | 0.78081 | 0.71748 | 0.64768 | 0.57992 | 0.51413 | 0.44529 | 0.38591 | 0.33338 | 0.28128 | 0.2353 | 0.19929 | 0.16517 | 0.13525 | 0.11455 | 0.090675 | 0.073623 | 0.0596 | 0.046968 | 0.037542 | 0.030162 | 0.023772 | 0.0184 | 0.01451 | 0.011853 | 0.0085 | 0.0072225 | 0.005665 | 0.0042 | 0.003065 | 0.002245 | 0.00187 | 0.001285 | 0.00072 | 0.0005 | 0.00053 | 0.00038 | 0.00021 | 0.00016 | 0.00012
MCS7 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.99999 | 0.99997 | 0.99972 | 0.99916 | 0.99706 | 0.99241 | 0.98221 | 0.96216 | 0.93369 | 0.89227 | 0.83691 | 0.77278 | 0.70353 | 0.62634 | 0.54802 | 0.47516 | 0.40744 | 0.34508 | 0.28515 | 0.23701 | 0.19426 | 0.15711 | 0.12705 | 0.10428 | 0.083423 | 0.065575 | 0.052228 | 0.040718 | 0.032872 | 0.025603 | 0.01969 | 0.015528 | 0.012192 | 0.0087725 | 0.006745 | 0.00451 | 0.003245 | 0.00298 | 0.00219 | 0.00165 | 0.00129 | 0.00089 | 0.00065 | 0.00049 | 0.00034 | 0.00022 | 0.00016
PER
Effective SNR(dB)

## Slide 6: Effective SNR to PER curves (1458 bytes LDPC)
Chart: 
| -2 | -1.9000000000000001 | -1.8 | -1.7 | -1.6 | -1.5 | -1.4 | -1.3 | -1.2 | -1.1000000000000001 | -1 | -0.9 | -0.8 | -0.70000000000000018 | -0.6000000000000002 | -0.5 | -0.4 | -0.3000000000000001 | -0.2 | -0.1 | 0
MCS0 | 1 | 1 | 1 | 0.9998 | 0.9965 | 0.97887 | 0.97423 | 0.90913 | 0.76817 | 0.60523 | 0.41153 | 0.23023 | 0.11747 | 0.050133 | 0.019933 | 0.009 | 0.0030067 | 0.0018 | 0.00105 | 0.0007 | 0.0004
MCS1 | 1 | 1 | 1 | 0.99987 | 0.99733 | 0.9953 | 0.9846 | 0.9132 | 0.78417 | 0.6111 | 0.40767 | 0.2338 | 0.117 | 0.0513 | 0.021367 | 0.0075667 | 0.0034 | 0.00215 | 0.0013 | 0.0007 | 0.0004
MCS2 | 1 | 1 | 1 | 1 | 0.9999 | 0.9983 | 0.9831 | 0.91743 | 0.77703 | 0.59653 | 0.4188 | 0.26 | 0.14073 | 0.067933 | 0.0284 | 0.011033 | 0.0037038 | 0.0011735 | 0.0011 | 0.0008 | 0.0003
MCS3 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.99987 | 0.99783 | 0.98413 | 0.9285 | 0.8155 | 0.66037 | 0.4973 | 0.3436 | 0.21373 | 0.11643 | 0.054067 | 0.024633 | 0.0101 | 0.0043333 | 0.0018 | 0.00125 | 0.001 | 0.0005
MCS4 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.99993 | 0.99907 | 0.9928 | 0.9676 | 0.91083 | 0.8275 | 0.72743 | 0.59703 | 0.42587 | 0.26493 | 0.1417 | 0.062867 | 0.025933 | 0.010767 | 0.0045 | 0.0011 | 0.0007 | 0.00025 | 0 | 0 | 0
MCS5 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.99993 | 0.99963 | 0.9969 | 0.9856 | 0.95307 | 0.89303 | 0.7997 | 0.68233 | 0.5321 | 0.3831 | 0.24387 | 0.13953 | 0.071167 | 0.0334 | 0.014567 | 0.0061276 | 0.0015829 | 0.0009775 | 0.00013873
MCS6 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.99995 | 0.99955 | 0.99575 | 0.9785 | 0.9537 | 0.89627 | 0.82323 | 0.7455 | 0.66067 | 0.54897 | 0.4261 | 0.2892 | 0.1774 | 0.095267 | 0.043933 | 0.021033 | 0.01375 | 0.0048 | 0.00215 | 0.001
MCS7 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.99995 | 0.99973 | 0.99797 | 0.9897 | 0.96477 | 0.90747 | 0.81283 | 0.6804 | 0.5201 | 0.366 | 0.22743 | 0.13587 | 0.074867 | 0.038933 | 0.0185 | 0.0101 | 0.0050667 | 0.002 | 0.0011 | 0.00055 | 0.0002 | 0.0002
MCS8 | 1 | 1 | 1 | 0.9998 | 0.9984 | 0.99105 | 0.9685 | 0.94217 | 0.8761 | 0.7785 | 0.64567 | 0.4958 | 0.36963 | 0.24007 | 0.14983 | 0.082567 | 0.045233 | 0.022233 | 0.010833 | 0.005 | 0.00265 | 0.00135 | 0.0008 | 0.0005
MCS9 | 1 | 1 | 1 | 0.9998 | 0.9988 | 0.99383 | 0.97787 | 0.94117 | 0.87563 | 0.7781 | 0.65953 | 0.51837 | 0.38647 | 0.26027 | 0.16227 | 0.098733 | 0.0541 | 0.031133 | 0.017733 | 0.0073333 | 0.00655 | 0.00395 | 0.002 | 0.0011 | 0.0005 | 0.0006
PER
Effective SNR(dB)

## Slide 7: Summary
In this proposal, the PHY abstraction tables were provided.
Using the calibrated tables facilitates multiple companies to derive same SLS results under same assumptions.
We suggest to include these results in the section of PHY abstraction in EMD document.

## Slide 8: Straw Poll
Do you support to include the following curves into Evaluation Methodology Document
  Post SINR to MI mapping curves for BPSK/QPSK/16QAM/64QAM/256QAM
  Effective SNR to PER mapping curves for MCS0~MCS9 of BCC 32bytes/1458bytes and LDPC 1458bytes.
  These curves were averaged from multiple companies' results
Y
N
ABS

## Slide 9: Reference
[1] 11-14-0585-05-00ax-phy-abstraction-types-for-11ax-system-level-simulation
[2] 11-14-0803-01-00ax-packet-length-for-box-0-calibration