## Slide 1: EPD, Mixed BSSes, and Group RAs
Date: 2014-07-17
Authors:

## Slide 2: Abstract
This presentation describes one way to resolve a number of intertwined 802.11ak (GLK) questions related to EPD versus LPD, mixes BSSes of GLK and non-GLK STAs, and Group Addresses RAs.

## Slide 3: Capabilities
GLK stations indicate they are GLK by including a GLK Information Element (IE) in Beacons, Probe Requests and Responses, DMG Beacons, (Re)Association Requests and Responses, Mesh Peering Opens, Mesh Peering Confirms, and … (TDLS?).
Capabilities/Options are indicated by bits/fields within the GLK IE, except that
  Support of EPD is indicated by Capability Information Field bit 13 and DMG Capability Information Field bit 62.

## Slide 4: Pairwise STA Communications
IBSS, PBSS, Direct Link, Mesh Peer, and Individually Addressed AP ↔︎ non-AP MPDUs carry
  EPD MSDUs if both STAs support EPD and
  LPD MSDUs otherwise.
Typically use the 4-address format but if traffic is actually intended for the receiver, may use 3-addresses when appropriate.

## Slide 5: Mixed BSSes
A GLK AP may permit association of non-AP STAs regardless of their GLK or EPD support.
  GLK APs indicate their policies on this by two BSS membership selector values, indicating that support is required, one for GLK and one for EPD. Non-AP STAs attempting to associate in violation of the policy are rejected.
  The “Supported Rates” IE will be renamed the “Supported Rates and BSS Membership Selectors” IE.
(A non-GLK AP doesn’t recognize GLK/EPD support requirement indications and so is happy to associate with such non-AP STAs if the STAs want.)

## Slide 6: Group Addressed RAs
An AP uses EPD for MSDUs carried by MPDUs with Group Addressed RAs if it requires all associated non-AP STAs to support EPD, as indicated by requiring EPD support in its Supported Rates and BSS Membership Selectors IE. Otherwise is uses LPD for such MPDUs with Group Addressed RAs.
A GLK AP transmitting an MPDU with Group Addressed RA intended for GLK non-AP STAs uses an RA constructed as shown on the following slide. They must use the four address format in order to also carry the true destination address.

## Slide 7: GLK Group RA Addresses
GLK APs send data MPDUs with a Group RA only using an RA constructed with a new TBD OUI. The lower 24 bits have additional information, including subsetting. Optionally, there would be support for a larger amount of subsetting information in the data portion of the frame.
GLK non-AP STAs ignore MPDUs with a Group Addressed RA not formed as above, that is, where the RA has a different upper 24 bits.
0x01TBD0
bits

## Slide 8: Questions
There are “relay” features in 802.11ad-2012 and in 802.11ah (Draft D2.0). How does these in interact with four address format, etc.?
Other questions?