## Slide 1: EPD, Mixed BSSes, and Group RAs
Date: 2014-09-11
Authors:

## Slide 2: Abstract
This presentation describes one way to resolve a number of intertwined 802.11ak (GLK) questions related to EPD versus LPD, mixes BSSes of GLK and non-GLK STAs, and Group Addresses RAs.

## Slide 3: Capabilities
GLK (General Link) stations indicate they are GLK by including a GLK Information Element (IE) in Beacons, Probe Requests and Responses, DMG Beacons, (Re)Association Requests and Responses, Mesh Peering Opens, Mesh Peering Confirms, and … (TDLS?).
Capabilities/Options are indicated by bits/fields within the GLK IE, except that
  Support of EPD is indicated by Capability Information Field bit 13 and DMG Capability Information Field bit 62.

## Slide 4: Pairwise STA Communications
IBSS, PBSS, Direct Link, Mesh Peer, and Individually Addressed AP ↔︎ non-AP MPDUs carry
  EPD MSDUs if both STAs support EPD and
  LPD MSDUs otherwise.
They typically use the 4-address format but, when appropriate, such as when traffic is actually intended for the receiver, may use 3-addresses.
  Details on using 4-address format need to be added to draft.

## Slide 5: Mixed BSSes
A GLK AP may permit association of non-AP STAs regardless of their GLK or EPD support.
  GLK APs indicate their policies on this by two BSS membership selector values, indicating that support is required, one for GLK and one for EPD. Non-AP STAs attempting to associate in violation of the AP’s policy are rejected.
  The “Supported Rates” IE will be renamed the “Supported Rates and BSS Membership Selectors” IE.
A non-GLK AP doesn’t recognize GLK/EPD support indications and so is happy to associate with GLK/EPD non-AP STAs if such non-AP STAs want to associate with the non-GLK AP.

## Slide 6: BSS membership selectors
Existing 802.11REVmc-D3.0 “Table 8-86—BSS membership selector value encoding”:
Proposed addition:
 | Value | Feature | Interpretation | 
 | 127 | HT PHY | Support for the mandatory features of Clause 20 (High Throughput (HT) PHY specification) is required in order to join the BSS that was the source of the Supported Rates element or Extended Supported Rates element containing this value. | 
 | 126 | VHT PHY | Support for the mandatory features of Clause 22 (Very High Throughput (VHT) PHY specification) is required in order to join the BSS that was the source of the Supported Rates element or Extended Supported Rates element containing this value. | 
 | Value | Feature | Interpretation | 
 | 125 | GLK | Support for the mandatory features of Clause TBD is required in order to join the BSS that was the source of the Supported Rates element or Extended Supported Rates element containing this value. | 
 | 124 | EPD | Support for EPD is required in order to join the BSS that was the source of the Supported Rates element or Extended Supported Rates element containing this value. | 

## Slide 7: Group Addressed RAs
A GLK AP transmitting a data MPDU with a Group Addressed RA intended for GLK non-AP STAs must use an RA constructed as shown on the following slide. It also must use the four address format in order to carry the true destination address.
A GLK AP transmitting a non-data MPDU with a Group Addressed RA or one intended for non-GLK non-AP STAs uses existing RA types that do not include those constructed as shown on the following slide.
If transmitting Group Addressed RA data MPDU to both GLK and non-GLK non-AP STAs, it must transmit twice.

## Slide 8: Group Addressed RAs
An AP that requires all associated STAs to support EPD, as indicated by requiring EPD support in its Supported Rates and BSS Membership Selectors IE, must use EPD for all MSDUs in MPDUs with Group Addressed RAs.
If an AP does not require EPD support by associated STAs, it must use LPD for all MSDUs in MPDUs with Group Addressed RAs.
(EPD for individually addresses MPDUs is covered by an earlier slide.)

## Slide 9: GLK Group RA Addresses
All data MPDUs sent by GLK APs to GLK STAs with a Group Addressed RA use an RA constructed with a new TBD OUI. The lower 24 bits have additional information, including sub-setting. Optionally, there would be support for a larger amount of sub-setting information in the data portion of the frame.
GLK non-AP STAs ignore data MPDUs with a Group Addressed RA not formed as above, that is, where the RA has a different upper 24 bits.
0b0XXXXXX01 0xXXXX
24 bits

## Slide 10: Example Bit Encoding
Lower 24 bits of constructed Group Addressed RAs could be as follows:
For type zero, the 22 bits indicate the receivers. Either
  Bit numbers are assigned at association time or
  AIDs are restricted and bit n represents AID 1000+n or something. (Don’t want to use low numbered AIDS due to Multiple BSSID feature use of them.)
2 bit type
22 bits

## Slide 11: Questions
What about OCB (Outside the Context of a BSS) operation? Not clear how to decide between EPD and LPB, for example, as there is generally no negotiation/association/peering phase…
There are “relay” features in 802.11ad-2012 and in 802.11ah (Draft D2.0). How do these in interact with GLK four address format, etc.?
What does it mean if an AP claims not to support EPD but requires EPD for non-AP STAs to associate?
Other questions?