## Slide 1: Frame Exchange Control for Uplink Multi-user transmission

## Slide 2: Background
In the 11ax PAR, it is said that “the project may include the capability to handle multiple simultaneous communications in both the spatial and frequency domains, in both the uplink (UL) and downlink (DL) direction”, [1].
  DL MU-MIMO has already been supported in 11ac.
  UL multi-user transmission was discussed in previous meetings, including UL MU-MIMO and UL OFDMA.
  UL MU transmission is identified as a candidate technology to improve the network efficiency in dense deployment case.
    The feasibility of supporting OFDMA and UL MU-MIMO has been analyzed in [2] and [3].

## Slide 3: Motivation
A general UL MU transmission procedure has been introduced in [3].
However the detailed scheme for UL MU transmission has not been discussed yet, in particular:
  Multi-user polling and information indication
  The policy for multiple frame transmission in a UL MU TXOP
  Multi-user acknowledgement
  Error recovery
In this contribution, we propose the rules for UL MU transmission in a TXOP.

## Slide 4: Analysis
The following issues should be considered to define a complete UL MU transmission protocol
  Multiple UL MU transmission procedure in a TXOP
    How to schedule multiple frame transmission in a UL MU TXOP, and control the procedure with less overhead
  Multi-user acknowledgement
    When AP receive multiple STAs’ UL frame, how to send the acknowledgement frame ? Sending in parallel or serial ?
  Error recovery
    When UL MU data fails, STA or AP which one initials the error recovery procedure? Is error indication needed?
  Flexible UL MU transmission scheduling
    How to schedule new STAs during a UL MU TXOP

## Slide 5: Considerations for UL MU transmission control
AP’s responsibility in UL MU transmission
  Schedule or contend channel time for UL MU transmission
  Poll multiple STAs’ UL data and sending ack to multiple STAs.
  Initiate the error recovery procedure
  Provision assistant information for UL MU transmission
    Power control
    Time and frequency synchronization
STA’s responsibility in UL MU transmission
  Waiting AP’s polling before UL MU transmission
  Send UL PPDU with power/time/frequency adjustment if AP indicated these information to the STA
  send UL PPDU with a time length which is determined by AP
    Easy for AP to control the transmission within the TXOP limit
    Easy for AP to acknowledge multiple STAs at a same time

## Slide 6: Multi-user acknowledgement and Polling
A scheme is needed to allow multiple UL MU transmissions with purposes such as:
  acknowledgement
  Polling and resource allocation
  error indication
  transmission control indication eg. time/frequency/power adjustment
Principle and justice
  To achieve the above purposes with less overhead
  To keep compatibility with legacy devices
A scheme using multi-user BA+Poll frame is introduced
  The multi-user BA + Poll frame combines the functions of BA, scheduling control error indication
  The multi-user BA + Poll frame can reuse the current BA frame structure
  The multi-user BA + Poll frame can be sent in non-HT format
  No additional scheduling/poll frame needed

## Slide 7: Multi-user acknowledgement and Polling
The multi-user BA+Poll frame used during a UL MU TXOP can:
  acknowledgement the previous UL MU transmission
  schedule the next UL transmission for the current group
    The Duration/ID field can be reused for the next UL MU PPDU TxTime calculation

## Slide 8: Error Recovery
When one of the UL MU STAs’ data fails, AP can use the multi-user BA+ Poll frame for error recovery
  indicate receiving failure to the transmitter, a null BA information field can be used as shown in slide 12
  both error indication and scheduling can be combined in same BA +Poll frame
  a STA can trigger retransmission in the next UL MU transmission when receiving the failure indication

## Slide 9: Schedule new user(s) during the UL MU TXOP
AP can use the multi-user BA+ Poll frame to poll a new STA within the UL MU TXOP
  Poll new STA(s) for UL MU transmission
  Indicate the time/frequency/power adjustment information and UL resource allocation for the new STA(s)

## Slide 10: Scheduling STAs at the beginning of a TXOP
AP can use the multi-user BA+Poll frame as a UL MU scheduling frame that transmitted as a initial frame of a TXOP.
  When transmitted as a scheduling frame, the multi-user BA+Poll frame is no longer a control response frame
  The new BA can use the null BA information fields to schedule multi-users of the UL MU TXOP, example of the null BA information fields is shown in slide 12

## Slide 11: Example of multi-user BA+Poll frame structure
Multi-user BA+Poll is almost the same as multi-TID BA
  We can use FC filed to indicate the new frame type or use the BA control field to indicate the new BA variant
  Each STA corresponds to a BA information field, the BA information fields can be a BA+Poll or a null BA
The polling bit indicated whether the corresponding STA is permitted to transmit in the following UL MU PPDU
  AP can base on the STA’s buffer status which is indicated in more data or other fields in UL data frame to determine the value of polling bit for this STA

## Slide 12: Example of null BA information fields
This field doesn’t contain the acknowledgement information for corresponding STA
This field can include the time/frequency/power adjustment information and UL channel resources allocation information, detail is TBD
A special value for Block ACK Starting Sequence Control field can be used to indicated that this field is a null BA information field

## Slide 13: Conclusion
UL MU TXOP needs a new scheme to allow flexible UL MU transmission.
In this proposal, we discussed a new control scheme with a multi-user BA+Poll frame
  to achieve the acknowledgement, polling and resource allocation , error indication and assistant UL transmission control indication.
  to provide the scheme with minimum overhead
  to keep compatibility with legacy devices

## Slide 14: Reference
[1] 11-14-0165-01-0hew-802-11-hew-sg-proposed-par
[2] 11-09-1036-00-00ac-uplink-mu-mimo-sensitivity-to-power-differences-and-synchronization-errors
[3] 11-14-0802-00-00ax-consideration-on-ul-mu-transmission