## Slide 1: Frame Exchange Control for Uplink Multi-user transmission
Date: 2014-09-15
Authors:

## Slide 2: Background
In the 11ax PAR, it is said that “the project may include the capability to handle multiple simultaneous communications in both the spatial and frequency domains, in both the uplink (UL) and downlink (DL) direction”, [1].
  DL MU-MIMO has already been supported in 11ac.
  UL multi-user transmission was discussed in previous meetings, including UL MU-MIMO and UL OFDMA.
  UL MU transmission is identified as a candidate technology to improve the network efficiency in dense deployment case.
    The feasibility of supporting OFDMA and UL MU-MIMO has been analyzed in [2] and [3].

## Slide 3: Motivation
A general UL MU transmission procedure has been introduced in [3].
Further design for UL MU transmission protocol needs to be discussed, in particular:
  Multi-user polling and information indication
  The policy for multiple frame transmission in a UL MU TXOP
  Multi-user acknowledgement
  Error recovery
In this contribution, we introduce some considerations for UL MU transmission in a TXOP.

## Slide 4: Analysis
The following issues should be considered to define a complete UL MU transmission protocol
  Multiple UL MU frame exchanges in a TXOP
    How to define frame exchange sequence in a UL MU TXOP, allowing multiple UL MU PPDU transmissions with less overhead
  Multi-user acknowledgement
    How, for the AP, to respond to the received UL MU PPDUs with acknowledgement frame?
  Error recovery
    How to initiate the error recovery procedure when UL MU transmission fails?
  Flexible UL MU transmission scheduling
    Allow scheduling of UL MU transmission from new STAs during a UL MU TXOP

## Slide 5: Analysis
AP’s responsibility in UL MU transmission
  Schedule for or trigger a UL MU transmission
  Poll multiple STAs’ UL data and feedback ACK to multiple STAs.
  Initiate the error recovery procedure when needed
  Provision assistant information for UL MU transmission control
    Power control
    Time and frequency synchronization
STA’s responsibility in UL MU transmission
  Send UL PPDUs as indicated by AP
  Perform power/time/frequency adjustment
  Obey the transmission duration as indicated by AP
    Easy for AP to control the transmission within the TXOP limit
    Easy for AP to acknowledge multiple STAs at the same time

## Slide 6: Multi-user acknowledgement and Polling
A multi-user acknowledgement and Polling scheme should provide following functions:
  Acknowledgement to received UL MU PPDUs, allowing Error indication
  Polling and UL MU transmission resource allocation
  Providing transmission control information, e.g. time/frequency/power adjustment
Principle and justice
  To achieve the above purposes with less overhead
  To keep compatibility with legacy devices
A scheme using multi-user BA+Poll frame is introduced
  The multi-user BA + Poll frame combines the functions of BA, scheduling control, error indication
  The multi-user BA + Poll frame can reuse the current BA frame structure,
  eg. Similar to Multi-TID BA variant
  The multi-user BA + Poll frame can be sent in non-HT format
  No additional scheduling/poll frame needed

## Slide 7: Multi-user acknowledgement and Polling
The multi-user BA+Poll frame used during a UL MU TXOP can:
  acknowledge the previous UL MU transmission
  schedule the next UL transmission for the current group triggered by more data bit in UL MU PPDUs
    The Duration/ID field can be reused for the next UL MU PPDU TxTime calculation

## Slide 8: Error Recovery
When one of the UL MU STAs’ data fails, AP can use the multi-user BA+ Poll frame for error recovery
  indicate receiving failure to the transmitter, a null BA information field can be designed in the BA+Poll frame
  both error indication and scheduling can be combined in same BA +Poll frame. Each STA corresponds to a BA information field, the BA information fields can be a BA+Poll info field or a null BA info field
  a STA can trigger retransmission in the next UL MU transmission when receiving the failure indication

## Slide 9: Schedule new user(s) during the UL MU TXOP
AP can use the multi-user BA+ Poll frame to poll a new STA within the UL MU TXOP
  Poll new STA(s) for UL MU transmission
  Indicate the time/frequency/power adjustment information and UL resource allocation for the new STA(s) by using BA information field for the new user.

## Slide 10: Scheduling STAs at the beginning of a TXOP
AP can use the multi-user BA+Poll frame as a UL MU scheduling frame that transmitted as a initial frame of a TXOP.
  When transmitted as a scheduling frame, the multi-user BA+Poll frame is no longer a control response frame
  The new BA can use the null BA information fields to schedule multi-users of the UL MU TXOP, example of the null BA information fields is shown in slide 12

## Slide 11: Conclusion
UL MU TXOP needs a new scheme to allow flexible UL MU transmission.
In this proposal, we discussed a new control scheme with a multi-user BA+Poll frame
  to achieve the acknowledgement, polling and resource allocation , error indication and assistant UL transmission control indication.
  to provide the scheme with minimum overhead
  to keep compatibility with legacy devices

## Slide 12: Reference
[1] 11-14-0165-01-0hew-802-11-hew-sg-proposed-par
[2] 11-09-1036-00-00ac-uplink-mu-mimo-sensitivity-to-power-differences-and-synchronization-errors
[3] 11-14-0802-00-00ax-consideration-on-ul-mu-transmission